## Slide 1
Describe M-Series Messages
EO 001.01
Notes: 7/01/10 Format Change

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Objectives
Identify References Governing M-Series Messages
Identify Capabilities and Limitations of M-Series Messages
Identify M-Series Messages in Common Use
Identify M-Series Message Identification and Identification Amplification field

## Slide 4: M-Series Message Governing References
M-Series Messages are the standard message format for Link 11A and Link 11B;
They are a fixed format messages, defined by standards
There are 2 formal standards:
  MIL-STD 6011
  STANAG 5511
Other than Governing Authority, there are no practical differences
Notes: This lesson was prepared off of the STANAG, not the MIL-STD

## Slide 5
M-Series Message Structure
M-Series Messages consist of 72 bits, which yields 48 bits of tactical information
The first 4 bits are the message label (eg M.1)
The next 12 contain the Track Number
The next 2 contain the identity
The remainder is message-specific information for a total of 48.
Notes: The number of bits is not important, its to highlight future lessons about what is lost during the message forwarding process
Emphasize the fact that these numbers are not tested, and they are not expected to know them as a TDL 200 graduate

## Slide 6
Common M-Series Messages
M.1 | Data Reference Position Message
M.81 | Data Reference Position Amplify Message
M.2 | Air Track Position Message
M.82 | Air Track Position Amplify Message
M.3 | Surface Track Position Message
M.83 | Surface Position Amplify Message
M.4A | ASW Primary Message
M.9A | Management Message (Information)
M.9G | Data Link Reference Point Position Information
Notes: This list is not exhaustive

## Slide 7
Field Size (bits) | M-Series Type | Subcomponent | Subcomponent Size (bits) | Example Value
32 | M.2 Message (First Frame) MIL-STD-6011C, page 5-32 | Label | 4 bits | 0010 binary
 |  | Track Number | 12 bits | 75 octal
 |  | Identity (Id) | 2 bits | 3 (Friend)
 |  | Primary Identification Amplification (Pri Amp) | 2 bits | 2 (Int/Fighter)
 |  | Scale Indicator (SI) | 1 bit | 1 (Fine)
 |  | Track Quality | 3 bits | 7
 |  | EDAC | 6 bits | 0
 |  | Padding | 2 bits | 0
32 | M.2 Message (Second Frame) | X Coordinate | 12 bits | +1260 decimal
 |  | Y Coordinate | 12 bits | +1880 decimal
 |  | EDAC | 6 bits | 0
 |  | Padding | 2 bits | 0
M.2 Message Example

## Slide 8
Field Size (bits) | M-Series Type | Subcomponent | Subcomponent Size (bits) | Example Value
32​ | M.82 Message​ (First Frame)​ MIL-STD-6011C, page 5-43​ | Label​ | 4 bits​ | 1000 binary​
 |  | Track Number​ | 12 bits​ | 75 octal​
 |  | Height​ | 8 bits​ | 4000 Ft / ( 31 + 1/4) = 128 dec​
 | ​ ​ | EDAC​ | 6 bits​ | 0​
 | ​ ​ | Padding​ | 2 bits​ | 0​
32​ | M.82 Message (Second Frame)​ ​ ​ | X Dot​ | 8 bits​ | -310 MPH / (3 + 33/34) = -78 dec​
 |  | Y Dot​ | 8 bits​ | 496 MPH / (3 + 33/34) = 124 dec​
 |  | Switch​ | 1 bit​ | 0 (X Dot, Y Dot)​
 |  | Size​ | 2 bits​ | 1​
 |  | Identity Amplification (Id Amp)​ | 3 bits​ | 0 (No statement)​
 |  | Height Source​ | 2 bits​ | 1 (Sensor)​
 | ​ ​ | EDAC​ | 6 bits​ | 0​
 | ​ ​ | Padding​ | 2 bits​ | 0​
M.82 Message Example
Notes: Make sure to point out the ID Amplification part of the message. It is used to specify what ID the track is. The ID, PRI AMP ID, and M.82 ID AMP all work together.

## Slide 9
M-Series Message Identification
From the M.2 Example, there are 2 bits to describe Track ID, and 2 bits to describe Track ID amplification
A bit is a 0 or 1, meaning with 2 bits, there are 4 possible combinations (00,01,10, 11)
Each combination can be converted from binary to decimal (0,1,2,3)
Each decimal number has been assigned an ID: Unknown (0), Friend (1), Hostile (2), Friend (3)
Notes: There is a slight deviation explaining bits here. This explains the M-Series message limitation in how Link 11 expresses ID.
The two Friend fields is not a mistake, it's how the ID system is designed.
The final ID is determined by the M.2 ID and PRI AMP fields, and the M.82 ID AMP field.
It takes 3 IDs to make an ID determination.

## Slide 10
M-Series Primary Identification Amplification
Where are Suspect, Assumed Friend and Pending?
The PRI ID Amp field also has 2 bits, and therefore 4 possible options.
These values are labelled 0-3
Suspect, Assumed Friend and Pending are generated out a combination of ID and ID Amp in a single message
Notes: This explains that you need more than the first ID field.

## Slide 11
M.2-Series Message Identification
PRI AMP | ID=0 Unknown | ID=1 Friend | ID=2 Hostile | ID=3 Friend
0 | Pending | General | No Statement | Special Misson
1 | Unknown | Helo | Undefined | Strike/Support/Bomber
2 | Assumed Friend | Undefined | Undefined | Interceptor/Fighter
3 | Suspect | Undefined | Undefined | Undefined
Notes: M-Series messages, compared to J-Series messages in that the do not carry as much information. For example, the chart above is the extent of the discription of the asset. There is no information on platform, or mission (aside from a generic indicator)

## Slide 12
M.82-Series Message Identification
The M.82 message had a field ID AMP that is 3 bits long, creating 8 different combinations (000, 001, 010, 011, 100, 101, 110, and 111)
M.2 ID, PRI AMP, and M.82 combine to create specific IDs
Examples:
ID 0 (Unknown) + PRI AMP 1 + ID AMP 3 = Unknown Fighter
ID 1 (Friend) + PRI AMP 1 (Helo) + ID AMP 1 = ASW Helo
Notes: MIL-STD 6011 and STANAG 5511 have the charts to calculate the output based on the numbers.
The C2 Hosts will do this work for you, however if one of those bits get lost or flipped, it's easy to see how you end up with really strange phenomenon.

## Slide 13: Confirmation Questions
List the two standards that govern M-Series Messages
  MIL-STD 6011 and STANAG 5511
How many M-Series messages are used to describe an Air Track?
  2: M.2 and M.82
How many ID Fields are used in the M.2 and M.82 to create a track ID?
  3
  M.2: ID, PRI AMP
  M.82: ID AMP

## Slide 14: Summary
Identify References Governing M-Series Messages
Identify Capabilities and Limitations of M-Series Messages
Identify M-Series Messages in Common Use
Identify M-Series Message Identification and Identification Amplification field.

## Slide 15
QUESTIONS?