## Slide 1
EO 002.02
Link 11 Network Parameters

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
Data Link Reference Points
Voice and Data Frequencies
Link 11 Cryptographic Parameters
Link 11 Polling Sequence
LSYSDATA Set

## Slide 4
Data Link Reference Points
In the OPTASKLINK the DLRPs are defined by the DLRPGRID Set
There can be many DLRPs depending on the AOR of the OTL
Some DLRPs can be valid only for a set period – all spelled out in the OTL
In the OTL, DLRPs are not in the LINK 11 SEGMENT
DLRPGRID/DLRP/L5/4520.3500N-02126.1500E/010800ZJUN2006//
Notes: The reason why DLRPs are not in Link 11 is because they also serve other Links.

## Slide 5
Voice and Data Frequencies
Voice Frequencies are set by the IVCCN Set (Interface Voice Control and Coordination Nets)
The IVCCN Set is not in the LINK 11 SEGMENT, and is applicable to the entire OTL
Each coordination net (DCN, TSN, VPN) needs its own IVCCN line
  Primary and Secondary nets also need their own IVCCN line
IVCCN can also be a chat server, defined by an IPV4 or IPV6 address
Notes: Voice Coord frequencies cannot be the same as Data Link frequencies
DCN = Data Coordination Net
TSN = Track Supervision Net
VPN = Voice Production Net

## Slide 6
Voice and Data Frequencies
Link 11 Data Frequencies are determined by the DALKFREQ Set
Each frequency is assigned a designator and codeword
  The designator is related to the frequency plan of an operation
  The codeword is the name given to the frequency
DALKFREQ also designates Priority (Primary, Secondary), and a Usage Indicator (Day, Night or Relay)
DALKFREQ also contains an Emissions Designator. This is a code that defines how the signal is coded, and is not Data Link specific
  B7D – HF Link 11
  F2D – UHF Link 11
Notes: The designator is what the frequency manager uses to keep track of all the frequencies. The codeword is the callsign assigned to the frequency for passing over the phone or net.
  A signal that is amplitude-modulated with independent sidebands (B)
  Two or more channels carrying digital information (7)
  Signal carries data, telemetry, or telecommand (D)
The Emissions Designator part is to explain that the B7D and F2D are not arbitrary, but actually reference an understood descriptor of signals. HF and UHF are modulated differently, (HF is amplitude modulated, UHF is frequency modulated) and if plotted on paper, would look very differently.

## Slide 7
DALKFREQ Set
DALKFREQ/DATA/FD:DATA01/ASGN:1234.5KHZ/PURPLE/P/B7D/D//

## Slide 8
Link 11 Cryptographic Parameters
CRYPTDAT Set defines how Link 11 is encrypted
It defines both the encryption equipment (KG-40), and the keymat
Crypto roll-over time is also defined in this field
CRYPTDAT/KG-84/AMASL6789/0200Z//
Notes: Crypto equipment aside from the KG-40 is mostly for Satellite Link 11, which is largely obsolete.

## Slide 9
Polling Sequence
The Link 11 Polling sequence is defined by the POLLSEQ set.
This field is not mandatory, some OPTASKLINKs allow participants to customize their polling sequences.
It defines all the units in a list.
POLLSEQ/SHIP:STORM/SHIP:ENTERPRISE/SHIP:ATRIUM/SHIP:ATLAS//
Notes: If a unit is on the polling list, but not active on the link, they will simply be polled and not respond. The ICO can direct units to drop them from the polling sequence to improve Net Cycle Times if required.

## Slide 10
LSYSDATA Set
LSYSDATA defines the Link 11 System Data
This designates the waveform parameters and speed settings required for all Link 11 participants
Most of the DTS settings are located in the LSYSDATA Set
LSYSDATA/22-18/ON/A1/SLEW//
Notes: Satellite Extended Time out frames are nominally for Sat Link 11, but can be used for split-site configurations with high latency. CADS uses time out frames.

## Slide 11
QUESTIONS?