## Slide 1
EO 003.01
Explain Interface Control Cells

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
ICC Hierarchy
ICO
ICC Manning Scheme
Elemental ICC Construct

## Slide 4
Explain Interface Control Cells
ICC Hierarchy
Responsible to the Component Commander or JTF Commander
Advise on employment/generation
Ingest and manage Tactical Data exchanges
Plan and coordinate MTN/MTA requirements
Manage network load files
Create OTL and OTL SUPPS
Conduct TSDF calculations
Resolve MTN deficiencies
Ensure TDL standards
Notes: Interface Control Cells can be employed in a plethora of environments and are hierarchical in design. Therefore an ICC may be designated using a variety of acronyms all designed to identify those ICC environments. A TICC is Tactical, a WICC indicates Wing, a SICC is Sector, a RICC is Regional and an MRICC denotes Maritime Regional, and finally a JICC indicates a Joint flavour. In spite of the variations however; the overarching role of the ICC remains unchanged.
In each case, an Interface Control Cell will employ a variety of CAF Personnel and TDL Specialists and will be responsible to the functional Component Commander or Joint Task Force Commander to deal with the day-to-day management and operations of Joint Multi-TDL Networks in order to guarantee optimum TDL performance.
ICCs are employed to support Operations like eFP LATVIA, Exercises such as MAPLE FLAG or CUTLASS FURY, or Regionally to support elemental TDL planning, management and distrubition. An example of a TICC would include the RCAF’s 42 RDR, whereas Regional examples include the RCAF RICC at 21 AC&W Sqn and RCN Maritime RICCs, located in Halifax and Esquimalt.
NOTE TO INSTRUCTOR – CLICK FOR EACH RESPONSIBILITY BELOW TO APPEAR
The ICC will be responsible to:
-Advise on the effective employment/generation of TDL capabilities;
-Ingest and manage the Tactical Data exchanges;
-Plan and coordinate MTN/MTA requirements;
-Manage applicable network load files;
-Create operational and exercise OPTASK LINK Messages and OTL SUPPS;
-Conduct Time Slot Duty Factor (TSDF) calculations and ensure link 16 deconfliction, ensuring compliance with national Frequency Clearance Agreements (FCA’s);
-Investigate and report, effective utilization of MTN resources, resolve deficiencies and refer unresolved issues as required; and
-Ensure the use of TDL ISO Joint Ops/EXs is conducted in line with agreed TDL standards and in conformance with national regulations that apply.

## Slide 5
Explain Interface Control Cells
TDL 400 - ICO
Ultimately responsible for the planning and management of the MTN
The ICO will:
  Coordinate Link 16 load files
  Distribute L16 Notification Msg
  Manage RF and IP TDL networks
  Distribute tactical data
  Manage ICC personnel
  Develop PLANs, OPORDS, CONEMP
  Coordinate Allies/NATO and EC L1s
  Monitor issues and provide advice
Notes: Essential to the Interface Control Cell staffing is the TDL 400 Interface Control Officer or ICO.
The ICO is the senior multi-TDL interface control specialist in support of the operation or exercise. Similar to the ICC hierarchal designation, the Interface Control Officer takes on the acronym of the center in which they are employed. Tactical ICO is a TICO, Regional ICO is a RICO, a Sector ICO is affectionately know as a SICO, and Joint ICO assume the coveted JICO nomenclature.
The Interface Control Officer ultimate responsibility is for the planning and management of the MTN within a theater of operations.
NOTE TO INSTRUCTOR – CLICK TO MAKE RESPONSIBILITIES APPEAR ON PRESENTATION
The ICO will ensure all Interface Control Cell responsibilities and functions as previously mentioned are accomplished as well as:
-Coordinate Link 16 load files;
-Distribute Link 16 Notification Messages;
-Manage the RF and IP TDL networks;
-Distribute tactical data to various Recognized Pictures and the COP;
-Manage ICC personnel;
-Develop High Level Direction via CONPLANs, Operating Concepts and CONEMPs;
-Coordinate with Allies, NATO and EC L1s; and
-Monitor issues within Ops and Exs and provide advice and troubleshooting expertise

## Slide 6
Explain Interface Control Cells
Optimum ICC Manning Scheme
Component Commander or Joint Task Force Commander
JICO
(TDL 400)
Watch Officer
(TDL 400)
Link 22 Manager
(TDL 300)
Multi-Link Operations Specialist Positions
(TDL 200)
Technicians and System Administrators
Joint Track Data Coordinator
(TDL 200)
Link 11/11B Manager
(TDL 300)
Link 16 Manager
(TDL 300)
Notes: Deployed JICC and TICC detachments such as the ones used during 2010 Olympics and G8/G7 conferences support the Component Commander or Joint Task Force Commander by managing the employment of TDLs. They require specific manning and qualifications, to provide 24/7 operations, for periods over 30 days.
    Watch Officer
The ICC Watch Officer is responsible to the ICO for ICC operations and active management of Multi-Link Network operations. The ICC Watch Officer supervises the ICC personnel during TDL planning, management and execution. The ICC Watch Officer monitors the overall quality of the Multi-Link Network and directs actions to rectify problems as they occur and will conduct dynamic planning to adjust the Multi-Link Network and interfaces to meet changing requirements and operations. Service/Component mission planning teams will coordinate, brief, and debrief with the ICC Watch Officer daily, or as necessary, to ensure corrective actions taken. When multiple regions or sector are established, the ICC Watch Officer coordinates and has resolution authority to resolve cross-regional Multi-Link Network issues with the Regional Interface Control Cell (RICC) and/or Sector Interface Control Cell (SICC).
    Link 11 Manager
The Link 11 Manager is responsible to the JICC Watch Officer and JICO for all Link-11 and Link-11B planning and execution. When multiple regions and/or sectors are established, the Link-11 Manager coordinates, and has the authority to resolve cross-regional Link-11 and/or Link-11B issues. In addition, the Link 11 Manager may be tasked to plan and manage any of the extended interface TDLs.
    Link 16 Manager
The Link 16 Manager is responsible to the JICC Watch Officer and JICO for all Link 16 planning and operations. When multiple regions and/or sectors are established, the Link 16 Manager coordinates, and has the authority to resolve cross-regional Link 16 operations. Link 16 managers have been given responsibility for all JREAP A, B and C link planning and operations.
    Link 22 Manager
The Link 22 Manager is responsible to the JICC Watch Officer and JICO for all Link 22 planning and operations. When multiple regions and/or sectors are established, the Link 22 Manager coordinates, and has the authority to resolve cross-regional Link 22 operations.
    Joint Track Data Coordinator
The JTDC is responsible to the JICC Watch Officer and JICO for all track management issues within the Multi-TDL Network. The JTDC ensures the clarity, accuracy, currency, and quality of track data displayed on Multi-TDL Networks. The JTDC facilitates the resolution of dual track designation and identification conflicts. The JTDC functionality is an integral component of the combat identification process and will assist the theatre identity authority in timely and accurate assessment of tracks of interest.
    System Administrator/Technician
The System Administrator (SA) is responsible to the JICC Watch Officer and/or JICO for all JICC CIS. The SA will coordinate with the appropriate CIS units to resolve all computer support issues for the JICC computers.
The Technicians are responsible to the Watch Officer and /or JICO for all communications, including cryptographic and maintenance issues for the JICC. They coordinate with the appropriate communications and maintenance activities or units to resolve communications and maintenance support issues.
SA and Technician support is provided through Wing or Base Telecommunications and Information Services Officers.

## Slide 7
Explain Interface Control Cells
Elemental ICC Construct
MRICC(A)
MRICC(P)
1 CAD RICC at CADS
Notes: CA
No yet developed
RCAF
Canadian Air Defence Sector or CADS houses the RCAF/CANR RICC. The RICC is within 21 AC&W Sqn Operations and is the TDL fusion centre for the RCAF. Their roll is both tactical and operational. This RICC fuses tactical TDL feeds and correlates local and remote tracks to deliver the Recognized Air Picture. The RICC then distributes the Recognized Air Picture to JIIFC to be fused with the Strategic COP as well as integrated into the CANR Air picture at 1 CAD Combined Air Operations Center.
Additionally thru CADs the RAP is distributed by Tactical Data Link back to the various TICCs and WICCs, can be shared with RCN MRICCs, other peer Air Defense Sectors, as well as with NATO or other Coalition Partners to facilitate tactical and situational awareness of the entire Canadian airspace
RCN
Maritime Regional Interface Control Cells or MRICCs are established within each of the coastal F6 organizations. MRICCs are key to planning and managing specific TDL operational and exercise Information Exchange Requirements (IERs) and will provide the means to distribute Tactical Data to the Regional Joint Operations Centers, share with the RCAF RICC, as well as NATO or other Coalition Partners to facilitate tactical and situational awareness of the Maritime Domain.

## Slide 8
Confirmation Questions
What is significant to note about the nomenclature of ICCs? Do their roles change with their operational environment?
What is the ICO ultimately responsible for?
What is a key consideration to establishing a deployed ICC?
Notes: 1 - What is significant to note about the nomenclature of ICCs? Do their roles change with their operational environment?
Ans: ICCs are hierarchical in design. Therefore an ICC may be designated using a variety of acronyms all designed to identify those ICC environments.
Ans: In spite of the variations however; the overarching role of the ICC remains unchanged.
2 - What is the ICO ultimately responsible for?
Ans: The Interface Control Officer ultimate responsibility is for the planning and management of the MTN within a theater of operations.
3 - What is a key consideration to establishing a deployed ICC?
Ans: Deployed ICCs require specific manning and qualifications, to provide 24/7 operations, for periods over 30 days.

## Slide 9
QUESTIONS?