## Slide 1
Mitigate Link 11 Limitations
EO 001.01
Notes: 7/01/10 Format Change

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Objectives
Identify Link 11 Participating Unit and Track Block Values
Identify Link 11 Position Plotting and Gridlock
Identify Relationship between System Coordinate Center, Data Link
Reference Point, Unit Position and Track Positions
Identify Track Quality Limitations of Link 11
Identify Track Identity and Amplification Limitations imposed by Link 11 (Talked about during M-Series Messages)

## Slide 4
Octal Notation
Decimal | Binary | Octal
0 | 000 | 0
1 | 001 | 1
2 | 010 | 2
3 | 011 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 001 000 | 10
9 | 001 001 | 11
10 | 001 010 | 12
11 | 001 011 | 13
12 | 001 100 | 14
Octal Notation is counting with 8 digits (0-7)
Humans use decimal notation with 10 digits (0-9)
Computers use binary notation with 2 digits (0-1)
Computers can use decimal notation, but it is wasteful
  0-7 would use 3 bits
  8 and 9 would use 4 bits
  The rest of the 4 bits would be wasted
A compromise is octal, which is easier for Humans to use and efficient for computers
Notes: A lot of information in data links is in Octal notation. It's important to understand what that means, but not necessarily how to calculate it.
The next step is Hexadecimal, which is base 16, and each character represents 4 bits. Most computer applications use hexadecimal nowadays.

## Slide 5: Link 11 PU and Track Block Values
Participating Unit Addresses
  01-76 Octal for a total of 62 available PUs
  00 and 77 are illegal numbers IAW MIL-STD 6011/STANAG 5511
  100-175 are reserved for Link 11B RUs
  176 is a Track Number used by Forwarding JTIDS Units for forwarding data originating from C2JUs with TNs of 200 and above
  177 is a Collective Address for all Interface Units (PUs, RUs, JUs, etc)
Track Block
  0200-7776 Octal for a total of 3967 available tracks
Notes: The initialization Parameters required include Unit Address (PU) ranging from 01 to 76
Track block allocation from 0200-7776
Encryption
Radio Frequency
Assigned NCS

## Slide 6: Link 11 Positions and Gridlock
Cartesian plotting vs Geodetic plotting
  Cartesian plotting uses an externally defined point on a map as a reference
  Units are plotted using a distance measured from that external point
  Geodetic plotting defines points on a map for each unit
  Cartesian plotting is more data efficient (less bits needed to transmit positional data), but requires external coordination
Link 11 uses Cartesian Plotting
Link 16 uses Geodetic Plotting
Gridlock considerations
  Gridlock is the procedure of comparing locations of data, and applying corrections
Notes: The initialization Parameters required include Unit Address (PU) ranging from 01 to 76
Track block allocation from 0200-7776
Encryption
Radio Frequency
Assigned NCS

## Slide 7
Fixed Geographical Position
Expressed in geodetic Lat/Long
Found in OPTASK LINK
Must be coordinated prior to operations
Reported by M.9G message
Data Link Reference Point (DLRP)
Notes: Data Link Reference Point (DLRP): All tracks reported over a Link 11 network are reported on an X/Y grid. The center point of this grid is called the DLRP. This is a common reference point that all units participating on the link have to enter to ensure that all track reporting is correct. The DLRP can be found in the OPTASK LINK and is entered as a Latitude/Longitude. The DLRP grid measures 1024 data miles (dm) on each axis (X/Y) from the center point (DLRP), so is 2048 dm on each side. In some cases, the DLRP can be broadcast on the M.9G message.

## Slide 8
SCC
System Coordinate Center (SCC)
Represents center of Area of Operations of a specific unit
Commonly is the unit position
Expressed as +/- data miles from DLRP
Needs to be within 1024 minutes of latitude and longitude of DLRP (approximately 1 NM)
Notes: The SCC is the center point of a unit’s display grid. Because of differences in capabilities in units, these grids can measure as small as 512 dm on each side, up to 2048 dm on each side. The SCC must exist within the DLRP grid for tracks to be plotted properly. The SCC is reported over the interface as an X/Y coordinate measured from the DLRP. Some PUs
use their own unit position as SCC as is the case for CCS.

## Slide 9
SCC
Track Location
Reported tracks are expressed at +/- data miles from SCC
Limited to +/- 512 data miles
Therefore, there is a practical limit to how far units can be apart before they cannot express location of a track
Track 1234
Notes: The SCC is the center point of a unit’s display grid. Because of differences in capabilities in units, these grids can measure as small as 512 dm on each side, up to 2048 dm on each side. The SCC must exist within the DLRP grid for tracks to be plotted properly. The SCC is reported over the interface as an X/Y coordinate measured from the DLRP. Some PUs
use their own unit position as SCC as is the case for CCS.

## Slide 10: Track Quality Limitations
Track Quality is a numerical value used in calculating Reporting Responsibility (R2)
It represents degrees of reliability of positional data of tracks
If two participants in a Link hold the same track (under two different track numbers), R2 is used to determine who "owns" the track
Track Quality is compared between the two units, and determines whose information is more correct
Link 11 assigns a track quality of 0-7, Link 16 0-15
Therefore Link 11 will always be at a disadvantage to Link 16 in terms of accuracy of data
Notes: Most of the information required by a unit to initialize Link 11 can be found in the OPTASK LINK. This information includes the DLRP, operating frequencies, unit addresses, track blocks, duties, etc. The unit must also enter data not found in the OPTASK LINK, such as SCC and UPOS.

## Slide 11: Summary
Identify Link 11 Participating Unit and Track Block Values
Identify Link 11 Position Plotting and Gridlock
Identify Relationship between System Coordinate Center, Data Link Reference Point, Unit Position and Track Positions
Identify Track Quality Limitations of Link 11
Identify Track Identity and Amplification Limitations imposed by Link 11 (Talked about during M-Series Messages)

## Slide 12
QUESTIONS?