## Slide 1
Recognize Translation Issues
EO 001.07
Notes: This lesson plan needs to be cleaned up and extraneous stuff removed
Prior to commencing instruction the instructor should:
1) Introduce himself
2) Have each student introduce himself to the class detaining the platform and level of JTIDS expedience.
The instructor should motivate the students towards the learning by explaining that a the level of detail presented will allow all students (regardless of their experience level) to learn.
Stress the reason for the Joint class is to insure that interoperability is achieved by providing a baseline of knowledge about terms, and procedures. Stress that platform unique procedure and terminology is detrimental to Joint, Combined and Allied operations.

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Learning Objectives
Data Forwarding Translation
Direct vs. Indirect PPLIs
Real time vs. Non-Real time

## Slide 4: Data Forwarding Translations
Data Forwarding is standardized, similar to Link 11 or Link 16
  MIL-STD 6020
  STANAG 5616
These standards are defined in 3 volumes
  Volume 1 – forwarding between Link 11 & Link 16
  Volume 2 – forwarding between Link 22 & Link 16
  Volume 3 – forwarding between Link 11 & Link 22
Notes: The fact that forwarding is standardized is important, because it means that the data is converted by a set of rules, and is not vendor specific
Memorizing the Volumes is not important, it's more to illustrate the fact that the references exist, and can be examined if necessary.

## Slide 5: Forwarding considerations
Not all message standards are created equally
  M-Series messages carry 48 bits of data
  J-Series words carry 70 bits of data
  J-Series messages can be comprised of as many as 10 words (700 bits!)
There is less data per message between M-Series and J-Series
  When converting between M -> J, the J-Series message will have large gaps with no meaningful data (blank)
  When converting between J -> M, some information contained in the J-Series message will be discarded
Notes: The bits aren't necessary for memorization, it illustrates that J-Series messages carry much more information objectively than M-Series

## Slide 6: Forwarding Limitations
Different Data Links do not have the same compatibilities
  Link 11 and Link 16 have different roles, rules and capabilities
  For example, there is no equivalent of J28.2 Free Text Messages in M-Series
Link 11 and Link 16 have different Interface Unit numbers
  Link 16 JUs cannot be displayed on Link 11
  Source number 176 indicates on Link 11 that the track is from a Link 16 participant
  That is any unit with a JU of 00200 or higher will be shown as IU 176 on Link 11
Link 11 and Link 16 have different Track Block numbers
  Link 11 cannot process Link 16 track blocks
  Forwarding Track Blocks mitigate this issue
Notes: Every time that you change something, a little bit is lost. Information is like energy, conversion isn't free.
Track block and interface unit number differences greatly impact the planning process.

## Slide 7
J3.2 AIR TRACK
TRACK NUMBER
STRENGTH
ALTITUDE & SOURCE
ID CONFLICT INDICATOR
TRACK QUALITY
ID CONFIDENCE
ID & AMP & SPEC INTEREST
LATITUDE
LONGITUDE
PASSIVE/ACTIVE
COURSE
SPEED
IFF MODE 1,2,3,4 & SOURCE
PLATFORM TYPE
PLATFORM ACTIVITY
PLATFORM ID
M2 AIR TRACK
TRACK NUMBER
ID & AMP
TRACK QUALITY
X,Y COORDINATE
M.82
TRACK NUMBER
ALTIUDE & SOURCE
X,Y SPEED
TIME TAG
STRENGTH
ID AMP
Link 11
AIR
FRIENDLY
Link 16
AIR
FRIENDLY
FIGHTER
INTERCEPTOR
F-15
Notes: 7
This slide illustrates how much information is stripped away when forwarding J-Series to M-Series. If the M-Series was forwarded back to J-Series, those fields would be blank.

## Slide 8: Analogy of Postcards and Letters
M-Series Messages are like postcards
  Small, and can only be mailed one card at a time
J-Series Messages are like letters
  Larger, and can place multiple pages in a single envelope
Copying over a postcard to a letter is easy to do, but results in a lot of wasted paper
Copying over a letter to postcard will require removing information from the letter to make it fit
Notes: This is the reason why messages forwarded from Link 11 to Link 16 tops out at TQ 7, due to the fact that there can't be enough information inside the M-Series message to get any more specific.

## Slide 9: Real time vs Non-Real time
Data has an expiry date. Old data is useless data.
Old is a relative term. How old is too old?
It depends on what the data is used for
  Ground station position
  Ship position
  Fighter position
  Network-enabled weapon employment
Less time sensitive data
More time sensitive data
Notes: In World War 2, the Germans got the news of the Invasion of Normandy too late to make any use of it. The same principle applies here. Data Link messages are information. It is time-sensitive. How time sensitive depends greatly on what the information is.

## Slide 10: Real time vs Non-Real time
Real-time data is RF Link 16 quality
  Most information is 1 frame old (12 seconds)
  The oldest possible is 1 epoch old (12.8 minutes)
Non-real time data is data that is not real time
  There is a big difference between an aircraft position that is real time vs non-real time
  Is RF Link 11 data real time?
Timelate is the term used to measure how late data is
  Measures the time data requires to propagate through gateways and networks
  Acceptable timelates will vary depending on where the information is display/used
Notes: The Link 16 standard is one frame or 12 seconds. Network enabled weapons update faster than that, but must be specially programmed into the Link 16 network to function. For tactical operations, 12 seconds or less is considered as real time as possible. This is because 12 seconds is considered to be a duration of a radar sweep.
SOPs and CONOPs will usually determine a timelate that is considered acceptable or useful.
Timelate is generated by bandwidth of the link (buffering), latency of the medium, processing time of gateways, and the delay between when a C2 System receives the data and displays it.

## Slide 11: Direct and Indirect PPLIs
Link 16 has 2 categories of PPLI
  J2.x Direct PPLI
  J2.0 Indirect PPLI
Direct PPLIs represent units in an RF network
  They are considered Real Time, and used for Link 16 Relative Navigation calculations
Indirect PPLIs represent units that are not in an RF network
  It alerts operators and systems that the PPLIs are not in the immediate network and treats them differently
Notes: Some systems will not allow Indirect PPLIs to do certain tasks, such as sending or receiving NPG 9 Air Control Messages

## Slide 12: Direct and Indirect PPLIs
Data Link Routers are required by Routing Standards to convert J2.x messages to J2.0 messages when they are pulled off an RF network
All Data Link Routers have the option to disable this feature, and send the data in its original form
This feature is usually labelled "J2.x to J2.0 conversion"
The ICO is responsible for deciding whether to use this feature or not.
Notes: It is not MIL-STD compliant to send a J2.2 over a JREAP. The ICO must decide whether or not to maintain this compliance. Usually the conversion is disabled only for compatibility reasons.

## Slide 13: Summary
Data Forwarding Translation
Direct vs. Indirect PPLIs
Real time vs. Non-Real time

## Slide 14: Collaborative Problem Solving
Situation: Using the diagram below, discuss the following questions:
  Can 12 ER send meaningful data to the CF-18?
  Can the 12 ER Weapons Controller give effective commands to the CF-18 over the data link?
  The CF-18 has been tasked to conduct a strike mission. Which unit is best suited to control the CF-18 for that mission?
  Is CADS any more effective than 12 ER in controlling the CF-18?
12 ER Deployed
CF-18
HMCS HALIFAX
12 ER
C2 System and Controller
HALIFAX C2 System and Controller
Link 11
Link 16
JREAP C
CADS
CADS
C2 System and Controller
Notes: Assume good voice comms and radar with all three platforms.
Due to the fact that the HALIFAX is forwarding M-J, 12 ER will not have access to the full control suite included in Link 16. There is no Weapons Engagement messaging, or acknowledgement messages that are able to be processed, and 12 Radar will be unable to use J28.2 text messaging. CADS is similarly affected, as it cannot get J-Series messages out to the fighter either.
For stage 2, replace Link 11 with a JREAP C. Is anything different? How so?
For stage 3, state that the JREAP C between 12 ER and the HALIFAX is very timelate due to the satellite connection – up to 1 minute. How does that change the situation?

## Slide 15
QUESTIONS?