## Slide 1
EO 001.05
Describe Legacy Protocols

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
Serial J
Sat J
Socket
IJMS

## Slide 4
References
Understanding Link 16
STANAG 5602
ADSI Users Guide

## Slide 5: Legacy Technology Definition
Legacy technology describes the term as “an old method, technology, computer system or application program, of, relating to, or being a previous or outdated computer system”.
Notes: Increasing operational costs and system downtime.
Security vulnerabilities.
System incompatibility.
Less technical support.
Inability to provide user needs.

## Slide 6: Serial J
Serial J is a proprietary serial based communication protocol developed by the MITRE defense company in support of their Multi-links Translator and Display System (MTDS).
Notes: The MTDS is an older C2 Host software that uses commercial over the counter technology.

## Slide 7: Serial J Limitations
Proprietary based (developed ISO a particular system).
Not compatible with JREAP.
Reduced baud rate.
Not compatible with newer systems.
Notes: You may see Serial J in an operator selectable data link field on some C2 Host systems.

## Slide 8: Sat J
Sat-J (or S-TADIL-J) is a communication protocol that supplements surveillance network connectivity when a JTIDS/MIDS is not available.
This protocol is optimized for the limited bandwidth available through DAMA SATCOM.
Notes: Initially developed for the USN.

## Slide 9: Sat J Limitations
Equipment Dependant.
Requires Satellite Access.
Half Duplex.
Not compatible with newer systems.
Notes: Requires access to Satcom equipment.
Satellite access takes time and money.
Update rates are very slow.
Sat J usually requires an RS 422 serial interface connection.

## Slide 10: Socket J
Socket J is a communication protocol which allows the moving of Link 16 compatible data over a TCP/IP network.
Notes: Client server oriented protocol which uses a socket based interface.

## Slide 11: Socket J Limitations
Does not follow J series message protocol structure.
Specific software required at both ends of communication transfer.
Does not adhere to TCP/IP communication Protocol.
Notes: Information errors may occur, or information may be discarded, depending on the C2 host being used.

## Slide 12: IJMS
Interim JTIDS/MIDS Message Specification (IJMS) is an early implementation of messages between class 1 JTIDS terminals.
Class 2 terminals retain an IJMS and JTIDS message capability.
Notes: First fielded in the early 90s.
NPGs still exist for legacy platforms to transmit and receive (if required).

## Slide 13: IJMS Limitations
Not fully compatible with Link 16.
Most systems can pass this data but cannot translate.
For older compatible platforms only (NATO AWACS)
Notes: IJMS was implemented and used until the next generation of JTIDS terminals were fielded in the mid 1990s.

## Slide 14
Confirmation Questions
What is Serial J used for?
What is Sat J used for?
What is Socket J?
What does IJMS stand for?
Notes: Serial J is a proprietary serial based communication protocol developed by the MITRE defense company in support of their Multi-links Translator and Display System (MTDS).
Sat-J (or S-TADIL-J) is a communication protocol that supplements surveillance network connectivity when a JTIDS/MIDS is not available.
This protocol is optimized for the limited bandwidth available through DAMA SATCOM.
Socket J is a communication protocol which allows the moving of Link 16 compatible data over a TCP/IP network.
Interim JTIDS/MIDS Message Specification (IJMS).

## Slide 15
QUESTIONS?