## Slide 1
EO 001.05
Describe Other Communication Protocols

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
SIMPLE
FMV/SDL
GCCS

## Slide 4
References
STANAG 5602 (SIMPLE)
MIL-STD-810/461/704 (FMV)
MIL-STD-188-184 (Telecommunications)

## Slide 5: Communication Protocol Definition
A communication protocol is a system of rules that allow two or more entities of a communications system to transmit information via any kind of variation of a physical quantity. Communicating systems use well-defined formats for exchanging various messages.
Notes: A good communication protocol should include the following details:
How to set up a connection.
How to end a connection.
How to start a message.
How to end a message.
How to deal with corrupted data.
How to format the data being sent.

## Slide 6: SIMPLE
The Standard Interface for Multiple Platform Link Evaluation (SIMPLE) a communications protocol to provide the means for geographically (national and international) separated Tactical Data Link (TDL) equipment (C4ISR, C2 and non-C2 test facilities) to exchange environment data and TDL messages in order to conduct detailed TDL Interoperability (IO) testing.

## Slide 7: SIMPLE Cont.
Intended to provide specifications for a common standard to interconnect ground rigs of all types, such as simulation and integration facilities.
Allows transmission of M-Series and J-Series messages over IP-based protocols.
Continues to find applications beyond its original purpose wherever transmission of J-Series data is not amenable over radio protocols such as Link 16.
Notes: SIMPLE not only provides the protocol for Link 16 data transfer it also provides:
Link 11 Protocols
Link 4 Protocols
IJMS Protocols
VMF Protocols
TIM/TOM Data Protocols
DIS Protocol Data Unit (PDU) data transfer
SIMPLE can be used to transfer data by:
Asynchronous
Synchronous
Ethernet Local Area Network (LAN) Protocols
User Datagram Protocol (UDP) broadcast
UDP multicast
Transmission Control Protocol (TCP)

## Slide 8: FMV/SDL
Full Motion Video (or Situational Data Link) is digital video data that is transmitted or stored on video discs for real-time reproduction on a computer (or other multimedia system) at a rate of not less than 25 frames per second.
Notes: There are many types of Software used to view this information (SC2PS).

## Slide 9: FMV/SDL Cont.
Military and Civilian sensor systems collect camera pointing information, platform position and attitude, and other data, and encode it into the video stream so that each video frame is associated with geo-positional information.
Notes: The CAF uses Remote Operational Video Enhanced Receivers (Rovers) to allow ground forces, such as Forward air controllers (FAC), to see what an aircraft or unmanned aerial vehicle (UAV) is seeing in real time by receiving images acquired by the aircraft's sensors on a laptop on the ground.

## Slide 10: CAF FMV/SDL Users
UAS (Blackjack, Raven)
CF-18
CP140- Aurora
Notes: Ask the students if they know other existing military platforms.

## Slide 11: GCCS
Global Command and Control System (GCCS) is a command and control (C2) system used to provide accurate, complete, and timely information for the operational chain of command.

## Slide 12: GCCS Cont.
Consists of hardware, software, common procedures, appropriation, and numerous applications and interfaces that make up an "operational architecture" that provides worldwide connectivity with all levels of command.
incorporates systems that provide situational awareness, support for intelligence, force planning, readiness assessment, and deployment applications that battlefield commanders require to effectively plan and execute joint military operations.
Notes: GCCS supports six mission areas (operations, mobilization, deployment, employment, sustainment, and intelligence) through eight functional areas: threat identification and assessment, strategy planning aids, course of action development, execution planning, implementation, monitoring, risk analysis, and a common tactical picture.
Usually connected to secret network (CSNI, SIPR)

## Slide 13
Confirmation Questions
What does SIMPLE stand for?
What is SIMPLE used for?
What CAF platforms use FMV?
What does GCCS stand for?
Notes: The Standard Interface for Multiple Platform Link Evaluation (SIMPLE)
A communications protocol to provide the means for geographically (national and international) separated Tactical Data Link (TDL) equipment (C4ISR, C2 and non-C2 test facilities) to exchange environment data and TDL messages in order to conduct detailed TDL Interoperability (IO) testing.
UAS, CF-18, CP-140
Global Command and Control System (GCCS)

## Slide 14
QUESTIONS?