## Slide 1
EO 001.02
Extract Data from the Network
Description Document

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
Describe the sections of an NDD
Explain the purpose of the NDD
Decipher the Connectivity Matrix (T/R/Y)
Locate platform ID Set
Locate Crypto requirements
Recognize Option Pools/TSR and impact on Surveillance capacity

## Slide 4: What is a Network Description Document?
Designed for a specific purpose, AOR / Exercise and for designated platforms to exchange data​
Introduction section gives an overview of what area and platforms the network supports​
​
ID SETs for each platform - assigned timeslots for transmitting and receiving​
​
  NDF creates the load files from the ID Sets in the NDD​
Notes: TP: L16 Terminals must know when to transmit and when to listen and what data it can pass; but it must be programmed first otherwise it is 'dumb'. ​
​
The Initialization Data Load (load-file) is what gets loaded into the terminal to program it. ​
​
Each IDL is tailored by the NDF to comply with the overall Network Design so to not cause interference. Each IDL is unique to the platform's capability and Information Exchange Requirements (IER) of the purpose for which the Network was designed. If the capability is not programmed into your IDL, you can't use it. Need relay, want to use J-Voice, need to transmit surveillance tracks, you need timeslots allocated to these functions. ​
​
If the network doesn’t have J-Voice built into it, it can not be used. ​
​
TSDF limitations are regulated and the TSDF Calculator will assist the planner with allowing Relay or Voice in congested AORs.​
​
Understanding the NDD will assist with overall Network monitoring and management. ​
(each networks architecture is different based on the situation/environment)​
​

## Slide 5: Network Description Document
Network Name
Introduction/Assumptions
Network Description
    Platform Functional Description
    Connectivity matrix
    Timeline
    COMSEC cross reference table
    Unit pulse density calculations
Network Ops Management
Appendices
Platform Loads
CAJE0008B
Country of
Origin
(2)
Originating
NDF
(1)
Network Use/
Environment
(1)
National Use
(2)
Series
Identifier
(2)
Version
Identifier
(1)
Notes: Country of Origin: AU – Australia; CA – Canada; FR – France; DE – Germany; IT – Italy; NT – NATO; US - United States
Originating NDF: A – Army; C – Combined; F - Air Force; J – Joint; M - Marine Corps; N – Navy; S – Shape;
Network Use/Environment: D - Wartime; E - Exercise; O - Operational; P - Peacetime; T - Test; U - Training; X - Experimental; Z - Other

## Slide 6: Platform Functional Description
Notes: TP: Have trainees open the NDD CAJE0008B_CH2 (2020); all the following exercises will use this NDD.
Instructor will ask the trainee to find the Platform Functional Description table.
This gives the reader a quick glance of:
a) what platforms have been included in this Network;
b) how many (Qty);
c) Tx NPGs; Rx NPGs;
d) respective surveillance capacity and if TSR or Option pools are used

## Slide 7: NDD Connectivity Matrix Abbreviations
Abbreviation | Meaning | Abbreviation | Meaning
127 | Stacked Net | NETE | Net Entry Transmit Enable
D | Dedicated (Access) | P2SP | Pack 2 Single Pulse
R | Dedicated w/Slot Reuse | P2DP | Pack 2 Double Pulse
O | Option Pool | P4 | Pack 4 Single Pulse
R | Receive | STD | Standard Packing
T | Transmit |  | 
TY | Transmit Relay | MY | Machine Relay
Y | Relay |  | 

## Slide 8: NDD Connectivity Matrix Practical Exercise
Notes: TP: Have trainees open the NDD CAJE0008B_CH2 (2020) and find the Connectivity Matrix page.
Walk the trainees following the T/R/Y O, R, D
Activity: Instructor to complete brief exercise of T/R/Y which can be used to confirm an architecture​

## Slide 9: Timeline
Notes: TP: Have trainees open the NDD CAJE0008B_CH2 (2020) and find the Timeline page.
Talk thru how multi-nets and Stacked nets are illustrated on the timeline.

## Slide 10: COMSEC Cross Reference Table
Notes: TP: Have the trainee find the COMSEC CROSS REFERENCE TABLE
This table lets those configuring their terminal what Secure Data Unit (SDU) requires crypto. Most Canadian Networks only operate with Crypto in the Default Net (0/1) locations.
Crypto Mod and new security measures will affect how Modern terminals are configured.

## Slide 11: Platform ID SET
Notes: TP: Have the search for Platform ID Set Cross Reference Table
This table allows quick look up to determine the ID SET numbers for each platform. This will be practically applied when we introduce CINEMA in PO004.

## Slide 12: Option Pools / Time Slot Reallocation
Notes: TP: Have the trainee find the Surveillance Option Pool table
Surveillance Option Pools allow ships the flexibility to adjust their surveillance capacity based on mission (primary track producers need more surveillance then other ships)

## Slide 13: Option Pools / Time Slot Reallocation
Notes: TP: Have the search for TSR instructions
Option pools - each option distributes the pool of timeslots differently amongst the option pool participants. Strict adherence to option/sequence numbers is required, to avoid network anomalies or data loss. The OPTASK LINK Message is the primary means of disseminating this information.
Surveillance Option Pools allow ships the flexibility to adjust their surveillance capacity based on mission (primary track producers need more surveillance then other ships); Time Slot Reallocation (TSR) is another surveillance tool used by designers.
Time Slot reallocation – TSR – used for Surveillance function, assigned to C2 platforms, dynamic reassignment of a pool of timeslots each frame dependant on demand. TSR rules: no single platform can use more than 60% of the total timeslots assigned to that group;
In connectivity matrix, TSR slot groups are indicated by Access 18/17. 18 – single timeslot where terminals transmit their desired timeslot request, 17 – slot group where the data is transmitted. If a terminal is not transmitting, it is in receive mode.

## Slide 14: TSDF – Unit Pulse Density Calculations
Notes: TP: Have the search for TSDF in the Pulse Density Calculations table
These percentages in this table indicate the total TSDF of all timeslots they are allocated whether they actually transmit on them or not. (previous lesson)

## Slide 15: Load_File breakdown
Notes: TP: This is TDL300 /400 level comprehension and only demonstrated.
Get the Trainee to find the Load_file breakout sheet for CF188, CP140, C2_MIDS (Surveillance options)

## Slide 16: Canadian Network Design Facility
Canada has two Network Designers who works for JTDLM, Mr Reza Mortazavi and Mr John Tomaszewski
file://eis-dco-mv03230/jtdlmc$
This FTP includes NDDs and Load files for CAF platforms
Requests for new load files sent thru Elemental Data Link Management Cells
Notes: TP: When an existing network no longer meets the needs of the environment it was designed for, and modification is no longer an option (not enough unassigned timeslots); a New Network may be the best option.
IER (Information Exchange Requirements) are collected and utilized to develop the Network
Networks for Exercises can have Red / Blue / Purple load files. These allow Network monitoring of all platforms, flight safety for Red platforms (lead seeing Blue); and realistic training for Blue forces.
As new platforms become L16 enabled, existing networks may need to be modified. Request for load files must be submitted early.
For non-emergency requests, the Elemental DLMC should be contacted first before anyone approaches the NDF. This will be discussed in a later EO.

## Slide 17: NDD FTP Site
Notes: TP: The ICO or Planner/supervisor is responsible to ensure you have the required load file for your platform/unit. However, there may be times when the Multi-Link Operations Specialist may be asked to obtain a load-file from the FTP. This could be because the file got corrupted (randomly happens) during your activity or shift and you need to download a new copy, or the network changes due to change of mission and you need to switch. Understanding that for every operation/exercise, there is a different load-file is important.
Before next click – advise Reza’s FTP also offers a TSDF calculator.
Specific load files are named the same based on platform and terminal type…ensure you are selecting the correct Network when downloading your assigned ID Set (load file)
You’ll notice that the file names are the same however the network where we retrieved them from are different. Once they are downloaded if not saved correctly you could be using the wrong file. If you are having issues, verify you are using the correct file.

## Slide 18
Confirmation Questions
Find and open NDD CAJE0007A
Who was this NDD designed for?
What is the ID Set for CF188?
How many different Cryptos does this network need?
Does this network have Option Pools, how many and who participates in them?
In the Connectivity Matrix, what Slot Block does the CP140s transmit Surveillance in? Is this Dedicated, TSR, or Option Pool; BONUS: How can you calculate Surveillance Capacity of this Surveillance capability?
What is the Total TSDF with Voice for the C130J?
Notes: TP: Confirmation will use NDD CAJE0007A, trainees will need to find where to ‘download’ this file first.
Confirm all trainees are using the correct NDD before proceeding;
Standing Network for the RCN and Ex CUTLASS FURY
43
Two - TSEC 1 (CVLL 0/1) and TSEC 2 (CVLL 2/3)
Yes, two pools, Option 1 Slot group 16 (512 tracks) – blue Ships/C2MIDS, Option 2 Slot Group 37 (128 tracks) – red Ships/C2MIDS;
CP140 is part of the TSR pool – the Demand message is Tx in Slot Block 18, Surveillance tracks are in Slot Block 19, TSR // Bonus: Packing limit (P4 = 4 tracks) x Total Slots per Frame (128 timeslots) = 512 tracks
18.9%

## Slide 19
QUESTIONS?