## Slide 1
Identify Link 11 Equipment
Link 11
EO 001.01
Notes: 7/01/10 Format Change

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Objectives
Identify Link 11 Equipment
Map Link 11 Equipment Connections

## Slide 4: Components of Link 11
C2 Host system
Naval Tactical Data System Card
KG-40 & KG-40A Encryptor
Data Terminal Set
Radio Transceivers

## Slide 5: C2 Host System
The C2 Host system is the computer that processes M-Series messages
  Generates M-Series messages for transmission
  Receives M-Series messages for consumption
The C2 Host system allows operators to manipulate the data in a meaningful way, for example:
  Create & delete tracks
  Change track IDs
There are many C2 Host systems in use across the CAF
  BCS-F (Air Force)
  CMS (Navy)
  TacView (Army)
  MICE (CSI)

## Slide 6: Naval Tactical Data System Card
The NTDS is the interface card that takes M-Series messages and prepares them for the Data Terminal Set
It also takes data from the DTS, and generates M-Series messages for the C2 Host to manage
Each C2 Host will have a different implementation of the NTDS
The C2 Host communicates with the NTDS, which communicates with the DTS
Few (if any) configuration options for operators.

## Slide 7: KG-40 & KG-40A Encryptor
The KG-40 encrypts data from the NTDS card before it gets to the DTS.
The KG-40 error tolerance can be configured:
  A1 – Message indicator (MI) must be error free
  A2 – MI must contain: no errors, one error – data corrected, or overall parity bit error data corrected
  B – MI not used in this mode/encrypted –decrypted regardless of errors
  Plain Text – MI not used in this mode/Secure or Clear
Notes: There are three modes that the KG-40 will operate in; A1, A2, B and Plain Text.
When selecting the different modes of operation:
A1 This means that the device will not let any message with errors through, even if it can be data corrected through error detection and correction. This is the strictest mode of operation and, because of the connectivity problems and noise on frequencies, particularly HF, this mode is not used.
A2 This is the normal operating mode for Link 11. In this mode, the MI must contain either no errors, one error that has been data corrected, or one overall parity bit error that has been data corrected.
B In this mode, the MI is not used and messages will be encrypted or decrypted regardless of errors. Since errors are not good for the tactical interface, this mode also is not used.
Plain Text: In this mode, the MI is again not used and neither is encryption. Basically, the KG-40 is bypassed. This mode is normally only used during testing and troubleshooting, not for operations.

## Slide 8: Data Terminal Set (DTS)
Data Terminal Sets convert digital information from the KG-40 to analog information suitable for transmission over the radio
Some models have more features than others
  Some cannot operate SLEW
AN USQ-125 (V)
Notes: The data terminal set (DTS) acts as a MODEM for Link 11 and also controls the functions of the NCS and the Picket station. As the NCS, the DTS will transmit the polls for the picket stations in accordance with the entered polling sequence. For a picket station, the DTS controls the transmission to reply to the poll sent by the NCS. Both NCS and picket are machine functions and require no operator action except to enter the polling sequence.

## Slide 9: Data Terminal Set (DTS)
Data Terminal Sets convert digital information from the KG-40 to analog information suitable for transmission over the radio
Several types of models in use
  USQ-125
  MX-512
Some models have more features than others
  Some cannot operate SLEW
May be configured into a split-site configuration for extended range
AN USQ-125 (V)
Notes: The data terminal set (DTS) acts as a MODEM for Link 11 and also controls the functions of the NCS and the Picket station. As the NCS, the DTS will transmit the polls for the picket stations in accordance with the entered polling sequence. For a picket station, the DTS controls the transmission to reply to the poll sent by the NCS. Both NCS and picket are machine functions and require no operator action except to enter the polling sequence.

## Slide 10: Data Terminal Set Controller
The DTS requires configuration
  NCS vs Picket
  CLEW vs SLEW
  Fast vs Slow
This configuration is controlled through an external controller
  Unit specific implementation
Notes: Link 11 is a secure data link, thus is required to be run encrypted. The encryption device that is utilized in Link 11 is called the KG-40.
Will not operate without encryption

## Slide 11: Radio Transceivers
A HF or UHF radio is required to transmit and receive data
Also includes antenna selection
  Directional vs Omni-Directional
Capabilities dependent on individual Operational Units
Notes: Link 11 is a secure data link, thus is required to be run encrypted. The encryption device that is utilized in Link 11 is called the KG-40.
Will not operate without encryption

## Slide 12: Link 11 Equipment Map
C2 Host
NTDS Card
KG-40
DTS
Radio Transceiver
DTS Controller
Antenna
Notes: Link 11 is a secure data link, thus is required to be run encrypted. The encryption device that is utilized in Link 11 is called the KG-40.
Will not operate without encryption

## Slide 13: Summary
Identify Link 11 Equipment
Map Link 11 Equipment Connections

## Slide 14: Confirmation Questions
What are 2 tasks the NTDS Card performs?
  Process M-Series messages into a format for the DTS
  To take data from the DTS, and generate M-Series messages from it
What piece of equipment is configured to act as NCS or Picket?
  DTS
If the DTS cannot communicate with the NTDS Card, what equipment is most likely to blame?
  KG-40, it is the pathway between the DTS and the NTDS Card

## Slide 15
QUESTIONS?