## Slide 1
Define Link 11B
EO 001.01
Notes: 7/01/10 Format Change

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Objectives
Identify Link 11A Characteristics
Identify Link 11B Characteristics
Compare Link 11A and Link 11B
Identify Link 11 Gateways

## Slide 4
Link 11A/B Use Cases
Link 11 A:
  Developed for the Navy
  Adopted by the Air Force
  Still widely used as a BLOS RF Data Link
Link 11 B:
  Used primarily by the Army and Marines
  Used heavily in Air Defense Batteries
  Quickly becoming obsolete. If you have the infrastructure to do Link 11B, use JREAP-B
Link 11 Sundown 2025
  NSA no longer generating Crypto post sundown
  Will another country generate crypto?

## Slide 5: Characteristics of Link 11A
Half duplex
Netted
Secure link
Roll call mode
  NCS
  Picket
Participating Units
M-Series messages
NCS
Picket 3
Picket 1
Picket 5
Picket 4
Picket 2
NCS Broadcasts, then Polls Picket 1
NCS Polls Picket 2
NCS Polls Picket 3
NCS Polls Picket 4
NCS Polls Picket 5
Picket 1 Broadcasts Response
Picket 2 Broadcasts Response
Picket 3 Broadcasts Response
Picket 4 Broadcasts Response
Picket 5 Broadcasts Response
1.
2.
3.
4.
6.
5.
7.
9.
8.
10.
Notes: The basic characteristics of L11 are that it is Half duplex. Meaning it can transmit or receive but not both simultaneously. Netted in that it utilizes a network, Secure. It is written using M series messages.

## Slide 6: Characteristics of Link 11B
Point-to-point
Full Duplex
Reporting Units
Uses serial comms
  Phone lines
  Serial cables
  Multichannel radio direct connections
M-Series Messages
Link 11B RU 1
Link 11B RU 2
Link 11B RU 3
Full Duplex
Full Duplex
Full Duplex
*Each RU requires 2 serial lines!
Notes: HF High Frequency RF
is the ITU (International Telecommunication Union)-designated range of radio frequency electromagnetic waves (radio waves) between 3 and 30 MHz It is capable of Long range and is beyond line of sight. It can be noisy to listen to, especially man-made interference from electronic devices, tends to have a great effect on the HF bands

## Slide 7: Link 11 A/B Similarities
Both defined by the same standards
  MIL-STD 6011
  STANAG 5511
Both use M-Series Messages
  Both share benefits
  Both share drawbacks
  Routing possible between Link 11 A/B without data loss
Notes: HF High Frequency RF
is the ITU (International Telecommunication Union)-designated range of radio frequency electromagnetic waves (radio waves) between 3 and 30 MHz It is capable of Long range and is beyond line of sight. It can be noisy to listen to, especially man-made interference from electronic devices, tends to have a great effect on the HF bands

## Slide 8: Link 11 A/B Differences
Mediums
  Link 11A is RF UHF & HF
  Link 11B is serial based
Architecture
  Link 11A is netted, half duplex, and controlled by NCS
  Link 11B is automatic full duplex point to point only
Crypto
  Link 11A uses the KG40/A for encryption
  Link 11B encrypts the serial carrier, and is transparent to the Link
Equipment
  Link 11A uses NTDS/KG-40/DTS
  Link 11B uses a modem to exchange digital data
Notes: HF High Frequency RF
is the ITU (International Telecommunication Union)-designated range of radio frequency electromagnetic waves (radio waves) between 3 and 30 MHz It is capable of Long range and is beyond line of sight. It can be noisy to listen to, especially man-made interference from electronic devices, tends to have a great effect on the HF bands

## Slide 9: Link 11 Gateways
NCS
Picket 1 and RU 1
Picket 2
Link 11B RU 2
Link 11B RU 3
Data can move between Link 11A and Link 11B by using a Gateway
Gateway units need equipment for both Link 11A and Link 11B
Implementation of Gateways is governed by the OPTASKLINK
Link 11A
Link 11B
Link 11 Gateway
Notes: HF High Frequency RF
is the ITU (International Telecommunication Union)-designated range of radio frequency electromagnetic waves (radio waves) between 3 and 30 MHz It is capable of Long range and is beyond line of sight. It can be noisy to listen to, especially man-made interference from electronic devices, tends to have a great effect on the HF bands

## Slide 10: Problem Solving Activity
3 Groups
  Group 1: Link 11A HF
  Group 2: Link 11A UHF
  Group 3: Link 11B
Two members of the class are Link 11Gateways
Create a configuration that will allow information to pass freely through all groups
What equipment will be necessary for this to work?

## Slide 11: Summary
Identify Link 11A Characteristics
Identify Link 11B Characteristics
Compare Link 11A and Link 11B
Identify Link 11 Gateways

## Slide 12
QUESTIONS?