## Slide 1
EO 001.06
VMF Waveforms and Requirements

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
VMF Waveforms
Equipment used
Special Requirements

## Slide 4
References
MILSTD 6017A
STANAG 5519
WWW.
MIL-STD-188-220
Understanding Voice and Data Link Networking

## Slide 5: VMF Waveforms
VMF is designed as a common means of exchanging digital data across an interface that could be between combat units at varied organizational levels, with varying needs for volume and detail of information, and applicable to a broad range of tactical communication systems.
This flexibility was achieved through the information variability of each message and by designing the standards so that the communications or network functions are independent of the textual section of the message. This separation of the communications function from the message textual section also provides the capability of changing one without affecting the other.
Notes: “Tactical radio hardware is not unlike a smartphone. An entire population using smartphones is like a battlefield full of soldiers, where different applications running on the smartphones (or as online service coming from the internet) give the people the desired functionality (for their devices).” Mr. Sohajek continued that: “Without any additional application running on a smartphone you can make a voice call or send a text, which is sufficient for certain people, however most people need more. Using additional applications you can exchange emails, files, pictures and videos to be played offline. Other people want to stream video, which requires different applications or services.”

## Slide 6: VMF Waveforms Cont.
High Frequency (HF)
High frequency (HF) is the International Telecommunication Union (ITU) designation for the range of radio frequency electromagnetic waves (radio waves) between 3 and 30 megahertz (MHz).
Notes: The dominant means of long-distance communication in this band is skywave ("skip") propagation, in which radio waves directed at an angle into the sky refract back to Earth from layers of ionized atoms in the ionosphere. By this method HF radio waves can travel beyond the horizon, around the curve of the Earth, and can be received at intercontinental distances. However, suitability of this portion of the spectrum for such communication varies greatly with a complex combination of factors:
Sunlight/darkness at site of transmission and reception
Transmitter/receiver proximity to solar terminator
Season
Sunspot cycle
Solar activity
Polar aurora
.

## Slide 7: VMF Waveforms Cont.
Very High Frequency (VHF)
Very high frequency (VHF) is the International Telecommunication Union (ITU) designation for the range of radio frequency electromagnetic waves (radio waves) from 30 to 300 megahertz (MHz), with corresponding wavelengths of ten meters to one meter.
Notes: Radio waves in the VHF band propagate mainly by line-of-sight and ground-bounce paths; unlike in the HF band there is only some reflection at lower frequencies from the ionosphere (skywave propagation). They do not follow the contour of the Earth as ground waves and so are blocked by hills and mountains, although because they are weakly refracted (bent) by the atmosphere they can travel somewhat beyond the visual horizon out to about 160 km (100 miles).

## Slide 8: VMF Waveforms Cont.
Ultra High Frequency (UHF)
Ultra High frequency (HF) is the International Telecommunication Union (ITU) designation for the range of radio frequency electromagnetic waves (radio waves) between 300 and 3000 megahertz (MHz).
Notes: Radio waves in the UHF band travel almost entirely by line-of-sight propagation (LOS) and ground reflection; unlike in the HF band there is little to no reflection from the ionosphere (skywave propagation), or ground wave. UHF radio waves are blocked by hills and cannot travel beyond the horizon, but can penetrate foliage and buildings for indoor reception. Since the wavelengths of UHF waves are comparable to the size of buildings, trees, vehicles and other common objects, reflection and diffraction from these objects can cause fading due to multipath propagation, especially in built-up urban areas. Atmospheric moisture reduces, or attenuates, the strength of UHF signals over long distances, and the attenuation increases with frequency.

## Slide 9: Equipment used
Single Channel Ground and Airborne Radio System (SINCGARS)
SINCGARS is a family of Very High Frequency (VHF) Frequency Modulated (FM) radio sets. It is designed for simple, quick operation using a 16 element keypad for push button tuning. SINCGARS is capable of short range or long range operation for voice or digital communications.
Notes: SINCGARS’ primary role is voice transmission for command and control (C2) between surface and airborne C2 assets. SINCGARS can transmit and receive secure data and facsimile transmissions through simple connections with various data terminal equipment.
SINCGARS electronic attack security features provide multiservice, Army, Marine, Navy, and Air Force communications interoperability, thus contributing to successful combat operations. SINCGARS is consistent with North Atlantic Treaty Organization interoperability requirements. The radios, which handle voice and data communications, are designed to be reliable, secure, and easily maintained. Vehicle-mount, backpack, airborne, and handheld form factors are available.

## Slide 10: Equipment used Cont.
HAVE QUICK
family of military radios and associated communications security equipment, principally used for aircraft, shipboard, satellite, and other applications where there is a direct line-of-sight between the transmitter and receiver, or between the transmitter and a satellite or other relay. They operate in UHF which is often preferred in aircraft applications because its antennas are physically smaller than the equivalent in the very high frequency (VHF) spectrum.
Notes: HAVEQUICK is a frequency hopping system is used as an anti-jamming communication system. Basically the HAVEQUICK system uses a series of 16 UHF AM (225-380 MHz) radio frequencies. During a radio transmission a computer in the aircraft rapidly switches the transmission between the 16 pre-set frequencies, both the length and order of frequency selection are "random" and are based on very precise timing. The the transmitter and receiver must be "in-sync" as to the timing of each frequency switch or the received signal will be broken.

## Slide 11: Equipment used Cont.
The Enhanced Position Location Reporting System (EPLRS)
EPLRS is a network of wireless tactical radios that distributes digital data between many mobile users. EPLRS also has a position reporting capability allowing mobile users to determine their position based on time difference of arrival measurements from multiple reference radio units.
Notes: The Enhanced Position Location Reporting System (EPLRS) is a network of wireless tactical radios that distributes digital data between many mobile users. In addition, EPLRS has a position reporting capability allowing mobile users to determine their position based on time difference of arrival measurements from multiple reference radio units.

## Slide 12: Equipment used Cont.
Digitally Aided Close Air Support (DACAS)
Android-based version of its Networked Joint Fires Cross Platform Dismounted Solution, an off-the-shelf Google Pixel tablet connected to a tactical hub supporting a TNR (Tactical Net Rover), a laser range finder, GPS, 152A or 117G radio, and a conformal battery.
Notes: JTACs can send and receive a variety of messages from 9-Lines to friendly points without coordinating VMF settings prior to the mission for both aircraft and other JTACs.This is the first truly operator friendly VMF solution.

## Slide 13: Equipment used Cont.
PRC 152A FALCON RADIO
The L3Harris Falcon III AN/PRC-152A provides simultaneous voice, video and high-speed data in a highly portable form factor. Employing the Soldier Radio Waveform (SRW) and L3Harris Adaptive Networking Wideband Waveform (ANW2®C) this handheld delivers ad-hoc, self-healing and adaptive networking capabilities to dismounted soldiers on the move.
Notes: The AN/PRC-152A covers the multiband frequency range, with 5 W transmit power for Line-Of-Sight narrowband waveforms including SINCGARS, HAVEQUICK I/II, and AM/FM VULOS, and a 10 W burst for legacy SATCOM.

## Slide 14: Equipment used Cont.
PRC 117G RADIO
The AN/PRC-117G Multiband Manpack Radio, or Multiband Multi Mission Radio (MBMMR), is a man-portable, tactical software-defined combat-net radio, covering the 30-2000 MHz frequency range, and provided with internal SAASM GPS (optionally an external commercial GPS can be connected).
Notes: The AN/PRC-117G radio is a single channel voice and data radio that is capable of operating in a frequency range of 30 Megahertz to 2 Gigahertz. Operational configurations include manpack, vehicular-mounted, or base-station operations. The primary AN/PRC-117G waveform is the ANW2, which is a Harris Corporation proprietary waveform. The AN/PRC-117G is capable of simultaneously transmitting both Voice over Internet Protocol and digital data on a single channel. Digital data include file transfers, chat, streaming video, and position location reports. The AN/PRC-117G can be used as a tactical satellite radio and to provide a networking radio bridge capability until the Manpack Radio and Mid-Tier Networking Vehicular Radio (MNVR) programs of record are available.

## Slide 15: Equipment used Cont.
Demand Assigned Multiple Access (DAMA)
DAMA is a protocol used in satellite communications, particularly Very Small Aperture Terminal (VSAT) systems. DAMA enables efficient and instantaneous assignment of transponder channels on a first come, first served basis according to data priority.
Notes: Demand Assignment Multiple Access (DAMA) is a class of multiple-access techniques that permit a population of users to share satellite resources on a demand basis. The need for flexible local and long-haul communications by mobile military users is increasing rapidly. Radio nets cannot provide the long- haul connectivity and, for the most part, do not support point-to-point communications. Thus, only satellite communications can meet the needs of these mobile users. DAMA permits more efficient and flexible allocation of
limited satellite resources.

## Slide 16: Equipment used Cont.
Ethernet
Ethernet is a way of connecting computers together in a local area network or LAN. It has been the most widely used method of linking computers together in LANs since the 1990s. The basic idea of its design is that multiple computers have access to it and can send data at any time.
Notes: Ethernet is the traditional technology for connecting devices in a wired local area network (LAN) or wide area network (WAN), enabling them to communicate with each other via a protocol -- a set of rules or common network language. Ethernet describes how network devices can format and transmit data so other devices on the same local or campus area network segment can recognize, receive and process the information. An Ethernet cable is the physical, encased wiring over which the data travels.
Connected devices accessing a geographically localized network with a cable -- that is, with a wired rather than wireless connection -- likely use Ethernet. From businesses to gamers, diverse end users depend on the benefits of Ethernet connectivity, which include reliability and security.

## Slide 17: Special Requirements
Equipment (radios, computers, antennas, etc.);
Crypto;
Human Interface (Software);
Frequencies, Satellite Access;
Gateways, cross domain solutions; and
Environment (security, LOS etc.)
Notes: Guided Discussion
Equipment – What type of radio do you need IOT exchange VMF data with the required platforms? Does anyone else require this information via BLOS? Is there a particular type of antenna required (omni, directional, high gain etc).
Crypto - Will crypto be required IOT participate in data exchange?
Human Interface – Is a type of sofware required to T/R, or view the VMF messages?
Frequencies – What frequencies will be used and where will you find them? (OTL)
Gateways – Will this data be combined with a bigger picture, or be sent on to secret enclave?
Environment – What security and safety factors must you take into consideration?

## Slide 18
Confirmation Questions
Is VMF limited to one medium?
What are some different types of equipment used to T/R VMF?
Who is the primary user of VMF?
Notes: No
SINCGARS, HAVEQUICK, 117G, FALCON, EPLRS ETC.
Land Force

## Slide 19
QUESTIONS?