## Slide 1
EO 002.03
Extract Link 22 Super Network & Network Parameters
from OTL

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
References
SETID Descriptors List
Link 22 Super Network
  NILE Super Network Info - NSNET
  Joint Cryptographic Data - JCRYPDAT
  FORCE FILTER
Link 22 Network
  NILE Network Info - NNET
  NILE Network Participants - NNETPART
  NILE Network Media Parameters & Settings - NNMEPARS
  NILE Network Cycle Structures - NNCS
  NILE Unit Bandwidth Requirements - NUBWR
  NILE Crypto Variable Logic Label Indicator - CRYPLST
  NILE Mission Area Sub Network - NMASN

## Slide 4
References
APP 11 (D) 1
ADAPT 33
STANAG 5522
Notes: Your references are as follows:
APP 11 (D) 1
ADAPT 33
STANAG 5522
The main one for dissecting and extracting Link22 tactical data will be APP 11 (D) 1, MRN #N017, Version 5.2
This document will be supplied to you as we proceed through the various SETIDs used for creating and entering in the correct data in correct format: while also more important for this class, being able to break down these same SETID with ease.

## Slide 5
SETID Descriptors
Notes: This is the list of the 11 Link 22 SETID Descriptors we will be covering for this lesson which focuses on extracting Link 22 Super Network & Network Parameters from an OTL.
(Instructor to review name and Format Name Sets)
These IDSETs are either Mandatory (M), Conditional (C), or Operational )(O).
  If mandatory the IDSET must be included in the completed OTL.
  If conditional then this SETID is required due to a data variable entered in a mandatory SETID field.
  If Operationally Determined then SETID required for this Mission/Exercise

## Slide 6
NILE SUPER NETWORK INFO -NSNET
Notes: LINK 22 SUPER NETWORK INFORMATION: Provides information about the LINK 22 super network.
This is a mandatory SETID for OTL.
LINK 22 SUPER NETWORK IDENTIFIER: Enter identifier assigned to the LINK 22 super network, for example: "SACLAN07B".
SNMU ADDRESS: Enter the LINK 22 track number assigned to the Super Network Management Unit (SNMU), for example: "01000
STANDBY SNMU ADDRESS: Enter the LINK 22 track number assigned to the stand-by super network management unit, for example: "01001".
SUPER NETWORK OST: Enter the date time group for the Operational Start Time (OST) of the LINK 22 super network, for example: "142359ZJUN2005".
NUMBER OF LINK 22 NETWORKS: Enter the number of LINK 22 networks assigned to the super network, for example: "8". Range is 1-8.
NUMBER OF LINK 22 UNITS: Enter the number of LINK 22 units assigned to the super network and its assigned LINK 22 networks, for example: "120". Range 2 through 125.
LOWEST LINK 22 ADDRESS : Enter the lowest LINK 22 address allocatable for this super network, for example: "20". Range 1 through 124.
Of note Canada does not operate in a Super network environment, only a single network at a time. This may change in the future as Link 22 becomes more operational.

## Slide 7
JOINT CRYPTOGRAPHIC DATA - JCRYPDAT
Notes: LINK 16 AND LINK 22 CRYPTOGRAPHIC DATA: Reports Multi-functional Information Distribution System (MIDS) LINK 16 and LINK 22 unique cryptographical data. Meaning this SETID is used for both, hence why it starts with a J.
This is a mandatory SETID for OTL.
CRYPTOVARIABLE LOGICAL LABEL (CVLL): Enter the LINK 16 Crypto Variable Logical Label (CVLL), for example: "127". Range 1 through 127.
KEY SHORT TITLE: Enter the crypto key short title associated with the CVLL, for example: "AKZT3180A1".
ENCRYPTION KEY SHORT TITLE: Enter the encryption key short title, for example: "AKZT3183A1
SECURE DATA UNIT (SDU) LOCATION NUMBER: Enter the Secure Data Unit (SDU) location number for the CVLL, for example: "45". And 67 both for SDU for use in example.

## Slide 8
FORCE FILTER - FORCEFLTR
Notes: LINK 22 FORCE FILTERS : Assigns the force-level active filter(s).
This is An Operationally Determined SETID for OTL.
FILTER IDENTIFIER NUMBER: Enter the transmit/forward filter number, for example: "FAB28".
In this example FAB stands for “DATA FORWARDING FILTER FOR DATA FORWARDED FROM LINK 16 TO LINK 11 AND LINK 11B”
Currently there is no designation for Link 22 other then: “TRANSMIT FILTER FOR ALL LINKS IN A MULTI LINK INTERFACE” which is M.

## Slide 9
NILE NETWORK INFO - NNET
Notes: LINK 22 NILE NETWORK INFORMATION: Provides information about the LINK 22 network.
This is A MANDATORY SETID for OTL.
This is a mandatory SETID for OTL.
LINK 22 NETWORK IDENTIFIER: Enter the LINK 22 network identifier, for example: "7". Range is 1-8.
LINK 22 NETWORK ADDRESS: Enter the LINK 22 address for the network (LINK 22 network group identifier address), for example: "00172".
NMU ADDRESS: Enter the LINK 22 address for the Network Management Unit (NMU), for example: "00174".
STANDBY NMU ADDRESS: Enter the LINK 22 address for the stand-by Network Management Unit (NMU), for example: "00175".
OPERATIONAL NCS PROVIDER: NETWORK CYCLE STRUCTURE: Enter the Operational Network Cycle Structure (ONCS) provider, for example: "DLP". Choices are DLP or SNC.
  DLP - DATA LINK PROCESSOR: The network management unit´s data link processor (DLP) supplies the operational network cycle structure for the link 22 network.
  SNC - SYSTEM NETWORK CONTROLLER: The network management unit´s system network controller (SNC) calculates the best operational network cycle structure based on available communication parameters and (if enabled) probing results.
DTDMA INDICATOR: Enter "DTDMA:" followed by the indicator of whether the Dynamic Time Division Multiple Access (DTDMA) is enabled or disabled, for example: "DTDMA:ENABLED”
LINK-LEVEL COMSEC INTEGRITY INDICATOR: Enter "DIVS:" followed by the indicator of whether the LINK 22 network link-level COMSEC data integrity verification service is enabled or disabled, for example: "DIVS:DISABLED".

## Slide 10
NILE NETWORK PARTICIPANTS - NNETPART
Notes: LINK 22 NETWORK PARTICIPANTS: Provides information about the LINK 22 network participants.
This is A MANDATORY SETID for OTL.
LINK 22 UNIT ADDRESS: Enter the LINK 22 octal track number assigned to the LINK 22 unit, for example: "01001".

## Slide 11
NILE NETWORK MEDIA PARAMETER SETTINGS - NNMEPARS
Notes: LINK 22 NETWORK MEDIA PARAMETER SETTINGS: Provides information about the LINK 22 network media parameter settings.
This is A MANDATORY SETID for OTL.
LINK 22 NETWORK MEDIA TYPE: Enter the LINK 22 network media type, for example: "UHFEPM". Choices are HFFF/HFEPM/UHFFF/UHFEPM.
LINK 22 FRAGMENTATION RATE: Enter the indicator of the fragmentation rate in a LINK 22 network, which specifies the number of coding frames in each network packet, for all participants of the LINK 22 network, for example: "1". Choices are 1-3, default is 1.
PRIMARY FREQUENCY: Specifies the primary frequency range or plan designator. Enter the radio frequency, for example: "122.1GHZ".
SECONDARY FREQUENCY: Specifies the secondary frequency range or plan designator. Enter the radio frequency, for example: "122.1GHZ".
HF LINK 22 HOP SET: Specifies the HF HOPSET designator in one of the following ways: Enter the indicator for a HF HOPSET used in a LINK 22 network, for example: "N13E7FF". N = HF,
UHF LINK 22 HOP SET: Specifies the UHF HOPSET designator in one of the following ways: Enter the indicator for a UHF HOPSET used in a LINK 22 network, for example: "A123E0A". A = UHF.
INITIALIZATION MODE: Enter the initialization mode for the LINK 22 network, for example: "PROBE“ or “SHORT” .
LINK 22 NETWORK START TIME Enter "NST:" followed by the date time group for the Network Start Time (NST) of the LINK 22 network, for example: "NST:161500ZJUN2005".
LINK 22 PROBING START TIME: Enter "PST:" followed by the date time group for the LINK 22 network Probing Start Time (PST), for example: "PST:152045ZJUN2005".
MEDIA SETTING NUMBER: Enter the Media Setting Number (MSN) associated with a network media type to a LINK 22 network, for example: "UHFEPM1".
There are a lot of parameters in this SETID that require certain fields depending on where/or if data entered in other fields. Here are the restrictions:
FIELD 3 IN SET ^ (NNMEPARS) IS REQUIRED IF FIELD 1 IN SET ^ (NNMEPARS) EQUALS "HFFF" OR "UHFFF", OTHERWISE IT IS PROHIBITED.
FIELD 4 IN SET ^ (NNMEPARS) IS PROHIBITED IF FIELD 3 IN SET ^ (NNMEPARS) DOES NOT OCCUR.
FIELD 5 IN SET ^ (NNMEPARS) IS REQUIRED IF FIELD 1 IN SET ^ (NNMEPARS) EQUALS "HFEPM", OTHERWISE IT IS PROHIBITED.
FIELD 6 IN SET ^ (NNMEPARS) IS REQUIRED IF FIELD 1 IN SET ^ (NNMEPARS) EQUALS "UHFEPM", OTHERWISE IT IS PROHIBITED.
FIELD 8 IN SET ^ (NNMEPARS) IS REQUIRED IF FIELD 7 IN SET ^ (NNMEPARS) EQUALS "SHORT", OTHERWISE IT IS PROHIBITED.
FIELD 9 IN SET ^ (NNMEPARS) IS REQUIRED IF FIELD 7 IN SET ^ (NNMEPARS) EQUALS "PROBE", OTHERWISE IT IS PROHIBITED.

## Slide 12
NILE NETWORK CYCLE STRUCTURE - NNCS
Notes: LINK 22 NETWORK CYCLE STRUCTURE Provides information about the LINK 22 network structure.
This is CONDITIONAL SETID for OTL. (NNCS) IS REQUIRED IF FIELD 4 IN (NNET) EQUALS "DLP", OTHERWISE IT IS PROHIBITED. And the example will be NNCS/-/-/-//.
TOTAL LINK 22 TX SLOTS: Enter the total number of transmission (TX) slots in the Operational Network Cycle Structure (ONCS) of a LINK 22 network, for example: "256".
UNIT LINK 22 ADDRESS: Specifies the unit LINK 22 address or special interrupt slot address. Enter the unit LINK 22 address, for example: "00125". Enter "INT:" followed by the special interrupt slot address, for example: "INT:00000".
LINK 22 TX SLOT SIZE: L22 MINI SLOTS. Enter the LINK 22 transmission (TX) slot size expressed in mini slots, for example: "32". Range is 2 through 32.

## Slide 13
NILE UNIT BANDWIDTH REQUIREMENT - NUBWR
Notes: LINK 22 BANDWIDTH REQUIREMENT: Provides information about the LINK 22 bandwidth requirement.
This is CONDITIONAL SETID for OTL. (NUBWR) IS REQUIRED IF FIELD 4 IN (NNET) EQUALS "DLP", OTHERWISE IT IS PROHIBITED.
ONCS EFFICIENCY : Enter the Operational Network Cycle Structure (ONCS) efficiency, for example: "75". range [75 through 100].
ONCS ACCESS DELAY TOLERANCE: Enter the Operational Network Cycle Structure (ONCS) access delay tolerance, for example: "0". 0=No tolerance, 1=Low tolerance, 2= Medium tolerance, 4= High tolerance.
UNIT LINK 22 ADDRESS: Enter the LINK 22 octal track number assigned to the LINK 22 unit, for example: "00776".
CHANNEL CAPACITY NEED: Enter the unit's channel capacity need index indicator, for example: "1". Choices go from 0=Ultra Low to 7= Ultra High.
CHANNEL ACCESS DELAY : Enter the unit's maximum channel access delay index requirement, for example: "1". Range goes from 0=unlimited to 5=high update rate.

## Slide 14
NILE CRYPTO VARIABLE LOGIC LABEL INDICATOR - NCRYPLST
Notes: CRYPTO VARIABLE LOGICAL LABEL INDICATOR Provides information about the LINK 22 network cryptographic resource description
This is A MANDATORY SETID for OTL.
CVLL INDICATOR: Enter the Crypto Variable Logical Label (CVLL) indicator, for example: "127". range [1 through 127]
KEY USE START TIME: Enter the date-time group of the expected or estimated key use start time, for example: "051516ZJUN2005”

## Slide 15
NILE MISSION AREA SUBNETWORK - NMASN
Notes: LINK 22 MISSION AREA SUBNETWORK Provides information about the LINK 22 mission area subnetwork.
MASN IDENTIFIER: Enter the Mission Area Sub Network (MASN) identifier, for example: "21". range [9 through 31]
MASN ADDRESS: Enter the group identifier address for the Mission Area Sub Network (MASN), for example: "00164".
MASN NAME: Enter the Mission Area Sub Network (MASN) name, for example: "ASW BARRIER".
MASN UNIT ADDRESS: Enter the LINK 22 unit number assigned to the mission area sub network unit, for example: "00175".

## Slide 16
Confirmation Questions
Conduct 002.03.02 - Extract NILE Link 22 Super Network & Network Parameters for Mission Planning Sheet exercise utilizing the following resources:
    LO 002.03.01 lesson plan
    APP11 (D) OTL Break down.

## Slide 17
QUESTIONS?