## Slide 1
EO 001.06
Describe Joint Range Extension Application Protocol (JREAP)

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
JREAP Definition
JREAP A
JREAP B
JREAP C

## Slide 4
References
CJCSM 6120.01, Joint Multi-Tactical Data Link (TDL) Operating Procedures (JMTOP)
Understanding Link 16
MIL-STD-3011, Military Standard for JREAP

## Slide 5: JREAP Definition
JREAP is the protocol and message structure for the transmission and reception of pre-formatted messages over communications media other than those for which these messages were designed.
JREAP provides a foundation for Joint Range Extension (JRE) of Link 16 and other tactical data links (TDL) to overcome the line-of-sight (LOS) limitations of other radio terminals such as the Joint Tactical Information Distribution System (JTIDS) and Multi-Functional Information Distribution System (MIDS)
  Extends coverage of these data links through the use of long haul media
Notes: A communication protocol is a system of rules that allow two or more entities of a communications system to transmit information via any kind of variation of a physical quantity. The protocol defines the rules, syntax, semantics and synchronization of communication and possible error recovery methods. Protocols may be implemented by hardware, software, or a combination of both.
Reduces reliance on relay platforms.
Reduction in capacity of Link networks.
Back up of communications if primary is lost.
Users without Link 16 equipment can utilise information.
JREAP was developed due to the need to communicate data over long distances without degradation to the message format or content. JREAP takes the message from the format it was originally formatted in and changes the protocol so that the message can be transmitted over Beyond Line-of Sight media.

## Slide 6: Prior to JREAP (BLOS)
Satellite Link 11
HF Link 11
Satellite Link 16
Serial Link 16
Socket J
Notes: All of these communications protocols have update rates that are very slow, or have compatibility issues. They should only be used for situational awareness, if used at all.

## Slide 7: JREAP TYPES
JREAP A (Satellite)
JREAP B (Serial)
JREAP C (TCP/IP Ethernet)
Notes: The JREAP enables tactical data to be transmitted over digital media and networks not originally designed for tactical data exchange. Formatted tactical digital messages are embedded inside of JREAP messages as data fields within available commercial and Government protocols, such as those used over satellites and terrestrial links. Specialized management messages are also provided to transport data not contained in the formatted messages, in order to support TDL-unique functions.

## Slide 8: JREAP A
JREAP A is an encrypted satellite link using a serial data interface to exchange information in a half-duplex or broadcast mode
JAOC
CVN
Notes: Half-duplex devices can only transmit in one direction at one time. With half-duplex mode, data can move in two directions, but not at the same time. The term duplex, on its own, refers to the capability to send and receive data. Duplex is often used when talking about conversations over a telephone or computer.
In computer networking, telecommunication and information theory, broadcasting is a method of transferring a message to all recipients simultaneously.
Military Ultra High Frequency (UHF) satellite and terrestrial Radio frequency (RF) communications are half duplex.
Military Super High Frequency (SHF) Satellite Communications (SATCOM) support full duplex operations but are limited to point-to-point circuits.
Military Extremely High Frequency (EHF) Medium Data Rate (MDR) SATCOM has circuit configuration limitations Commercial SATCOM is mostly point-to-point and supports full-duplex usage.

## Slide 9: JREAP A MEDIA
25 kHz UHF TDMA/DAMA SATCOM (MIL-STD-188-183)
5 and 25 kHz UHF non-DAMA SATCOM (MIL-STD-188-181)
Notes: DAMA multiplexing channels allow dedicated access to portions of the channel without interference and, through time division multiple access (TDMA), enables more networks to access the channel. TDMA is accomplished when a network controller station transmits control signals that establish precisely recurring intervals of time (frames).
Demand-Assigned Single Channel, DASA. This mode offers operation on single channel, which is often requested by the users. The broadcast is accessible only on either 5 kHz or 25 kHz via the control system of DAMA waveforms.
Baud rates are 2400 and 4800 bps (operator selectable).
C2 host software is required.

## Slide 10: JREAP B
JREAP B is a secure synchronous or asynchronous point-to-point serial data interface used to exchange information in a full-duplex data-transparent mode.
JAOC
BDE TOC
Notes: In Synchronous Transmission, data is sent in form of blocks or frames. This transmission is the full duplex type. Between sender and receiver the synchronization is compulsory. In Synchronous transmission, There is no gap present between data. It is more efficient and more reliable than asynchronous transmission to transfer the large amount of data/
In Asynchronous Transmission, data is sent in form of byte or character. This transmission is the half duplex type transmission. In this transmission start bits and stop bits are added with data. It does not require synchronization.

## Slide 11: JREAP B MEDIA
MUX
VIPER via phone lines
KG-84A/KIV-7
Other point-to-point full-duplex
media devices
Notes: In communication transmission systems, mux (pronounced muks, sometimes spelled "MUX") is an abbreviation for multiplexing, a device that sends multiple signals on a carrier channel at the same time in the form of a single, complex signal to another device that recovers the separate signals at the receiving end.
The VIPER Universal Secure Phone allows you to easily switch between making end-to-end secure and non-secure calls on Voice over IP and analog networks, eliminating the need for multiple desktop phones. The VIPER is the only VoIP phone certified to protect information classified Top Secret/SCI and below over commercial wired networks. In Asynchronous Transmission, data is sent in form of byte or character. This transmission is the half duplex type transmission. In this transmission start bits and stop bits are added with data. It does not require synchronization.
The KG-84 and KIV-7 are encryption devices.
Baud rates vary with infrastructure capabilities (ex ISDN).

## Slide 12: JREAP C
JREAP C is a secure data link interface that encapsulates JREAP over Internet Protocol (IP) using IP based networks for the exchange of information.
TCP
UDP
JAOC
LAN/WAN
TACC
Notes: The Internet Protocol (IP) is the method or protocol by which data is sent from one computer to another on the Internet. Each computer (known as a host) on the Internet has at least one IP address that uniquely identifies it from all other computers on the Internet.
TCP (Transmission Control Protocol) is a standard that defines how to establish and maintain a network conversation through which application programs can exchange data. TCP works with the Internet Protocol (IP), which defines how computers send packets of data to each other.
UDP (User Datagram Protocol) is a communications protocol that is primarily used for establishing low-latency and loss-tolerating connections between applications on the internet. It speeds up transmissions by enabling the transfer of data before an agreement is provided by the receiving party.

## Slide 13: JREAP C MEDIA
Secure Net Based Applications (CSNI)
TDL WAN (For CAF TDL information sharing)
IICB
TACLANE
LAN
Notes: CONSOLIDATED SECRET NETWORK INFRASTRUCTURE (CSNI) is a secure network used by the Government of Canada.
TDL WAN is an enclave within CSNI.
IICB (need more information)
TACLANE is an encryption device.
LAN
Baud rates are extremely high, network dependant.

## Slide 14
Confirmation Questions
What is JREAP?
What are the three types of JREAP?
What does JREAP take advantage of?
Notes: JREAP is the protocol and message structure for the transmission and reception of pre-formatted messages over communications media other than those for which these messages were designed.
JREAP A, B, C
Civilian infrastructure

## Slide 15
QUESTIONS?