## Slide 1
EO 001.02
Explore Link 16 Terminals and Features

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
Describe the types and features of the various Link 16 terminals used in Canada:
  MIDS LVT Family
  Small Tactical Terminal (STT)
  TacNet Tactical Radio (TTR)
  Battlefield Awareness and Targeting System (Dismounted)
  MIDS Joint Tactical Radio System (JTRS)
  MIDS on Ship (MOS)

## Slide 4
MIDS LVT Legacy
MIDS LVT 1/4/7
  CF188 (1s), HMCS Frigates (4s), CC130J (4s)
  Requires host platform to control;
  ground units requires Mini-Rack to control
  J-Voice
  200 W / 1000 W
MIDS LVT 2 / 11
  LVT 2 - Airspace Coordination Centres and BISON
  LVT 11 - RCAF - MCRUs
  Ground variant – has control panel on front
  200 W
Notes: TP: LVT 1/4/7
LVT 1 – J-Voice and TACAN; 1553 Bus or Ethernet (Plat D)
LVT 4 – J-Voice; no TACAN, 1553 Bus or Ethernet (Plat D)
LVT 7 – No Cdn platform, B2s in the US
TP: MIDS LVT 2 / 11
LVT 2 does not have built-in J-Voice card
LVT 11 includes built-in J-Voice card
NO TACAN in either
Designed for ground units, front control panel allows operator to power up, Stand-by, ON, and small display for terminal status display codes
TP: MIDS JTRS

## Slide 5
MIDS JTRS
MIDS JTRS
  CF188, CC130J, RCAF Ground Entry Stations, MRCUs, and CC150 MRTT
  Requires host platform to control;
  ground units requires Mini-Rack to control
  J-Voice and TACAN
  1W, 25W, 200W
  4 Channel Radio (1 for L16, 3 for software defined waveforms)
  Meets Frequency Remapping, CryptoMod requirements
  CMN-4 and CCR capable
Notes: TP: MIDS JTRS
Architecture ensures interoperability with legacy systems during transition to the Objective Force
Scalable, flexible, programmable SCA compliant architecture can readily support evolving requirements
Maintains current Link 16 and TACAN functionality; same footprint as MIDS LVT 1, uses same connector configuration and position (easy swap out in existing platforms)

## Slide 6: Small Tactical Terminal (STT)
Link 16
Link 16 Frequency Remapping
Crypto Modernization Ready
Power output: 63W
STT Block Upgrade will provide CMN2
CSE Approved for single Channel use in Canada by CP140, 8 ACCS, CANSOFCOM, and CA (future)
Simultaneous Two-Channel Comms for Air and Ground Interoperability
Notes: No TACAN; requires cooling rack
Mission Flexibility
» Dual-channel radio
» Link 16 and VHF/UHF waveforms
» Voice and wideband data capable
» Low size, weight, and power
» Lower acquisition costs
» Multi-mission, multi-user, and multi-waveform
» Meets current and future requirements
Situational Awareness
» Friendly force tracking
» Air and surface picture
» Interfaces with:
ViaSat Link 16 toolset
Air Defense Systems Integrator (ADSI®)
Joint Range Extension (JRE)
TRAX
BOSS
Gateway Manager
SPIDR
»Link 16 frequency remapping
» Crypto Modernization ready
» Modular design for easy growth – requires firmware and hardware upgrade for BU2 (CMN2 only)

## Slide 7: TacNet Tactical Radio (TTR)
Power Out
  90W, 50W, and 1W Modes
Size Weight and Power constrained platforms (SWaP-C) – in consideration by the TacHel community for Link 16 solution
Compatible with MIDS LVT and JTRS
Note: Not approved for use in Canada yet by CSE
Notes: No TACAN
Power Out + Crypto: 90W, 50W, and 1W Modes
• Host Dynamic Switching Between: Power Modes and Antenna Selection
• Host Power Not Required for Crypto Loading
Cooling Air Not Required
• Tactical Mounting in Unrestricted Positioning (Uses ARC-210 Mount)
• Host 1553 & Ethernet (Platform A & J)
• GPS: Through Host or Direct Connect

## Slide 8: Battlefield Awareness and Targeting System (BATS)
BATS-D (AN/PRC-161)
  radio can be used vest-worn, handheld, or mounted
  full Link 16 network access to ground forces
  Ideal for Joint Terminal Attack Controllers (JTACs), Forward Air Controllers (FACs), and Tactical Air Control Party (TACP) specialists
  J-Voice capable
  8 W
Modernization:
  CrytpoMod compliant
  Enhanced Throughput
  Frequency Remapping
Notes: No TACAN
J-Voice and Platform-J data capable
Voice PTT Key and mic/speaker
»»Link 16 enhanced throughput
»»Extremely low size, weight, and power
»»Link 16 frequency remapping
GROWTH CAPABILITIES
»»Concurrent multi-net
»»Link 16 precision navigation
»»Enhanced anti-jam

## Slide 9
MIDS on Ship (MOS)

## Slide 10: Simple Key Loader
SKL version 12 software update is required to load MIDS JTRS terminals

## Slide 11
Confirmation Questions
Floating Flip Chart Exercise

## Slide 12
QUESTIONS?