## Slide 1
Describe Tactical Data Link
Gateways
EO 001.07
Notes: This lesson plan needs to be cleaned up and extraneous stuff removed
Prior to commencing instruction the instructor should:
1) Introduce himself
2) Have each student introduce himself to the class detaining the platform and level of JTIDS expedience.
The instructor should motivate the students towards the learning by explaining that a the level of detail presented will allow all students (regardless of their experience level) to learn.
Stress the reason for the Joint class is to insure that interoperability is achieved by providing a baseline of knowledge about terms, and procedures. Stress that platform unique procedure and terminology is detrimental to Joint, Combined and Allied operations.

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Learning Objectives
Define TDL Gateways
Identify TDL Routers
Identify TDL Retransmitters
Identify TDL Data Forwarders
Recognize TDL Gateways Currently in Use

## Slide 4: Gateways
Gateways
  Interface between two systems that use different protocols or mediums
  They require accepted procedures for interfacing between the connected systems or networks
Notes: There are several ways that gateways transfer information
- From RF to non-RF links
- From one standard to another standard (M-Series to J-Series)
- From tactical level to operational level (Real time to non-real time)

## Slide 5: Gateways
There are two types of gateways:
  Data forwarders
    - Between two or more TDLs, or
    - Between a TDL and a non-TDL system
  Routers and re-transmitter
Router
(J to J)
JREAP
MIL-STD-3011
Link 16
MIL-STD-6016
Forwarder
(J to M)
MIL-STD-6020
Router
(TDL-non TDL)
Link 11
MIL-STD-6011
VMF
MIL-STD-6017
GCCS
Notes: The picture shows many different protocols and standards freely communicating in one architecture. Gateways are required to make this happen.
This allows flexibility in bringing in many different units with different capabilities and still operate with a common data set.

## Slide 6: Gateway Example
Pilot Interface
JTIDS
Network
C2 System
E-3 Initiates Track
Link 16
Terminal
SADL
Radio
SADL
Radio
Link 16
Terminal
Gateway
H
Link 16
Hostile Air Track
SADL Platform
Link 16 Platform
SADL Net
J-Series Message
J-Series Message
K-Series Message
Forwarding Occurs
Notes: In this case, the air track (the green plane) is detected by the E-3, and a Hostile J3.2 track is created. The J3.2 is sent over Link 16 to a Ground Station equipped with a Link 16 terminal and a SADL Radio. The Ground Station also has a Gateway between the two radios, and is capable of Forwarding J-Series to K-Series. The K-Series message is generated from the J3.2 and sent over the SADL radio to the SADL platform. The pilot sees the Hostile Air Track.
The SADL platform is not capable of Link 16 or J-Series messages, and the E-3 is not capable of SADL or K-Series messages. Using the Gateway, both units can effectively communicate with each other. That is the purpose of Gateways.

## Slide 7: Routers and Re-Transmitters
Ground Station
Routers move similar data across different mediums
  Link 11A -> Link 11B is an example, as it remains M-Series
  Link 16 -> JREAP is another example, as it remains J-Series
Retransmitters move similar data across similar mediums
  Bridging two Link 16 RF networks using two Link 16 terminals is an example
E-3 Sentry
CF-18
Link 16
Terminal 1
Retransmitter
Link 16
Terminal 2
Notes: Routers and Re-transmitters are one kind of Gateway.
Routers retain the same data, but use different mediums, think Link 16 RF and JREAP. All the Router is doing is taking the same information, but changing what medium it's one. JREAP B to JREAP C would also count. The medium is changing from Serial to TCP/IP.
Retransmitters are the most basic kind of Gateway, only able to share data across a similar medium. In the example, the retransmitter is hosting two Link 16 networks seperated by geograhy or crypto. Units in each Link 16 network can communicate with each other by sending J-Series messages through the retransmitter.

## Slide 8: Data Forwarders
Data Forwarders change information from one standard into another
  J-Series to M-Series
  J-Series to K-Series
  FJ-Series to J-Series
M-Series
J-Series
Forwarder
Notes: Data Forwarders are the most capable gateway, allowing conversion of Data and Medium. Using Forwarders is how messages are converted from one standard to another.

## Slide 9: Gateways Currently in Use in the CAF

## Slide 10: Joint Range Extension (JRE)
Router and Forwarder
Made by SAIC (formerly Engility)
JREs are often custom orders
  Cannot assume they all have the same features
  Version numbers are important
Hosts Link 16 Terminals
Hosts SADL Radios
JREAP A, B, and C
JRE DLT (Data Link Translator) is an optional forwarder for M-Series
Currently in use with RCAF
  CADS
  1 CAD

## Slide 11: Joint Air Defense System Integrator (ADSI)
Router and Forwarder
Made by Ultra Electronics
ADSIs are modular
  Customers can purchase additional capabilities (Link 11A/B, etc)
Hosts Link 16 Terminals
Hosts SADL Radios
JREAP A, B, and C
Addon available for Link 11
Capable of non-TDL protocols including Radar feeds and GCCS
Can be used as a C2 System
Orginally 3 computers (see picture)
  Now employed with virtual machines on a laptop
Currently in use with CA and RCAF
  4th Regt (GS)
  Mobile Radar Squadrons (12 & 42 Radar)

## Slide 12: Gateway Manager
Router and Forwarder
Made by Northrup Gromman
For NORAD, the Gateway Manager is the data link computer for the Battle Control System (BCS) operated at CADS
Can host a Link 16 terminal (but doesn't)
Has an NTDS Card for Link 11
Capable of JREAP A, B, and C
Has no map or plotter
Currently in use in the RCAF and RCN
  CADS (21 AC&W Sqn)
  RCN (MSLC East and West)
Notes: Sentry is the C2 Host system used in the NORAD Battle Control System

## Slide 13: CRC Systems Integrator
Router and Forwarder
Made by NATO
Full C2 System suite, with data link capabilities
Modular system, can use full CSI Server or individual Java Applications
Can host a Link 16 Terminal
Uses JREAP B, and C
Capable of Link 11
Has advanced options including
  Link 16 Simulator
  MIDS terminal emulator
  Radar combiner
Currently in use pan CAF
  RCAF in 1 CAD and 51 AC&W Sqn
  CA in 4th Regt (GS)
  RCN aboard Halifax Class and MLSC East and West
Notes: CSI presence in the CAF is likely to grow. Also, there are rapid version updates that increase capabilities and user-friendliness.

## Slide 14: Summary
Define TDL Gateways
Identify TDL Routers
Identify TDL Retransmitters
Identify TDL Data Forwarders
Recognize TDL Gateways Currently in Use

## Slide 15
QUESTIONS?