## Slide 1
EO 001.06
Identify VMF Message Types

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
K Series Message
K Series Functional Area Messages
Variable Message Format Structure

## Slide 4
References
MILSTD 6017A
STANAG 5519
WWW.
MIL-STD-188-220
Understanding Voice and Data Link Networking

## Slide 5: K Series Message Definition
K-series binary variable message format is medium independent. The VMF message format used is a bit-oriented digital information standard incorporating a variable message length and providing a common means of exchanging data among combat units at different organizational levels.
Notes: The types of K series message support the different types of ground forces operations and activities.
Currently most CA participants use VMF for text messages and friendly force positional data.

## Slide 6: K Series Message Types
K00 - NETWORK CONTROL
K01 - GENERAL INFORMATION EXCHANGE
K02 - FIRE SUPPORT OPERATIONS
K03 - AIR OPERATIONS
K04 - INTELLIGENCE OPERATIONS
K05 - LAND COMBAT OPERATIONS
K06 - MARITIME OPERATIONS
K07 - COMBAT SERVICE SUPPORT
K08 - SPECIAL OPERATIONS
K09 - JOINT TASK FORCE (JTF) OPERATIONS CONTROL
K10 - AIR DEFENSE/AIR SPACE CONTROL
Notes: Message types = K series Functional areas
Each functional area have subcategories of information (i.e. fir support operations – fire mission)
Have the students match the message types with definitions on the board. ( K04 with the definition for example)

## Slide 7: K Series Message Types
K00 - NETWORK CONTROL
Network Control messages support the establishment and maintenance of the digital data links, or "networks", that use the VMF messages.
The term "network" may be interpreted as a collection of connected systems (i.e., single channel radios, satellites, personal communication systems (PCSs)), switching systems, local or wide area networks (LANs or WANs), and tactical intranets used singularly or in a variety of combinations.

## Slide 8: K Series Message Types
K01 – GENERAL INFORMATION EXCHANGE
General Information Exchange messages pertain to information that is common to more than one of the VMF functional areas or does not fit into any of the joint functional areas. Common use messages and the free text message are included in this functional area.

## Slide 9: K Series Message Types
K02 – FIRE SUPPORT OPERATIONS
Fire support operations include direct and indirect surface-to-surface artillery (SSA) and mortar fire, naval surface fire support (NSFS), close air support (CAS), and assault support. The functions of fire support are technical fire control, tactical fire control, fire support coordination, fire planning, target intelligence, survey data, meteorological data, support and sustainment, and fire unit status.

## Slide 10: K Series Message Types
K03 – AIR OPERATIONS
The messages in the air operations VMF functional area are those messages that support the tactical functions of offensive counter air operations, close air support, air interdiction, air reconnaissance and surveillance, electronic warfare, airlift, aerial refueling, combat search and rescue, aeromedical evacuation, and weather services. The functional area also includes the apportionment, allocation, and tasking of air assets; the control of enroute air traffic; and the coordination, control, and assessment of air operations.

## Slide 11: K Series Message Types
K04 – INTELLIGENCE OPERATIONS
The messages in the intelligence operations VMF functional area support the planning and direction of intelligence operations, collection, processing, production, integration, analysis, interpretation, and dissemination of information regarding the status, capabilities, and intentions of enemy forces and their supporting facilities. Weather and geographical features are also included in the messages used to support intelligence operations.

## Slide 12: K Series Message Types
K05 – LAND COMBAT OPERATIONS
The messages included in the land combat operations VMF functional area support the coordination and control of land combat operations, and planning and control tactical employment of ground units and Army aviation units. The functional area also includes maneuver, communications support, deception, electronic warfare, land minefield/mine laying, helicopter air assault, nuclear, biological, and chemical (NBC) warfare, and civil affairs.

## Slide 13: K Series Message Types
K06 – MARITIME OPERATIONS
Messages in the maritime operations VMF functional area support such activities as amphibious operations, convoy operations, naval control and protection of shipping, maritime interdiction, anti-surface warfare, mine warfare, coastal, and riverine operations, electronic warfare, combat search and rescue, and antisubmarine warfare.

## Slide 14: K Series Message Types
K07 – MARITIME OPERATIONS
Messages in the combat service support VMF functional area support the movement and maintenance of forces including the acquisition, movement, storage, distribution, maintenance, evacuation, and disposition of supplies and material. Combat service support also includes the acquisition, movement, evacuation, hospitalization, and status of personnel; acquisition or construction, maintenance, operation, and disposition of facilities; and the acquisition and furnishing of services. The functional area covers logistics support, health services, personnel services, non-combat engineering, and explosive ordinance disposal.

## Slide 15: K Series Message Types
K08 – SOF OPERATIONS
Messages to support the special operations VMF functional area pertain to operations conducted by specially trained, equipped, and organized DoD forces against strategic or tactical targets in pursuit of national military, political, economic, or psychological objectives. The functional area includes foreign internal defense and development, unconventional warfare, direct action, counter terrorism, psychological operations, and civil affairs.

## Slide 16: K Series Message Types
K09 – SOF OPERATIONS
Messages in the joint task force operations control VMF functional area support the coordination and control of all forces assigned and attached to and in a joint force.

## Slide 17: K Series Message Types
K10 – AIR DEFENCE/AIRSPACE COORD OPERATIONS
Messages in the air defense/airspace control VMF functional area support all defensive measures designed to destroy attacking aircraft, missiles, and ballistic missiles or to nullify or reduce the effectiveness of such attack. These measures include air defense use of aircraft, missiles, air defense artillery, non-air defense weapons in an active air defense role, and electronic countermeasures (ECM) and electronic counter-counter measures (ECCM). The functional area also includes passive air defense such as the use of cover, concealment, dispersion, and protective construction. Airspace control is the provision in a combat zone of services to increase operational effectiveness of ground, surface, and air operations by promoting the safe, efficient, and flexible use of airspace.

## Slide 18: K Series Message Example
K02.1
K = Type of K Series Message
02 = Fire Support Operations
.1 = Check Fire Message
K Series Messages have a defined information format, the length of each message is not. Only required information is sent, not packeted.

## Slide 19: VMF Message Example
Notes: The message description contains the message title, purpose, index numbers, DFI/DUI numbers, data field names, categories, groupings, recurrences, and field lengths.
Message number – type of K series message (KO.1 for example)
Title – name of message
Purpose – entered by sender
Index number – provides a line number displaying the numerical position of each field within the message.
DFI/DUI - provides numerical reference of the message in the VMF message dictionary.
Bits – length of DUI in binary digits.
CAT – types of fields in the message.
Group – grouped information in the message.
Repeat codes – number of repeatable fiels in the message.
Resolution coding etc – descriptive notes or titles of fields.

## Slide 20
Confirmation Questions
What are K Series messages?
What are the different types of K Series messages?
Are K Series Messages Fixed Format?

## Slide 21
QUESTIONS?