## Slide 1
EO 001.01
Describe Radiation Characteristics​ Link 11​
Notes: 7/01/10 Format Change

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Objectives
Identify HF and UHF Frequency Bands and Characteristics
Identify Link 11 Waveforms (SLEW and CLEW)
Identify Antenna Types and Radiation Patterns
Identify Ionospheric and Atmospheric Impacts on HF and UHF Radiation
Identify Link 11 Roles, Operating Modes and Duties

## Slide 4: High Frequency
3-30 MHz
Long range
Not LOS critical
Noisy
Higher Transmitter Power
Radiation Safety Concerns
BLOS
Notes: HF High Frequency RF
is the ITU (International Telecommunication Union)-designated range of radio frequency electromagnetic waves (radio waves) between 3 and 30 MHz It is capable of Long range and is beyond line of sight. It can be noisy to listen to, especially man-made interference from electronic devices, tends to have a great effect on the HF bands
HF Transmissions can reradiate on cables and guywires making them dangerous to handle in an active RF environment. The Navy has strict rules on when HF can be radiated and with how much power. This is true both ashore and at sea. Aircraft refuelling will often cease HF transmissions due to these safety issues.

## Slide 5: Ultra High Frequency
LOS
300 MHz – 3 GHz
Short Range
LOS critical
Lower Transmitter Power
Fewer Safety Limitations
Low Noise
Notes: designates the ITU radio frequency range of electromagnetic waves between 300 MHz and 3 GHz (3,000 MHz) It has a shorter range than HF, requires line of sight but offers a very clean signal. Tall buildings can interfere as well but it is capable of going through interior walls for indoor use.
UHF does not have the same re-radiation issues as HF, as well as is operated with significantly less power (200 W vs 1000 W). This means that UHF can be radiated without waivers or restrictions, including aircraft refuelling.

## Slide 6: Wave Forms
Waveforms are how information is encoded into radio waves.
MIL-STD 6011 & STANAG 5511 determine how this is done for Link 11
There are 2 Waveforms for Link 11:
  Conventional Link Eleven Waveform (CLEW)
  Single-Tone Link Eleven Waveform (SLEW)
Notes: CLEW and SLEW are two options for wave forms. Default is SLEW
SLEW and CLEW are not compatible waveforms
SLEW, among other
enhancements, provides increased propagation and a more powerful Error
Detection and Correction (EDAC) algorithm. While the option exists to operate
in either CLEW or SLEW, all participants in a given Link 11 net must select the
same waveform to achieve connectivity between units. SLEW is used by NAVY only

## Slide 7: CLEW
CLEW is the original Link 11 Waveform
16 frequency tones (like a touch-tone phone) are generated and combined to make the data signal.
Each tone is capable of carrying digital information.
In noisy RF environments, certain tones may be difficult to receive, reducing reliability.
Notes: This topic gets complicated fast.
The tones are modulated using QPSK (Quadrature Phase Shift Key), which offsets the phase of the fixed frequency in four increments (45, 135, 225 and 315 degrees)
The first tone is used for doppler correction (measuring the frequency shift due to a relative motion), and is combined with the last tone to create the preamble signal.
Tones 2-15 are used for encoding digital data.

## Slide 8: SLEW
CLEW is an alternate Link 11 Waveform
Not all Data Terminal Sets are capable of SLEW
The DTS encodes all data into one tone
The tone selected is optimized for a noisy RF environment, and it more tolerant of RF noise (better Signal to Noise ratios are possible)
Gives more range for the same power
Notes: This topic gets complicated fast, but even worse
A single tone is encoded with an eight-phase modulation process. More details are available in MIL-STD 6011/STANAG 5511

## Slide 9: Antenna Types
There are two types of antennae for RF systems
  Omni-directional
  Directional
When RF energy is generated, it creates an RF lobe
The RF lobe is the 3-dimensional area in which RF energy is present
Omni-directional is like a lightbulb – energy is equally distributed in a sphere
Directional is like a flashlight – energy is cast into one direction
Notes: The L11 OPTASK LINK portion is identified by the LNKXI segment.
The OPTASK LINK for L11 will contain
LNKXI
DLRPGRID
PERIOD
LSYSDATA
CRYPDAT
DALFREQ
LPUDATA

## Slide 10
Antenna Type Radiation Patterns
Antennae radiate all power delivered by the radio, this determines the size of the lobe.
The lobe is the 3-dimensional space that Radio Energy is present in
Careful shaping of the lobe can extend radio signal
Directional Antennae are designed to do exactly that

## Slide 11
Balloon Thought Experiment
Imagine a balloon filled with air.
From the center of the balloon, how far can you measure to the surface of the balloon?
Squeeze the balloon in the center.
From the center of the balloon, can you measure farther?
Have you added any extra air into the balloon?
Are there points of the surface of the balloon where you measure closer to the center?
Notes: Get actual balloons for this?

## Slide 12
Balloon Thought Experiment
The volume of the balloon is the lobe
It represents the radio energy transmitted by the antenna
The surface of the balloon is the farthest range of the radio signal
In a directional antenna, the range is farther in one axis, but shorter in the other axis
Notes: Get actual balloons for this?

## Slide 13
Examples of Omni-Directional Antennae
Notes: Get actual balloons for this?

## Slide 14
Examples of Directional Antennae

## Slide 15
Atmospheric Impacts on
Radio Frequencies
RF noise is comprised of natural phenomenon (lightning, static, solar energy) and man-made interference
    UHF is less impacted by noise
    HF is greatly impacted by noise
HF is also impacted by ionospheric noise, due to how HF can radiate beyond line of sight.

## Slide 16
HF Propagation Characteristics
HF waves have 3 general methods of propagation:
  Sky Waves
  Ground Waves
  Direct Waves

## Slide 17
HF Direct Waves
Direct Waves are the simplest of the 3 types
It is when 2 units are within Line of Sight of each other, and the radio waves travel directly to each other.

## Slide 18
HF Ground Waves
Ground Waves travel across the ground hugging the surface of the earth.
Terrian absorbs RF energy, including vegetation, elevation features (hills and mountains) and ocean waves
Atmospheric and Terrain interference will also depend of frequency selection

## Slide 19
HF Sky Waves
Sky Waves are ricocheted off the ionosphere
Where in the ionosphere the wave reflects will change the angle of reflection.
Wave reflection location will depend on output power, frequency selection and ionospheric space weather

## Slide 20
HF Sky Waves
Ionospheric activity can vary by:
  Time of day
  Solar Activity
Operators primarily use frequency selection as a control to establish connectivity
Ionospheric conditions change over time, making the correct frequency selection also change over time
  Sun up Frequency up, Sun down frequency down

## Slide 21
HF Sky Waves

## Slide 22
HF Frequency Prediction Resources
The Ionospheric Communications Enhanced Profile Analysis and Circuit Prediction Program (ICEPAC)
  A computer program designed to predict point to point and area frequency selection derived from scientific observations.
  It factors time of year, latitude, longitude, solar activity, and time of day to predict the correct frequency to use
  The codebase and data are considered outdated
Voice of America Coverage Analysis Program
  https://www.voacap.com
  Updated ICEPAC data with more current information
  Retained old codebase, so there is only so much possible
Proppy
  https://soundbytes.asia/proppy
  Updated ICEPAC codebase to make it compatible with more software plugins
  Updated data

## Slide 23: Link 11 Roles
Net Control Station - the NCS is the controlling unit for Link 11. They are responsible for polling picket units and controlling the net cycle
Picket - the picket is a station polled by the NCS to begin transmitting.
Radio Silence - a station set to radio silence will receive all information on a net, however will not respond when polled by the NCS
Notes: The L11 OPTASK LINK portion is identified by the LNKXI segment.
The OPTASK LINK for L11 will contain
LNKXI
DLRPGRID
PERIOD
LSYSDATA
CRYPDAT
DALFREQ
LPUDATA

## Slide 24: Link 11 Operating Modes
Net Synchronization - net sync is designed to synchronize all participants on a net, and to verify RF communications. The Net Sync signal carries no data.
Net Test - net test sends test messages over the net to allow all units to ensure that they are receiving data correctly.
Roll Call - normal mode of Link 11 operation. A unit called by NCS will broadcast data then return control back to NCS.
Broadcast - a unit will broadcast its information once (short broadcast), or continuously (long broadcast) regardless of NCS direction
Notes: The L11 OPTASK LINK portion is identified by the LNKXI segment.
The OPTASK LINK for L11 will contain
LNKXI
DLRPGRID
PERIOD
LSYSDATA
CRYPDAT
DALFREQ
LPUDATA

## Slide 25: Link 11 Duties
Link 11 Duties are assigned by the JICO, and recorded in the OPTASKLINK
Duties include:
  NCS
  Standby NCS
  Gridlock Unit
  Forwarding Units
Duties discussed in more detail in EO 003.0x
Standby Duties annotated with an "S"
Duty Code | Link Duty
88 | DLRP Transmit Unit
88S | DLRP Transmit Unit Secondary
83 | Grid Reference Unit
83S | Grid Reference Unit Standby
804 | Interface Control Officer
85 | Link 11 Broadcast Unit
84 | Link 11 Net Control Station
89 | Link 11 to Link 11 Gateway
823 | Link 16 Data Forwarding Unit to Link 11A (FJUA)
Notes: HF High Frequency RF
is the ITU (International Telecommunication Union)-designated range of radio frequency electromagnetic waves (radio waves) between 3 and 30 MHz It is capable of Long range and is beyond line of sight. It can be noisy to listen to, especially man-made interference from electronic devices, tends to have a great effect on the HF bands

## Slide 26: Summary
Identify HF and UHF Frequency Bands and Characteristics
Identify Link 11 Waveforms (SLEW and CLEW)
Identify Antenna Types and Radiation Patterns
Identify Ionospheric and Atmospheric Impacts on HF and UHF Radiation
Identify Link 11 Roles, Operating Modes, and Duties

## Slide 27: Confirmation Questions
Between SLEW and CLEW, which is more tolerant of RF noise?
  SLEW
At very long ranges, which HF Wave Propagation is most likely to be successful?
  Sky Wave
During an exercise, 2 static ground stations attempt to communicate using HF. Should they employ directional or omni-directional antennas?
  Directional

## Slide 28
QUESTIONS?