## Slide 1
EO 001.02
Describing Link 16 Waveforms and Principals

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
Review Legacy Link 16 principles to include:
  Packing Structures
  TDMA
  Dedicated Access, Contention Access, Time Slot Reallocation
  Frequency Hopping
  Stacked Nets and Multi-Net Operations

## Slide 4
OVERVIEW
Explain Modernization Link 16 principles to include:
  Concurrent Multi-Netting
  Concurrent Contention Receive
  Enhanced Throughput
  Frequency Remapping

## Slide 5
Table Topics Exercise
Topics from the reading assignment
Notes: TP: Using the topics from the reading review material, each trainee will pick a topic from the bag and explain the principles on a flip-chart; these are all introduced in detail on TDL 100 but important to stress for comprehension of the modernization principles.
Practice building an Essence for each of the topics to introduce the end of lesson confirmation activity.
Example:
TDMA – separates transmissions so they are not transmitting at the same time; each user is assigned time to transmit in timeslots;
Frame - 12 seconds consisting of 1536 timeslots,
Timeslot - each timeslot is 7.8124 msec;
Pulse stream – 72, 258, or 444 pulses; pulses are spaced 13 microseconds (μsec); 6.4 μsec transmitting; 6.6 μsec changing frequency;
Frequency Hopping – pseudo random use of 51 center frequencies determined by the crytpo
Dedicated Access – All receive dedicated transmissions as only one unit/platform is transmitting
Stacked Nets – Only receive tx if you are on the same Net; operator selectable
Multi-Netting – other information tx on a different net you won’t receive; built in the network
Contention Pools – sacrifice distance for performance of close range;
Spectral Contention (slot Reuse) – receiver only receives the closest transmitter

## Slide 6: Legacy Network capacity tools
Networks use different dynamics to increase capacity
  Stacked net
  Multi net
  Time slot reuse
Operator selectable 127 nets (0-126)
NPGs 9, 12, 13, 19, 20
Mutually exclusive groups performing
different functions using the same timeslots;
(but different hopping pattern.)
Network managers/JICOs must ensure that separate nets are assigned to each community. Net 127 = “no net assignment”
Feature designed into network;
not operator selectable
Notes: Stacked nets
All Ships and C2 participants are assigned timeslots in Dedicated Slot Reuse (DSR) on net 127 for Control Uplink, which means that all participants will use the same timeslots for Control Uplink (NPG 9). Note that net 127 indicates “no net assignment” and is an operator selectable net. Network managers/JICOs must ensure that separate nets are assigned to each community. If an OTL states 127, coordination with participants or JICO for net assignment is required.
Control Backlink is designed as a stacked net. Fighter participants are assigned contention timeslots on Net 127 for Control Backlink (NPG 9). Note that net 127 indicates “no net assignment” and is an operator selectable net. Network managers/JICOs must ensure that separate nets are assigned to each community.
Voice – (NPG 12/13) can be defined within the OTL based on “groups”

## Slide 7: CMN-4 and CCR
Concurrent Multi-Netting-4 (CMN-4) consists of two capabilities:
      Concurrent Multi-Netting (CMN)
        Receive up to 4 message packages in:
          Same Time Slot
          On up to 4 different nets*
      Concurrent Contention Receive (CCR)
        Receive up to 4 message packages in:
          Same Time Slot
          On only 1 net
This is achieved by increasing the number of receivers from one to (up to) four.
*Technically 4 different Psuedo-random sequence (hopping pattern).
Notes: Hopping pattern is defined by Net Number, TRANSEC CVLL, and/or Crypto mode.
Concurrent Contention Receive (CCR):
    Multiple message receptions with the same pseudorandom sequence
Concurrent Multi-Netting (CMN):
    Multiple message receptions with different pseudorandom sequences

## Slide 8: How it works today
4 different nets are operating on the same timeslots…
Net 1
Net 2
Net 3
Net 4
So the Fighter is only able to receive on one of the nets.
The net number is different, so the hopping pattern is different…
Fighter
Notes: TP: This picture is describing Multi-Netting: Mutually exclusive groups performing different functions using the same timeslots; (but different hopping pattern.) It is a feature designed into network; not operator selectable.

## Slide 9: How it works with CMN
4 different nets are operating on the same timeslots…
Net 1
Net 2
Net 3
Net 4
But the CMN-4 Fighter is able to receive on all 4 nets at the same time
The net number is different, so the hopping pattern is different…
CMN-4 Fighter
Notes: TP: Even with these advanced capabilities, there are still Limitations:
    Can only transmit on one net (Pseudo-random sequence)
    Cannot receive while transmitting (some data loss)

## Slide 10
New capabilities enabled by CCR
  Increases capacity by reducing size of contention pools;
  Allows for more functionality in a single load file
  Improves probability of reception
  Enables a fighter participant to receive from multiple wingmen simultaneously in the same time slot (significantly improving SA)
Concurrent Contention Receive

## Slide 11: How Contention works today
Single Net.
These 4 aircraft are in contention access mode…
They happen to transmit in the same slot
This Fighter only decodes the transmission that reaches it first
The net number is the same, so the hopping pattern is same…
Fighter
970
Notes: TP: This picture is describing Contention Access: although they are using the same net number, the fighter only receives the transmission from the closets tranmitter.

## Slide 12: How it works with CCR
Single Net.
These 4 aircraft are in contention access mode…
They happen to transmit in the same slot
But the CMN-4 Fighter can receive all 4 transmissions!
The net number is the same, so the hopping pattern is same…
CMN-4 Fighter
Notes: TP: With CCR, the fighter is now able to receive all of the transmission.

## Slide 13: Enhanced Throughput
Link 16 Enhanced Throughput (LET)
    Increases the capacity of each time slot
The number of J-series words incrementally increases from 12 (using current Packed 4 limit) up to 123 using the highest LET rate

## Slide 14: How Packing works today
Message Structure | Data Words | Bits | Tracks
Std Double Pulse | 3 Data Words | 225 bits of data | 1 Track
Packed 2 Single Pulse | 6 Data Words | 450 bits of data | 2 Tracks
Packed 2 Double Pulse | 6 Data Words | 450 bits of data (same data twice) | 2 Tracks
Packed 4 Single Pulse | 12 Data words | 900 bits of data | 4 Tracks
Notes: TP: Double Pulse -

## Slide 15: Number of tracks for LET Packing Limits
The following table is based on a standard 3-word J-series message
Message Structure | Data Words | Bits | Tracks
LET Mode 0 | 40 Data Words | 2944 bits of data | 13 Tracks
LET Mode 1 | 61 Data Words | 4416 bits of data | 20 Tracks
LET Mode 2 | 93 Data Words | 6752 bits of data | 31 Tracks
LET Mode 3 | 108 Data Words | 7800 bits of data | 36 Tracks
LET Mode 4 | 123 Data Words | 8800 bits of data | 41 Tracks
All users must have LET in order to participate in that data exchange
Notes: Reduces Anti-Jam – Denied Axis environment
  MIDS JTRS working to solve
Reduces Message Error Rates (MER)
Reduces RF LOS Range
  Lab testing showing this may not be as bad as advertised

## Slide 16: Frequency Remapping/CryptoMod
Due to imposed National Security Agency (NSA) crypto modernization program standards and Federal Aviation Administration frequency remapping requirements, the current Link 16 hardware and software used across many platforms in the CAF must be replaced.
Compliance date : 1 Jan 2022
Notes: TP: Crypto Modernization is driving the requirement to replace the terminals we will look at in LO 001.02.04. – This has World-wide implications!
NOTE: Frequency Remapping is only being implemented in the United States but Canadian platforms may need to operate in a remapped AOR in support of NORAD.

## Slide 17: Frequency Remapping
Notes: TP: JTIDS/MIDS waveform systems will incorporate a remapping capability for up to 14 carrier frequencies (any 14 among the 51). This is needed because NSA has sold off portions of the lower band of Link 16 frequencies for future Systems.
Incumbent Systems:
TACAN / DME Interrogators and Beacons
SSR / Mode S Interrogators and Transponders
TCAS
1090 Extended Squitter ADS-B
Universal Access Transceiver
Link 16 JTIDS/MIDS
Non-ICAO ARNS system (RSBN)
Proposed New AM(R)S Systems:
LDACS 1
LDACS 2
UAS CNPC
Adjacent Band Systems
GSM
GNSS

## Slide 18: Frequency Remapping Example
14
JTIDS / MIDS
CARRIERS
TACAN / DME
CHANNELS
EVERY
1 MHz
ATCRBS
MODE S
IFF
TCAS
JTIDS / MIDS
FREQUENCIES
EVERY
3 MHz
5
JTIDS / MIDS
CARRIERS
32
JTIDS / MIDS
CARRIERS
1030
1090
1215
960
New
Aviation
System(s) ?
Unauthorized Frequencies
969 MHz
1008 MHz
(illustration shows the case where the lowest 14 frequencies are designated as unauthorized)
The unauthorized carrier will be remapped to an authorized frequency for the pulse transmission in accordance with a remapping algorithm* calculation performed in each Terminal
Remapping:
When an unauthorized carrier frequency gets selected for a MIDS pulse transmission:
* Algorithm defined in the DOD Regulation 4650.1-R1
Notes: TP: How it works Now - Link 16 uses 51 Frequencies to hop on in a pseudo-random hopping pattern.
Frequency Remapping is accomplished by an algorithm that causes the terminal apply the algorithm when one of the upto 14 frequencies in the lower band of 969 to 1008 would be selected to be transmitted on.
  The required remapped frequencies will be indicated in the frequency assignment.
  The remapped frequencies will be contained in the network initialization file.
  Modifications have been made to the JTIDS Network Design Aid (JNDA).
The number of frequencies to be remapped is handled via the IDL created by the Network Design Facility.

## Slide 19: How Crypto works now
Link 16 is structured to support multiple cryptonets using different TEKs (i.e., it can use more than one short title at a time)
Current terminals are capable of smoothly operating on four cryptonets simultaneously
Notes: TP: SDU locations are daily pairs allowing 4 different Cryptonets (CVLL 0/1) (CVLL 2/3) (CVLL 4/5) (CVLL 6/7)

## Slide 20: After Crypto Modernization (CM)
Operate on 32 Crytponets simultaneously
No maximum limit of platforms on any given crytponet
No worldwide TEK to avoid Global compromise
NSA will be generating brand new Keymat
Notes: TP: After Link 16 modernization, the Link 16 can be initialized to operate on up to 32 cryptonets simultaneously.
Although no maximum limit on the number of platforms that can be on any single cryptonet is prescribed for Link 16 TEK cryptonets, this number should be as small as operationally feasible.
To minimize the risk of global compromise, the same TEK (Transmission Encryption Key) short title must not be used worldwide.

## Slide 21: Target dates
Key Dates from Joint Requirements Oversight Council Memorandums (JROCMs):
  Link-16 Crypto Modernization (CM) – Operational Networks : 01 Jan 22 / Training Networks 1 Jan 25
  Link-16 Frequency Re-mapping (FR) - 1 Jan 25
  Link-11 - 01 Jan 25
Notes: TP: Nice to know – not tested.
1. All platforms to be MIDS J by 2022 or be considered “a disadvantaged user”
2. All L11 platforms must be replace with another system (probably Link 22) by end 2024
3. Link 22 training requirements – this course is expanding L22 into the TDL Series.

## Slide 22: What does this all mean?
Essence Exercise
Concurrent Contention Receive
Concurrent Multi-Netting
Enhanced Throughput
Frequency Remapping
Crypto Modernization
Notes: TP: Instructor facilitating the Essence Exercise on What does this all Mean? First in 32 words or less, describe in your own words the following terms, then cut in half to 16, then see if you can describe the key ‘essence’ of the term in 8 words.
Concurrent Contention Receive
Concurrent Multi-Netting
Enhanced Throughput
Frequency Remapping
Crypto Modernization

## Slide 23
QUESTIONS?