## Slide 1
Mitigate Data Loops
EO 001.07
Notes: This lesson plan needs to be cleaned up and extraneous stuff removed
Prior to commencing instruction the instructor should:
1) Introduce himself
2) Have each student introduce himself to the class detaining the platform and level of JTIDS expedience.
The instructor should motivate the students towards the learning by explaining that a the level of detail presented will allow all students (regardless of their experience level) to learn.
Stress the reason for the Joint class is to insure that interoperability is achieved by providing a baseline of knowledge about terms, and procedures. Stress that platform unique procedure and terminology is detrimental to Joint, Combined and Allied operations.

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Enabling Learning Objectives
Define Data Loops
Identify Data Loops
Correcting Data Loops

## Slide 4: Data Loop Definition
A Data Loop is:
  when a unit receives its own data from another unit
  or when a unit receives the same information from two different sources
Data Link Gateways offer flexibility and connectivity to data link architectures
Units can participate in an operation without the requirement to be in the RF
The use of Data Link Gateways can cause data to "loop" back to its originator
The exact effect will depend on the Data Link Gateway, and how its coded
Elimination of Data Looping is a goal of all Data Link Operators
Notes: Data Loops have a long history of being poorly defined. Ask the trainees if they've heard of data loops being defined in any other way.
Also, ask if they have ever seen data loops in operations, and what impact it had on them.

## Slide 5: Own Unit Data Loop Example
TIC 3 AIR Site
CF-18
42 Radar MIDS
CADS
1. CF-18 Generates J2.2 PPLI
2. J2.2 PPLI is transmitted through RF Link 16 to the TIC 3 AIR MIDS JTRS
3. CADS converts the J2.2 to J2.0 and sends it to 42 Radar
3. 42 Radar receives a J2.2 from the CF-18 and a J2.0 from CADS, which is sent into the RF Link 16 network
4. The CF-18 recieves a J2.0 message with its own JU from 42 Radar
Notes: There are multiple types of loops here. The CF-18 being received twice at 42 radar (from CADS and the C-18) is also a kind of loop.
The Loop can be broken by CADS not forwarding the TIC3AIR picture to 42 Radar.

## Slide 6: 2 Source Data Loop Example
Sentry C2 Host
CADS Gateway Manager 1
CADS Gateway Manager 2
EADS Gateway
WADS Gateway
1. E-3 Generates a J2.2 PPLI
2. EADS sends the PPLI to CADS GWM 1 and WADS
3. WADS sends the PPLI to CADS GWM 2
4. GWM 2 sends PPLI to Sentry
4. GWM 1 sends PPLI to Sentry
5. Sentry receives two copies of the same PPLI
Notes: In this case, Sentry is receiving 2 copies of the same PPLI and associated air picture.
What happens when EADS has a filter in, but WADS doesn't?
In Sentry's case, it takes the first JU and Air Picture it gets, and discards all of the data from the other source.

## Slide 7: Concurrent Interface Units
A Concurrent Interface Unit (CIU) is a unit that operates on multiple types of Link without forwarding.
  It can operate on Link 11 and Link 16, but cannot forward
  Must use a common IU and trackblock between the two links
  A common source of data looping
Most common example is the US E-3 Sentry
CIU considerations also apply to units operating two Links, but configured not to forward
Notes: Concurrent Interface Units are the star of the show for the TDL 300 course. They are a massive planning issue.

## Slide 8: Concurrent Interface Unit Example
HMCS SHIP CMS
1. E-3 Generates a J2.2 PPLI JU 00020
HMCS MIDS
HMCS Link 11
No Forwarding
2. Ship receives J2.2 JU 00020
1. E-3 Generates a M.1/M.81 Position Message PU 20
2. Ship receives M.x PU 20
3. Ship receives J2.2 JU 00020 and M.1/M.81 PU 20
Notes: If the ship is configured to forward between Link 16 and Link 11, then they would send the PU 20 back to the E-3. That's another Data Loop.
The really complicated part comes in when the operation or exercise requires other platforms to be forwarded, like a CP-140 or a Cyclone. The ship can't just turn off forwarding to fix the issue. Careful routing and filtering needs to be in place to correct Data Loops.

## Slide 9: Data Loop Detection
Most Gateways have an automated means of Data Loop Detection
  Usually flagged as an error or warning with more details
Best Data Loop detection is on paper, from an architecture diagram
Notes: With the wide veriety of available C2 Systems and Gateways, it's impossible to have a concrete answer to what data looping looks like. The most reliable indicator is from the equipment itself.
Data loops from an operating system can be very difficult to see, as from the individual routing tables it may not be obvious. Best practice is to eliminate data loops in the planning process and stick to the plan.

## Slide 10: Consequences of Data Looping
Lost Data
  Tracks, Reference Points, Pointers
  Inability to send/receive Directed Messages
    - Air Control Commands
    - J28.2s
Inefficient on low bandwidth Links
  Sends the same data twice, therefore doubles data requirements
  Affects low bandwidth mediums, such as JREAP A & B
  Can cause message buffering, increasing timelate
Notes: Some systems are barely affected by data loops – the internal detection and correction system will fix most of the issues.
Systems like the JRE have a "smart forwarding" feature that will reduce data looping that can be used
Troubleshooting a data loop is difficult, because they manifest in different ways in different systems, and in a properly designed architecture, data loops only occur when changes are made. If they are caused by a unit that enters and exits the link, it will look like an intermittant fault.
Bandwidth is a measure of how much information can be sent over time. Message buffering is when a system has to hold information until there is enough bandwidth to send it out.

## Slide 11: Correcting Data Looping
Coordinate with the ICO and other units
Review the Link Architecture
  A visual map will be the basis of understanding how data flows
Verify your systems are configured in accordance with SOPs
  Usually data loops are introduced with architecture changes
Isolate units using routing/filtering until the problem unit is identified
  Use a systematic approach
Notes: There is an infinite variety in the ways that data loops can be presented. This also applies to how to correct them. There isn't a single way to approach the problem.

## Slide 12: Summary
Define Data Loops
Identify Data Loops
Correcting Data Loops

## Slide 13: Confirmation Questions
Define Data Loops in two different ways.
  When a unit receives its own information
  When a unit receives information from another unit in more than one way
What type of unit is a common source of data looping issues?
  Concurrent Interface Units
What are 2 consequences of Data Looping
  Data Loss
  Uses up more bandwidth

## Slide 14
QUESTIONS?