## Slide 1
EO 001.02
Define Link 16 Deconfliction Process

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
Deconfliction Process to include:
  Clearance to Radiate Authority
  Clearance to Operate Authority
  Time Slot Duty Factor Guidance
  Deconfliction Server requirements

## Slide 4
Clearance To Radiate (CTR)
In Canada:
  DND-A-100-2014, Airspace Control Operational Arrangement Use of Link 16 in Canada
  DAOD 6002-4
  DND Frequency Spectrum Management (DFSM)
  Industry Canada
  Terminal’s Licence is your CTR
Notes: TP: DFSM - acting as the technical authority for RF spectrum management for the DND and the CAF
- Requests for Spectrum supportability (DNDP35 Part 5-5)
- Requests for Spectrum – both RF equipment and frequencies operating in Canada must be licensed (DNDP35 Part 6)
NOTE: every terminal is licenced in Canada for use at their primary location; when you deploy within Canada, this licence must be updated with the current operating location
Industry Canada: Industry Canada is the Canadian national authority for RF spectrum management and delegates certain management authorities and responsibilities to the DND and the CAF.

## Slide 5
Clearance To Radiate
Outside Canada:
  DFSM will submit Frequency Supportability Requests thru SHAPE to the Host Nation
  Only the Host Nation can grant Clearance to Radiate
Notes: TP: DFSM - acting as the technical authority for RF spectrum management for the DND and the CAF
- Requests for Spectrum supportability (DNDP35 Part 5-5)
- Submitted in advance of deployment (60 days preferred)
SHAPE – Supreme Headquarters Allied Powers Europe (SHAPE) at Casteau, Mons, Belgium.
Host Nation: provides approval for Radiating any RF Frequencies within their bounderies

## Slide 6: Clearance to Operate
What constitutes Clearance to Operate in Canada?
  MIDS Notification Message submitted to appropriate Authorities
  Unit / Platforms inclusion in the Standing or Exercise OpTASKLINK
  Approved entry of activity into the US Deconfliction Server
CJOC STOP 16 DIRECTIVE
Notes: TP: In Canada, MIDS Notification Message will be submitted by your ICO or TDL300 planner; units that operate on a regular basis typically submit these to NAV Canada and DFSM for an entire month timeframe.
For exercises with high TSDF, a Waiver is submitted to DFSM ahead of time and included in the MIDS Notification Message at para 9.
Conduct Time Slot Duty Factor (TSDF) calculations and ensure link 16 deconfliction, ensuring compliance with national Frequency Clearance Agreements (FCA’s);
All MIDS Notification messages must include a POC for STOP Link 16 and during operations, operators must monitor Guard for Stop Link 16 or CEASE Buzzer calls. In an emergency situation where flight safety is in jeopardy, NAV CANADA will order "STOP LINK16" over the guard frequencies, and advise CFICC of their actions. Note: All units/platforms are to man the guard frequencies 243.0/121.5 MHz during all Link16 operations.

## Slide 7: Clearance to Operate
What constitutes Clearance to Operate outside Canada?
  The entity that is responsible for Link 16 Operations and will provide OpTASKLINK parameters is the granter of CTO
  CTO authority will require confirmation of CTR from Host Nation for duration of activity
  CTO authority provides Network and Crypto requirements
Notes: TP: The ICO or Planner responsible for your unit/platform’s Link 16 requirements will be completing these requests;
The Elemental DLMC (RCN / RCAF) will assist and make the initial coordination with the appropriate TDL agencies (ie: TDL @ CAOC Uedum, CPD @ CAOC Torrejon, or TDL POC for applicable region/range training area in the US (MIRAMAR, KEY WEST, CONR, etc); As per Annex B, Canadian Frequency Clearance Criterial, para 3.1: MIDS operations in Non-NATO countries have to be coordinated with the Host Administrators or Theater Spectrum Manager.
The Network Design Facility needs the Network and Identification Set details early to ensure platform load files are built in time to test before departure.

## Slide 8: Time Slot Duty Factor (TSDF)
TSDF Limitations:
Geographic Limitation:
  - No more than 100% TSDF within 100 NM radius circle of each terminal
  - 100% = 396,288 pulses per 12-sec interval
  - 400% total TSDF within 200 NM radius around any terminal
Individual Terminal Limitation:
  - No single or closely spaced terminals can use over a combination of more than 50%
100 / 50 (300)
Notes: TP: The ICO or Planner responsible for your unit/platform’s Link 16 requirements will be completing these requests and calculations;
Conduct Time Slot Duty Factor (TSDF) calculations and ensure link 16 deconfliction, ensuring compliance with national Frequency Clearance Agreements (FCA’s);
Time Slot Duty Factor is the calculation of the percentage of timeslots being used within a geographical area to ensure no harmful interference to other systems in the same frequency band
ATC systems such as TACAN, DME, IFF operate in the same frequency band as L16
TSDF calculations are always calculated on the times slots assigned regardless of whether or not transmissions occur
Closely spaced terminals are defined as within 3 NM radius of each other.

## Slide 9: TDMA Breakdown & TSDF
1536 time slots
12 seconds
FRAME
98304 time slots
12.8 minutes
EPOCH
A-0
B-0
C-0
1536 time slots
12 seconds
TIME SLOTS
(Time slot = 7.8125 msec)
396,288 pulses per frame
Notes: 1536 time slots are divided into 3 Sets (A – B – C ) of 512 ts in each (numbered 0 – 511)
The 12 Frame allows for 396,288 pulses

## Slide 10: Time Slot Duty Factor (TSDF)
How to calculate the Total TSDF?
TSDF FORMAT:
TOTAL TSDF / HIGHEST SINGLE UNIT
UNITS TSDF
RELAY TSDF
+ VOICE TSDF
TOTAL TSDF
Notes: TP: The ICO or Planner responsible for your unit/platform’s Link 16 requirements will be completing these calculations but as a Multi-Link Operations Specialist, you may be tasked to monitor TSDF compliance using CINEMA or other tools (PO004 will provide hands on training with CINEMA)
THE NDD provides worse case TSDF for each platform – we will be going the the NDD in the next lesson.
  Add the NDD provided TSDF for all participating units together
  Next, add in any relay TSDF (also found in NDD)
  Finally, add in any voice TSDF (also found in NDD)
  Then find the platform with the highest TSDF

## Slide 11: TSDF and Deconfliction Process
Units must self-regulate and ensure their Link 16 transmissions do not cause harmful interference
CJCSI 6232.01 compliance: all units within 200nm of US territory must be approved in the JID Deconfliction Server before transmitting
Notes: To comply with NAVCAN/FAA/National Air Traffic Management systems, units transmitting on Link 16 are required to self-regulate and ensure they do not cause harmful interference

## Slide 12: De-confliction Process
Two types of areas: single point (used for fixed transmitters); JTIDS Operating Area (JOA) for moving terminals
Notes: TP: Wing or Link Unit Managers (LUM) are responsible for entering activity into the deconfliction server whenever L16 operations are planned. For activity that is not within the 200 NM of the US Border or that activity in support of Operations (NORAD missions) do not get entered into the Deconfliction Server.
The Server calculates TSDF 100 NM around the single point for fixed, and 100 NM around the JOA border for moving of all activity entered into the database to approve operations and provides the maximum TSDF available (remaining to use) when entering your activity.
The Joint De-confliction Server calculates the buffer zones around areas to approve transmissions
The information included in the Canadian MIDS Notification Message matches what gets entered into the Deconfliction Server.

## Slide 13
Confirmation Questions
What Link 16 activity must be entered into the US JID Deconfliction Server?
  All activity within 200 NM of the US territory
What frequency will Stop Link 16 or Cease Buzzer calls be transmitted on?
  Guard 243.0 / 121.5
Explain how Total TSDF is calculated.
  THE NDD provides worse case TSDF for each platform
  Add the NDD provided TSDF for all participating units together
  Next, add in any relay TSDF (also found in NDD)
  Finally, add in any voice TSDF (also found in NDD)
  Then find the platform with the highest TSDF

## Slide 14
Confirmation Questions
Why is TSDF Calculations and Deconfliction important?
  Conduct Time Slot Duty Factor (TSDF) calculations and complete link 16 deconfliction to ensure compliance with national Frequency Clearance Agreements (FCA’s)
Who is the Authority for Clearance to Radiate in Canada?
  DND Frequency Spectrum Management
What elements in Canada constitute Clearance to Operate?
  MIDS Notification Message submitted to NAVCANADA and appropriate agencies; inclusion in the OpTASKLINK for the exercise or operation; approved entry in the US JID Deconfliction Server (where necessary)

## Slide 15
QUESTIONS?