## Slide 1
EO 001.02
Decode Link 16 Messages

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3: Introduction
Notes: Throughout this course we will be talking about all the various components of Link 16. When referring to Link16, this diagram shows that it includes the software, hardware, RF equipment and the waveforms of Link 16. For the ease of instruction, this material will be spread over various Learning Objectives, Enabling Objectives and Performance Objectives to help solidify the theory of Link 16 and how the Canadian Armed Forces uses it within Multi-Link Operations.

## Slide 4
OVERVIEW
Describe J-Series Messages to include:
  Initial, Extension, and Continuation Words
  Common Messages and their use
  Network Participation Groups
Compare Identity and Amplification categories of Link 16 v Link 11
Examine MilStd 6016 / STANAG 5516 in relation to Link 16 principles

## Slide 5
Lesson
Notes: TP: The host sends information to the terminal using JTIDS Terminal Input Messages (TIMS) or MIDS Functional Input Messages (FIMS).
On airborne platforms, the host is the mission computer; at ground-based installations, the host is the tactical computer. Host will be discussed in a later PO.
Excerpt from Understanding Link 16 Guidebook

## Slide 6: J-Series Message Sets
J0.X System Mgmt
J2.X PPLIs
J3.X Track Reports
J7.X Information Mgmt
J9.0 Commands
J10.X Weapons Coord and Mission Mgmt
J12.X Air Control
J13.X Platform Status
J14.X EW
J15.0 Threat Warning
3.0 Reference Point
3.1 Emergency Point
3.2 Air Track
3.3 Surface Track
3.4 Subsurface Track
3.5 Land Track 3.6 Space Track
3.7 EW Product
32 Categories
8 Sub-categories
Notes: TP: The building blocks of a MIDS network are Network Participation Groups (NPGs), they support a specific function and the exchange of specific J-series messages.
Up to 256 Messages are possible but not all are defined. (32 x 8 = 256)

## Slide 7: J Series Message Sets
3.0 Reference Point
3.1 Emergency Point
3.2 Air Track
3.3 Surface Track
3.4 Subsurface Track
3.5 Land Track 3.6 Space Track
3.7 EW Product
3.2I
3.2E0
3.2C1
Most messages are 2 or 3 words:
I = initial word
E = extension word
C = continuation word
Notes: TP: J-Series messages are generated by the terminal and the host system, which is usually the combat system. Each JTIDS word is 70 bits and 5 bits for parity. All J-Series messages begin with an Initial (I) word. Additional required information is then added in extension (E) words, and optional information is included in the continuation (C) words. The first two bits of a word indicate whether it is an I, E, or C message. Messages may be from two to eight words, but most are two or three words.
J-Series messages are functionally-oriented with variable-length strings of 75-bit words. A message is started by an initial word; it may then be followed by extension words to transmit logically associated data field groupings that are longer than can be accommodated by the initial word. The extension words may be followed by continuation words which supply supplemental information normally transmitted on a infrequent basis. There may be multiple J-Series messages varying in function within a time slot.
SECTION 5, PART 1, J-SERIES MESSAGE DESCRIPTIONS of ATDLP 5.16 for more detailed information.

## Slide 8: Track Data Comparison
J3.2 AIR TRACK
TRACK NUMBER
STRENGTH
ALTITUDE & SOURCE
ID CONFLICT INDICATOR
TRACK QUALITY
ID CONFIDENCE
ID & AMP & SPEC INTEREST
LATITUDE
LONGITUDE
PASSIVE/ACTIVE
COURSE
SPEED
IFF MODE 1,2,3,4 & SOURCE
PLATFORM TYPE
PLATFORM ACTIVITY
PLATFORM ID
M2 AIR TRACK
TRACK NUMBER
ID & AMP
TRACK QUALITY
X,Y COORDINATE
M.82
TRACK NUMBER
ALTIUDE & SOURCE
X,Y SPEED
TIME TAG
STRENGTH
ID AMP
Notes: TP: J-Series messages allow for more granular information about a single track to be passed and displayed. The above comparison shows all the different fields that can be populated with amplification information on a Single L16 air track vice that which is limited in Link 11.
BONUS TP: Not all J-Series Messages are compatible for forwarding to Link 11. This list is outlined in STANAG 5616.
Only the following J-series messages are compatible for translation to Link 11:
J2.0, J2.2, J2.3, J2.4, J2.5, J2.6
J3.X
J5.4
J6.0
J7.0 – J7.7 (J7.6 excluded)
J9.0
J10.6, J10.5, J10.3, J10.2
J13.5, J13.4, J13.3, J13.2
J14.0, J14.2

## Slide 9: Octal numbers for IUs and Track Numbers
IU / TN Range (Octal) | Use
00001-00076 and 00100-00176 | C2 IUs
00200 – 07776 | Non-C2 IUs and TNs
10000 – 77776 | Non-C2 IUs and TNs
77777 | Reserved for Network Manager
00176 | Pseudo-TN for forwarding data from C2 JUs with TN greater than 00177
00177 | Collective Address
00077 and 07777 | Illegal for use on the interface
0A000 – ZZ777 | Reserved exclusively for TN allocation
Notes: TP: These were presented during EO 001.01 lessons where you learned why these links use OCTAL numbering; here you can see how they relate to PUs and TNs within Link 11. See how many more JUs (upto 5 digits in High block JUs) and TNs (alpha numeric & 5 digits)
The octal numbers 00001-00076 and 00100-00175 are allocated as addresses on Link 16 for C2 IUs.
NonC2 IU addresses and TNs for the use of reporting tactical information are allocated from octal numbers 00200-07776.
The octal numbers from 10000-77776 are also reserved as nonC2 IU addresses and TNs for use in reporting tactical information.
The octal number 77777 is reserved as the Network Manager dedicated address and is assigned in addition to the unit's JU address.
The alphanumeric octal characters 0A000-ZZ777 are reserved as TNs for exclusive use in reporting tactical information.
Track number 00176 (octal) is reserved as a pseudo-TN for forwarding data from Link 16 C2 JUs with TNs greater than 00177 (octal).
The octal number 00177 is reserved as a collective address; it is not assignable as a unit address. The octal numbers 00077 and 07777 are illegal for use on the interface.

## Slide 10: Network Participation Groups
NPG are:
  building blocks of a Link 16 Network
  Support a specific function
  Support the exchange of specific J-Series messages
NPGs are defined by
  Participants
  Function
  Access Protocol
ENTRY
RTTs
PPLIs
EW
A/C
SURV
VOICE
F-F

## Slide 11: Categories of NPGs
System NPGs
C2 NPGs
Notes: TP: All participants in the RF Link 16 Network require timeslot allocation for these System Messages. They are what allows the terminal to connect and report itself.
NOTE: not everyone will have transmit allocation in NPG 4, this is only assigned to the JICC or Network manager. NPG 4 allows for on-the-fly reallocation or design of a Network.
Function of Command and Control – Tx slots would be allocated to C2 platforms and track producers

## Slide 12: Categories cont’d
Non-C2 NPGs
Single use
Notes: TP: Non-C2 NPGs primarily used in the CAF are NPG 9 (Fighter Back-link) and the internal Ftr-to-Ftr (NPG 19);
US assets also use NPG 20 for crypto isolated message exchange between US fighters. Of note: the CF 188 is not capable of using NPG 20.
Some Canadian networks are now built with NPG 19 Crypto isolation when working with Allied partners in Canada. This was a request of the CF188 community during Maple Flag 17. Most legacy networks allow NPG 19 to operate on the default Net/Crypto.
We will expand this into Stacked Nets, Multi-netting, Dedicated and Contention when we talk access modes in a later lesson.

## Slide 13: Standards for Link 16
MIL-STD 6016, F, Ch 1: TDL 16 Message Standard, January 31, 2017
STANAG 5516, Ed 8: Tactical Data Exchange - Link 16, April 1, 2019
ATDLP 5.16, B1: Standard Operating Procedures for NATO Link-16, April 1, 2019
ATDLP 5.16 (A) (1): Tactical Data Exchange - Link 16
STANAG 5616, Ed 5: Standards for Data Forwarding between Tactical Data Systems employing Link 11/11B, Link 16 and Link 22, August 17, 2011

## Slide 14
Confirmation Questions

## Slide 15
QUESTIONS?