## Slide 1
EO 002.02
Extract Link 16 Units Specific Information from the OpTaskLink Message

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
OpTaskLink JU Specific sets
Legal entries
Notes: TP: This lesson will be a guided exercise to familiarize trainees with the Link 16 segments of an OTL, each trainee needs to have access to electronic copies of OTLs and Message Drafter for Guided exercise and review activity.

## Slide 4: Link 16 OTL Segment
LNKXVI/LINK 16 SEGMENT//
PERIOD/020800ZSEP2019/291600ZSEP2019//
JNETWORK/CAJE0007A/10JUL2003/OVERLAND/Z/ZERO//
CPD/01MAY2007/1//
JCRYPDAT/1/AKAT3109/-/0/1//
JTRNMODE/NO TEST/EXER/NOR/MODE 1//
JSTNETS/FTF/19/015/CAP BRAVO//
JSTNETS/VOICE A/12/025/ADCCN//
FORCFLTR/FJ28 /ALL/9/FIXED/-/AL/PE//
GENTEXT/JTIDS NETWORK MANAGEMENT/THE JICO WILL BE LOCATED AT THE CAOC AND PERFORM OVERALL MANGEMENT OF THE MTN//
JUDATA/SHIP:NIMITZ/CS:STONEWALL/JU:00076/16/-/
/BLOCK:05000-05277/-/SHIP(12)/-/NORM/200/PRI/Y/-/-/FBLOCK:07000-07777//
JSURVOPT/2/1/CVBG-1//
LKSXDUTY/812/815//
FILTER/FJ28/ ALL/FIXED/-/AL/PE//
Notes: TP: In Canada, OTLs are often written to APP-11 or USMTF format. For this course, the Message Drafter is APP-11 compliant.

## Slide 5: L16 Segment
Two main parts:
  Network wide parameters
  Individual unit parameters
Link 16 Sets starts with a ‘J’
LNKXVI/
PERIOD/
JNETWORK/
CPD/
JCRYPDAT/
JTRNMODE/
JSTNETS/
FORCFLTR/
GENTEXT/
JUDATA/
JSURVOPT/
JCNTROPT/
LKSXDUTY/
UNITFLTR/
UNITTSR/
All platforms use this information
Individual
platform settings are here

## Slide 6: APP 11 (D)(1)
Notes: TP: Continuing with the APP 11(D)(1) OPTASKLINK.pdf, find L16 and lets now look at the JTIDS Unit specific sets.

## Slide 7: JUDATA Set
Start of Period – DTG
End of Period options:
DTG
DTG ASAPAFT
DTG ASAPNLT
DTG NET
DTG NLT
UFN
Notes: Find the JUDATA Set
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 8: JUDATA (cont’d)
Example:
JUDATA/SHIP:NIMITZ/UIC:USAJ12345/CS:STONEWALL/JU:00001/16 /AMD:00300-00477/BLOCK:AB201-AB500/-/STSBLK:AB201-AB500/SHIP-3 /12/NORM/1000/PRI/-/-/FBLOCK:00300-00500//
Notes: Find the JUDATA Set
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 9: JSURVOPT
Example:
JUDATA/SHIP:NIMITZ/UIC:USAJ12345/CS:STONEWALL/JU:00001/16 /AMD:00300-00477/BLOCK:AB201-AB500/-/STSBLK:AB201-AB500/SHIP-3 /12/NORM/1000/PRI/-/-/FBLOCK:00300-00500//
JSURVOPT/2/1/EVENT 1AC//
Notes: Find the JSURVOPT Set – follows a JUDATA set for a participant that is participating in a Surveillance Option Pool.
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 10: JCNTROPT
Example:
JCNTROPT/09/1/27/EVENT 1AC//
Notes: Find the JCNTROPT Set – Similar purpose as JSTNETS already covered in the last lesson.
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 11: JFTROPT
Example:
JFTROPT/20/1/27/-/EVENT 1AC//
Notes: Find the JCNTROPT Set – Similar purpose as JSTNETS already covered in the last lesson. Could be isolated under each JU when control and FTF has been designated for the Platform specifically.
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 12: UNITTSR
Example:
UNITTSR/0/DISABLED/SUSPEND/7/4/STN/ON/3/1843/2// UNITTSR/4/ENABLED/OPERATE/7/4/TABLE:115/OFF/6/1122/2//
Notes: Find the UNITTSR – Amplifies the TSR Settings of the JUDATA above it.
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 13: JWCRYPDT
Example:
JWCRYPDT/WPN:JSOW/USEZD M12166 880091/AKAC123/CVLL:1 /USEZD M12168 880091/USEZD M12166 880092/01/CVLL:2 /UW3AEN2348 88921/USEZD M2233/23//
Notes: TP: Find the JWCRYPDT Set – Network Enabled Weapons – new capability and this segment will set out specifics for these new weapons.
Key: M- mandatory, C – Conditional, O- Operationally Determined Set/Segment,
Some fields can be repeated

## Slide 14
Confirmation Activity
Using the OpTaskLink Link 16 Segment to complete the Unit Specific Parameters of the Mission Planning Sheet.
Notes: TP: Confirmation will use CF 19 OTL to complete their Unit assigned parameters of their Mission Planning sheet. Each trainee will be assigned a unique unit. Trainees will Use Think, Pair, Share to compare answers.

## Slide 15
QUESTIONS?