## Slide 1
EO 002.04
Extract JREAP and Legacy Information

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
JREAP and Legacy Links
JOINT RANGE EXTENTION Segment
UNITINFO Set
TIMEREF Set
LNKPROT Set
CONMATRX Set
FORCFLTR Set
SATCONN Set
SECTEL Set
SECINTER Set

## Slide 4
JREAP and Legacy Links
Joint Range Extension Application Protocol is defined by MIL-STD 3011, and has 3 annexes
  Annex A for Satellite Communications
  Annex B for Serial Communications
  Annex C for Computer Network Communications
JREAP was developed to solve the problem of many different BLOS standards that were developed independently
  Sat-J replaced by JREAP A
  Serial-J replaced by JREAP B
  Socket-J replaced by JREAP C
These Legacy standards are still in use in some countries/operations
  Most Gateways are backwards compatible
Notes: The JREAP Protocols define how to exchange data, including data assurance, transfer rates, and error detection. They may use existing protocols (such as TCP/IP), but it defines how those protocols are used to exchange data.
NATO has developed a competing product called SIMPLE (Standard Interface for Multiple Platform Link Evaluation), which is governed by STANAG 5602. It does not have a JREAP-A analogue, but can used on computer networks and serial connections.
The legacy protocols were developed independently of each other, usually by vendors looking to sell a product. The protocol would then be exclusive to a specific piece of equipment, or licensed for a fee. JREAP was introduced to bring order to chaos, and create an open standard.
Not all organizations or countries have the ability to upgrade their link equipment, so backwards compatibility is important. It comes down to what equipment is available, and what that equipment is capable of.
Gateways can also move between standards as well. Input SIMPLE, and output JREAP C for example.

## Slide 5
JOINT RANGE EXTENTION Segment
The JOINT RANGE EXTENTION Segment in the OTL holds all the information for units to be configured to operate JREAP and Legacy Links
The segment describes
  JREAP A and Sat J
  JREAP B and Serial J
  JREAP C and Socket J
It is divided into JRE Units and then further into JRE networks
JOINT RANGE EXTENTION SEGMENT
  JRE Unit info
    Network 1
    Network 2
  JRE Unit info
    Network 3
    Network 4
Notes: The JRE Segment is divided into Units and Networks.
In APP-11, the units and networks are not well divided, and it takes some effort not to get lost in the document. Treat the UNITINFO Set as a header, and all of the information after it as you would LPUDATA for Link11 or JUDATA for Link 16.

## Slide 6
JOINT RANGE EXTENTION Segment
Each unit is defined with the UNITINFO Set
  A single unit can have many different networks
Each network is defined by several sets
  TIMEREF – Time Reference
  LNKPROT – Link Protocol
  SECINTER/SECTEL/SATCONN - Secure internet/telephone/satellite
  CONMATRX – Connection matrix
  FORCFLTR – Force level filter
The term network is decieving. Most networks have 2 participants
  JREAP A is capable of multiple participants on a network
  JREAP B is capable of 2 (phone line)
  JREAP C is capable of 2 (TCP Client and Server)
Notes: If you have an OTL that relies heavily on JREAP, the JOINT RANGE EXTENTION Segment will be very bulky.
In each network, only FORCEFLTR is not required. A unit with 2 JREAP-Bs will require 9 lines to defined.

## Slide 7
UNITINFO Set
UNITINFO describes a unit's JREAP data in the architecture
  Similar to LPUDATA and JUDATA
If a unit has a secondary JU (due to being on two architectures), it is also listed
A JREAP track block is also assigned, if necessary
Notes: Usually, the JRE Track Block is the same as a Link 16 track block. JREAP Units that are not C2 may still require a small trackblock for generating reference points or similar data.

## Slide 8
TIMEREF Set
JREAP and Legacy links require the timing to be configured
This is used to determine the timelate of the information, and to apply corrections if necessary
There 2 main ways to measure the timing
  If both units have a good time signal, read the timestamp of the received message, and compare with your local clock = UTC
  The network can send Round-Trip timing messages to measure the delay, and use that value = RTT
TIMEREF determines the timing solution for one network of the unit.
Notes: Units that are on low bandwidth, high latency connections (such as satellite) will tend to use UTC, as no timing data is required to be sent over the network.
Units that are on high bandwidth, low latency connections (such as TDLWAN) will tend to use RTT as it is reliable. Also, if a unit does not have access to a time server such as an NTP server, or GPS, RTT is the method of choice.
If the time information is incorrect, the corrective calculations (called extrapolation in JREAP) will incorrectly calculate the tracks in incorrect positions.

## Slide 9
LNKPROT Set
The LNKPROT Set defines the critical elements of the JRE protocol for the one network
This is where it is stated if a unit is using JREAP or a Legacy Protocol
  For JREAP-C, it also determines if TCP/IP or UDP is in use
Notes: Each LNKPROT Set is

## Slide 10
CONMATRX Set
CONMATRX defines, for a specific network, which units are connected
Each network requires one CONMATRX line.
  For JREAP B & C, it is who you are connected to.
It defines units as 2 pieces of data
  Source Link Designator
  Unit Designator
Notes: Each Gateway defines their connections as a source link designator. If a unit has multiple JREAP Cs with another unit, it allows the OTL to specify which connection it is referring to.
Nowhere in the OTL does it define what these source designator numbers mean, the must be referenced elsewhere.

## Slide 11
SATCONN Set
The SATCONN Set determines if the satellite is using a VHF or UHF satellite connection
JREAP A is defined to be a UHF DAMA circuit
  VHF in SATCONN set is only for legacy protocols
It carries no information about DAMA configurations or Satellite Network Controllers
  Consult the OPTASKCOMMS for this information
Notes: This is the only set where multiple CONMATRX partipants make sense.

## Slide 12
SECTEL Set
The SECTEL set provides the data to establish Secure Telephone Lines for serial links
It provides the transmission rate in bits per second (or baud) and a telephone number
Notes: No infrastructure information is here either. No mention of line crypto or VIPER vs STE. Just the information an operator needs to input into his gateway.

## Slide 13
SECINTER Set
The SECINTER Set provides information on the configuration of network parameters for BLOS links
It provides:
  Either an IPV4 or IPV6 network address
  A TCP Port Number
  Network Client or Server designation
    - In APP-11(D)(1), Server is called MASTER
If the LNKPROT is UDP, the Network Client set will be /-/
Notes: Again, no infrastructure information. No firewall configurations or subnet masks, just the information you enter into your gateway to configure this link.
Although computer networks have connected all the computers and systems together, a JREAP C is a point-to-point connection between 2 computers.

## Slide 14
FORCFLTR
Assigns a unit filters when operating in the architecture
Just like other OTL filter sets, the filter is designated by a letter and number, which is defined elsewhere
The term FORCE is FORCFLTR means that the filter is a force-level filter rather than an individual filter
  It doesn't mean that the unit is forced to use the filter
  All filters designated in an OTL are required
Notes: This filter set is similar to, and serves the same purpose of the other filter fields in the OTL.

## Slide 15
Example
HEADING/JOINT RANGE EXTENSION DATA SEGMENT//
UNITINFO/UNIT:CADS/-/CS:SIDECAR/44444/AA000-AA777//
TIMEREF/RTT//
LNKPROT/16/UNIT:EADS/TCP-IP(JPC)//
SECINTER/IPV4:10.20.30.1/6000/MASTER//
CONMATRX/100/UNIT:EADS//
TIMEREF/RTT//
LNKPROT/16/UNIT:WADS/TCP-IP(JPC)//
SECINTER/IPV4:10.20.30.2/6005/CLIENT//
CONMATRX/200/UNIT:WADS//
TIMEREF/UTC//
LNKPROT/16/UNIT:ANR/UDP-IP(JPC)/
SECINTER/IPV4:10.20.30.3/6010/-//
CONMATRX/300/UNIT:ANR//
TIMEREF/UTC//
LNKPROT/16/UNIT:CONR/JREAP-B//
SECTEL/9600/1-705-494-2011//
CONMATRX/400/UNIT:CONR//
Notes: This segment only defines 4 JREAPs from CADS to it's adjacent sectors.
Each unit is required to spell out all of it's connections in the same way.

## Slide 16
QUESTIONS?