## Slide 1
EO 001.06.01
Describe Variable Message Format (VMF) and User Community

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
VMF Definition
History of VMF
VMF in Canada
VMF in NATO

## Slide 4
References
MIL-STD 6017A
STANAG 5519
WWW.
MIL-STD-188-220
Understanding Voice and Data Link Networking

## Slide 5: VMF Definition
VMF is designed as a common means of exchanging digital data across an interface that could be between combat units at varied organizational levels, with varying needs for volume and detail of information, and applicable to a broad range of tactical communication systems.
Notes: Link 11,16,22 etc are reliant on a particular type of equipment, VMF can use a variety of mediums for data exchange.
The four advantages are listed below:
①Information coding standard of variable message format is bit-oriented. Messages are passed vie binary code. It can not only reduce the amount of data transmitted, but also improve machine automatically recognize and deal with the message easily.
②Because of its coding standards, VMF can make use of network resource to enhance the adaptability and effectiveness of the message.
③According to the literal meaning of VMF, the specific format and length of VMF can be adjusted in practical application.
④Because of its flexible syntax, VMF only allow users to send necessary information. The size of the necessary information could be changed, thereby reducing the amount of data transmitted and saving bandwidths.

## Slide 6: VMF History
Originally developed by United States Military;
Development began in 1970s;
VMF was originally to be included in Link 16;
Standard development was originally to include fixed and variable formats to satisfy the needs of all users.
Notes: Fixed format words in link 16 consist of 75 bits 70 data 4 parity and one spare bit,
VMF messages vary in content and length.
Variable messaging in Link 16 and VMF are different, don’t confuse the two.

## Slide 7: VMF History Cont.
As development progressed, the land force requirement became too large;
US Army began its own development;
VMF was then developed as its own standard (K Series);
First fielded in 1990s.
Notes: The Land force required specific types of messages that catered to a specific type of messages (JTAC, Artillery etc)

## Slide 8: VMF Users in Canada
RCAF – CF-18, Tactical Air Control Party (TACP)
CA – Joint Terminal Attack Controller (JTAC)
Digitally Aided Close Air Support (DACAS)
Enhanced Position Location Radio Set (EPLRS)
SOF – DACAS, Positional Information.
Notes: RCN Doesn’t use VMF presently.
JTAC and TACP can send and receive JTARS, updated enemy and friendly positions and more via text message with the CF-18.
EPLRS operates in a TDMA based network (vehicle mounted), primarily for positional data and test messages.
SOF requirements and use are similar to those of the JTAC and TACP.

## Slide 9: VMF Users in NATO
NATO has stated that the three TDL’s it will support moving forward are:
VMF
Link 16
Link 22
Notes: VMF was initially developed for the Land force.
Link 16 was initially developed for the US Air Force/Marines.
Link 11/22 was initially developed for the USN.
VMF was initially developed for the US Army. It will continue to be a method of digital data transfer in Canada (CA), along with its allies. The majority of messages are for Land force use.

## Slide 10
Confirmation Questions
What is VMF?
Who was it originally developed for?
Who uses VMF in Canada?
Notes: VMF is designed as a common means of exchanging digital data across an interface that could be between combat units at varied organizational levels, with varying needs for volume and detail of information, and applicable to a broad range of tactical communication systems.
It was developed for the US Land force (Army).
CA, RCAF, SOF

## Slide 11
QUESTIONS?