## Slide 1
EO 001.03
Describe the Link 16 Synchronization Process

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
Link 16 Synchronization Process
  Sync States
  IEJU
  RTTs
  Time base
Link 16 Duties
Notes: TP: This lesson will be a guided exercise to familiarize trainees with the Link 16 Synchronization Process and Link duties required to function in a Link 16 Network effectively

## Slide 4: Synchronization States
Sync State 1
No Sync
Sync State 2
Coarse Sync
Sync State 3
Fine Sync
Notes: TP: During JTIDS/MIDS operations, a terminal will be in one of three synchronization states.
No Sync is considered Sync State 1. In No Sync, a terminal has entered an estimate of system time and started net entry, but has not received any Initial Entry messages.
Coarse Sync is Sync State 2. In Coarse Sync, a terminal has received an average of two Initial Entry messages and its time error is within ½ time slot (3ms) of the time base. In Coarse Sync, a terminal is capable of receiving all JTIDS messages, but can only transmit RTTs.
Fine Sync is Sync State 3. In Fine Sync, a terminals system time is within 4 pulses of the time base. In Fine Sync a terminal is capable of normal operations. Fine Sync can be achieve in two different means:
- Active Fine Sync is achieved through the use of Round Trip Timing messages.
- Passive Fine Sync is achieved through received PPLIs.

## Slide 5: Sync State 1 - No Sync
NTR identifies network time
NTR time quality is 15 in a STRN, < 15 in an ETRN
NTRs are, by definition, in Fine Sync
1
2
3
4
5
6
12
7
8
9
10
11
Notes: TP: In order to start the sync process, there needs to be a time base.
In a System Time Reference Network (STRN), the time base is known as the Network Time Reference (NTR).
The NTRs clock is the model upon which all other units will base their system time.
In a STRN, the NTR has a time quality of 15 and is automatically in sync state 3, Fine Sync. This gives the NTR the capability to transmit and receive all messages.
In an External Time Reference Network (ETRN), the time base is Universal Coordinated Time (UTC), which is a capable terminal will normally receive via GPS. There is an NTR in an ETRN, but the NTR models his clock off the GPS satellites. An NTRs time quality in an ETRN is < 15.

## Slide 6: Clock Model
JUs must model their clocks after the NTR’s clock to gain and maintain synchronization
The NTR identifies system time for other units
Initial Entry Messages J 0.0
1
2
3
4
5
6
12
7
8
9
10
11
1
2
3
4
5
6
12
7
8
9
10
11
Notes: TP: A JU is required to model its clock against the NTRs clock, whether in a STRN or ETRN.
The NTR will broadcast Initial Entry Messages (J0.0). Each Initial Entry Message will identify the start of a specific frame.

## Slide 7: Initial Entry Messages (J0.0)
Label J0
Sub-label .0I
Message length 0-7 additional words
Default net number 0
RTT Reply Status 0 (will reply)
Time Quality 0-15
Slot Block Assignments Not used
Information Fields
Notes: TP: An Initial Entry Message (IEM) is used to identify the start of a specific Frame in a JTIDS/MIDS Epoch.
It is always transmitted in timeslot A-0 on net 0.
The IEM will also provide the time quality of the unit transmitting.
The NTR will transmit an IEM in every Frame.

## Slide 8: Estimated Time of Day
An entering unit must guess at network time
This guess is used to calculate the proper reception codes
Large time estimate errors will delay entry
Recommended entry accuracy is +/-6 seconds
1
2
3
4
5
6
12
7
8
9
10
11
?
Notes: TP: In order for a JU to start net entry, the first thing it must do is estimate the time of day.
The estimate is a guess at network time, normally based on a time hack, or GPS time.
The guess is used to calculate a future reception code for receiving an IEM.
When a JU enters its guess, it also enters an error estimate, or an estimate of how accurate its guess is. For some systems, this error estimate is fixed, but most systems can change the estimate.
The larger the estimate, the longer it will take for a terminal to receive its first IEM. The recommended error estimate is +/- 6 seconds.

## Slide 9: Look Ahead
The NTR identifies System Time
  Transmits a different net entry message at the beginning of each frame
All units entering must guess at that time
  Entered time should be as accurate as possible (+- 6 sec recommended)
The entered uncertainty is used to calculate the proper reception codes
  Establishes the look window
T0
T1
T0
2DT
}
actual error
}
T2
error estimate
Notes: TP: As stated prior, the NTR identifies System Time (JTIDS time) and transmits an IEM in timeslot A-0 each frame.
Each IEM is different, as it identifies the start of a specific frame in an epoch.
Each JU must guess at system time and will enter an error estimate, based on how good their guess is. (Improved by using a GPS or conducting a TIME HACK off a platform that is currently in Fine Sync, this does not have to be the NTR)
This error estimate is used to calculate the reception codes for a future IEM. Based on the error estimate, a look window is created.
This look window is equal to two error estimates (i.e. if the error estimate is 6 seconds, the look window will be 12 seconds). The terminal will calculate what the reception code (hopping pattern) will be at a future time and will wait and listen for that specific pattern.

## Slide 10: Sync State 2 - Coarse Sync
First initial entry messages received
  The clock will be set
Second initial entry message received
  The speed of the clock will be determined
  Coarse sync will be declared
Up to 3 time uncertainties (3DTs) to achieve coarse sync
T0
T1
T0
T2
T3
T3
Notes: TP: Once the predicted hopping pattern is received, the terminal will start following transmission, using the first IEM it receives to set its clock (i.e. to tell it when the start of the frame is).
Then the terminal will use the second, or subsequent, IEM to set the clock speed.
Once the clock is set and the clock speed is determined, and the terminal time is within ½ of a timeslot from the NTR, then the terminal will declare coarse sync.
It is understand that it can take up to 3 time uncertainties in order to achieve coarse sync.
If the terminal does not declare coarse sync within the maximum allowable time, it will reattempt entry until it attains coarse sync or the process is reinitialized manually.

## Slide 11: Coarse Synchronization
Using network prediction codes, a unit listens for the net entry message
Coarse Sync is declared upon receipt of two J0.0 messages
In Coarse Sync
  A unit can receive all messages
  Only RTTs can be transmitted
Notes: TP: Once the terminal declares coarse sync, the unit will be able to receive all messages, but only be able to transmit RTTs.
Whether in a STRN or an ETRN, coarse synchronization will be achieved the same way.

## Slide 12: Sync State 3 - Active Fine Sync
From Coarse Sync, the terminal tracks received PPLIs
generates and transmit Round Trip Timing Interrogations (RTT-Is)
  NPG-2 messages are addressed to the unit with the highest time quality
  NPG-3 messages are broadcast on the net number (up to 15) of the highest received time quality
PPLI
Any unit that performs Active sync known as a Primary Unit (PRU)
Notes: TP: Once in coarse sync, a terminal can attempt to achieve fine sync either actively or passively. A unit attempting active fine synchronization is known as a Primary Unit (PRU).
In active fine sync, a terminal in coarse sync will begin to track received PPLIs. If the terminal does not receive any PPLIs, it will not be able to achieve fine sync.
Once the terminal starts to receive PPLIs, it will track the PPLIs with the highest time qualities and generate round trip timing interrogations (RTT-I) messages.
There are two different types of RTTs that can be transmitted:
NPG-2 are RTT-A. RTT-A are addressed to a specific unit with the highest time quality. RTT-A’s are always transmitted on Net 0.
NPG-3 are RTT-B. RTT-B are broadcast on the net number of the highest time quality received (i.e. you receive a PPLI from the NTR with a time quality of 15, you broadcast on Net 15).
The NPG 3 - RTT-I is broadcast to whoever is on the net listening and will utilize the first response it receives. NOTE: Most Networks only use NPG 3 for RTTs.

## Slide 13: Round Trip Timing
3 RTT-I messages are sent every 12 seconds
RTT-responses (RTT-R) are used to refine time and gain Fine Sync
Notes: 3 RTT-I’s are sent every 12 seconds until a unit attains fine sync.
When the terminal transmits a RTT-I, the reply it will receive is called a RTT-R (response). These responses are used to refine the time data and gain fine sync.

## Slide 14: Round Trip Timing (RTT) Messages
RTT-I and RTT-Rs are special messages transmitted in the same timeslot
  consist of 72 pulses
  do not contain data words
  the only message transmission allowed in coarse sync
RTT-responses (RTT-R) are used to refine time and gain Fine Sync
RTT-I
Propagation
Delay
Propagation
Delay
RTT-R
Notes: RTTs are special messages because although a JTIDS terminal transmits them, they are not J-Series messages. They also have some other unique attributes:
- An RTT timeslot is the only timeslot in which you will transmit and receive in the same timeslot. The RTT-I and RTT-R are both transmitted in the same timeslot
- RTTs (either I’s or R’s) consist of only 72 pulses with no data words.
- An RTT is the only message that can be transmitted in coarse sync
- Because of the requirement for the RTT-I and RTT-R to be transmitted in the same timeslot, an RTT only has enough propagation delay for the RTT-I and the RTT-R to travel 300nm each.
RTT-responses (RTT-R) are used by the terminal to further refine the time data and attain fine sync when attempting active fine synchronization

## Slide 15: RTT-A vs RTT-B
RTT-A
- addresses
dedicated
1 TS per
single net
RTT-B
broadcast
contention
8 TS total
stacked net
NTR
PPLI
- Qt = 15 - JU 12
- listening on 0
RTT-I - JU 12
my SDU # 125
net 0
NTR
PPLI
- Qt = 15 - JU 12
- listening on 15
RTT-I - any JU with Qt 15
my SDU #125
net 15
Notes: TP: RTT-A’s are normally dedicated. However, a single terminal/load is only assigned one dedicated timeslot for RTT’s. In order to transmit 3 RTT’s in 12 seconds, the terminal must utilize other timeslots in its load to transmit the other two. These two slots are normally the PPLI and a surveillance timeslot.
RTT-B’s are normally contention access. The terminals in the network have a group of timeslots (normally 8) of which they pick three to transmit in.

## Slide 16: RTT-R
NTR
RTT-R
- To SDU #125
- RTT TOA
RTT-I - JU 12 or any JU
- Net 0 or net of Qt
- My SDU # 125
Notes: TP: An RTT-R is the response sent in reply to an RTT-I.
The RTT-R is addressed to the SDU address of the terminal which transmitted the RTT-I and contains the RTT Time Of Arrival.
The RTT-R is used in order to refine a terminal’s time data and attain active fine synchronization.

## Slide 17: Synchronization in an ETRN
JU will achieve coarse sync in the same way as a JU in a STRN
Fine sync is different
  JU will utilize the ETR as a source for time refinement
  If the time quality of the ETR is the same as the highest PPLI received, the Terminal will utilize the ETR for time refinement.
  If a PPLI has a better time quality than the ETR, then the terminal will RTT off the PPLI
Notes: TP: In an ETRN, a JUe (a JU utilizing ETR) will achieve coarse synchronization the same was as a JU in a STRN. However, a JUe will achieve fine synchronization in the following manner:
- Once coarse sync is achieved, the JUe will also use the ETR as a source for time refinement, as well as PPLIs it receives.
- If the time quality of the ETR is greater than or equal to the highest time quality the JUe receives from a PPLI, the JUe will utilize the ETR for time refinement.
- If the time quality of the ETR is less than the highest time quality in the PPLIs the JUe receives, the JUe will perform normal active, or passive, fine synchronization.

## Slide 18: Passive Synch Modes
Two passive modes of operation
  Data Silent (DS)
    - Voice and TACAN only
  Long Term Transmit Inhibit (LTTI or RS)
    - No transmissions
Any unit that performs passive sync or selects DS or LTTI (RS) is known as a Secondary Unit (SU)
Notes: TP: There are two passive modes of operation:
- Data Silent (DS), in which a terminal will be capable of transmitting voice and TACAN only. It will make no other transmissions, to include RTT and PPLI.
- Long Term Transmit Inhibit (LTTI), also known as Radio Silent (RS). In LTTI/RS, the terminal will make no transmissions, but will be able to receive all transmissions.
Any unit that performs passive fine synchronization or selects and operates in the Data Silent or Long Term Transmit Inhibit modes are known as Secondary Units (SU).

## Slide 19: Passive Sync
Fine Sync can be obtained passively
takes longer than Active Sync
  rx PPLIs are used vice RTTs
  Terminal compares TOA messages with expected TOA
Requires at least 3 sources (units in fine sync) of PPLIs
  Good geometry required
Net Entry
PPLI
PPLI
PPLI
Notes: TP: A terminal can attempt to attain fine synchronization passively.
Whether a terminal attempts active or passive fine synchronization, it will always attain coarse synchronization the same way (receipt of IEM’s from the NTR/IEJU).
Passive fine synchronization will normally take longer than active fine synchronization.
In passive synchronization, a terminal will utilize PPLIs vice RTT to gain fine sync.
The terminal will compare the time of arrival of the PPLI message with the expected time of arrival, based on the position reported in the PPLI. It will use the difference in the times to make time refinements.
Passive synchronization will normally require at least 3 sources (PPLIs from units in fine sync), and good offset geometry.

## Slide 20: Sync Maintenance
After Fine Sync achieved
  RTT exchange still required
    - Once every 20 seconds
  JU will either RTT or sync off the ETR, based on time quality
NTR is not required
  IEJUs will function as the NTR
  A JU must first be in Fine Sync first before assuming NTR duty
Notes: TP: After fine synchronization is achieved, a terminal will perform sync maintenance to ensure its clock retains proper time.
To perform sync maintenance, terminals will exchange RTTs about once every 20 seconds.
A JUe will either RTT off a received PPLI or will sync off the ETR, based on the received time qualities.
Once the network is up and operating, the NTR is not required for continued operation.
Units that are already in the network will be able to remain, but no other units will be able to join, unless there are IEJUs operating.
IEJUs also transmit IEMs (J0.0) and will allow units to enter the network.
If the NTR drops out of the network, it is best if another one is assigned to maintain sync stability.
Before a unit assumes duties as NTR, however, it must be in fine sync or else it will fragment the network.

## Slide 21: IEJUs
Initial Entry JTIDS Units (IEJUs) also transmit IEMs
Units beyond line of sight of the NTR can use IEJUs to gain network time
IEJUs transmit the IEM (J0.0) in every other frame
  Timeslot A-0
  once every 24 seconds
NTR
IEJU
Notes: TP: An Initial Entry JTIDS Unit (IEJU) is a unit that is designated to, once fine sync is achieved, transmit Initial Enter Messages (IEM) (J0.0).
IEJUs are assigned to assist in the net entry process by allowing units out of line of sight of the NTR to attain coarse synchronization.
However, where an NTR will transmit an IEM in the first timeslot (A-0) in every frame, an IEJU will transmit an IEM in the first timeslot in every other frame. This allows the IEJU to still receive IEMs from other IEJUs and the NTR, which assists in it’s own sync maintenance.

## Slide 22: Time Base
Zulu or GMT is the only authorize Time Base
Two NTRs will interfere with the Network and cause Fracture
    Note: NTRs do not have to be in line-of-sight of each other to interfere.
Two NTRs need different Crypto
1
2
3
4
5
6
12
7
8
9
10
11
J-Fact: All NTRs uses timeslot A0-6 and net 0
  The use of Time-Offset is not authorized
Notes: TP: The other major factor in net entry is the time and the time base.
Normally, if there is only one active Link 16 Network in use, GMT (ZULU) time will be utilized as the time base.
However, if more than one Link 16 Network is operating in the same area, two NTRs will interfere with each other unless:
- Old practice was to use a Time-Offset: this is when their time base is different (shift by at least + 5 Min from ZULU, but no more than + 10 Min)
- Each network is using a different TSEC crypto
Remember, NTRs do not have to be within line of sight of each other in order to interfere. If there is a platform that is in line of sight of both NTRs, depending on the changes in distances between the NTR, it could shift from one network to the other. Also remember that no matter what network you are using, the IEM is always sent in timeslot A-0 on net 0.
This means that only different Crypto can ensure you don’t fracture a Network.
Bonus point: What happens if you are using a different Network (NDD) but using the Same Crypto as another active Network within LOS?
Terminals will get stuck in Coarse Sync and never attain Fine Sync.

## Slide 23: Synchronization Summary
Sync Issues, check
  Connectivity
  Crypto
    - Correct days loaded, CCPD, CVLL (load Map)
  Time
    - Do you have communications to support a time hack
  Loads
    - Load file corrupt, wrong network loaded, etc
  Operator error
Notes: TP: Synchronization Process Summary:
When having issues gaining Fine Sync, you need to check:
- Connectivity:
> Do you have LOS with the NTR/IEJU
- Crypto:
> Correct day loaded
> Using correct CCPD
> Is your crypto loaded in the right location (check your crypto load map)
- Time:
> Do you have comm to complete a time hack?
- Network Loads:
> Do you have the right network loaded?
> Is the file corrupt?
- Operator error

## Slide 24: Link 16 Duties
NTR (812)
MNCS (814)
IEJU (815)
FJUA (823)
FJUAB (825)
JICO (805)
JRE JU
JREU
CDOA (809)
L16CDA (820)
NC (821)
L16PR (826)
MRLYU (813)
DLM (800)
TDC (801)
L16CRYPT (827)
Notes: TP: Slide Sort Activity – matching code with the definition the first section of this lesson we introduced three key duties/roles when operating in Link 16, they include:
NTR – Net Time Reference
ETR – External Time Reference
IEJU – Initial Entry JTIDS Unit
Other common duties that will be assigned to units participating in Multi-Link Operations using Link 16 are:
MNCS – MIDS Net Control Station
FJU = Is a JU that forwards data among Ius using J-Series, M-Series, or other Data Link Message Formats.
FJUA – Link 16 to Link 11 Forwarder;
FJUAB – Link 16 Forwarder to Link 11/Link 11 B;
JICO – indicates which unit the overall JICO can be reached thru
JRE JU – is a unit connected directly on Link 16 and connected via Joint Range Extension
JREU – is a unit connected directly on a JRE Interface and not communicating on Link 16
CDOA – Change Data Order Authority
L16CDA – Link 16 Change Data Authority
NC – Navigation Controller
L16PR – Link 16 Position Reference
MRLYU – MIDS Relay Unit
DLM – Data Link Manager
TDC – Track Data Coordinator
L16CRYPT – CryptoNet Manager

## Slide 25
Confirmation Questions
Name the 3 states of Synchronization
What is required to enter into Coarse Sync?
Describe the two ways of achieving Fine Sync?
What is the only authorized Time Base?
What is the only way to obtain Network separation between two NTRs? Explain why and what affects can happen.
Explain some issues that can affect the synchronization process.
Notes: TP: Confirmation will use a Slide Sort activity: Trainees will match cards with definition and code.
No Sync, Coarse Sync, and Fine Sync
Receipt of two IEM (J0.0) messages
Active Sync uses RRT-I/R exchange to fine-tune terminal clock, requires 3 RTT-I/R exchange to obtain Fine Sync;
Passive Synch – does not transmit RTTs, uses the time of arrival of the PPLI message with the expected time of arrival, based on the position reported in the PPLI. It will use the difference in the times to make time refinements; requires good geometry (3 or more players already in Fine sync); takes longer than active sync. Two modes – DS (data silent) and LTT-I (long-term transmit Inhibited)
4) Zulu or GMT
5) Different Crypto; all NTRs transmit the J0.0 message in the A-0-6 timeslot; therefore, the only way to isolate a network from another with two NTRs in LOS to a IU is to use crypto to change the frequency hopping pattern. Common issues of dualing NTRs – Fractured Net (same crypto and network, players sync with one or the other NTR but entire architecture is not exchanging data); Stuck in Coarse sync – different network NTRs using the same crypto.
6) Time, load-file, crypto, LOS between participants (Connectivity), operator error

## Slide 26
QUESTIONS?