## Slide 1
EO 002.03
Extract NILE Unit Link 22 Specific Information from OTL

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
References
SETID Descriptors List
Link 22 NILE Unit
  HEADING
  PERIOD
  GENTEXT
  NILE UNIT DATA - NUDATA
  LINK DUTY -LKDUTY
  UNIT RECEPTION QUALITY - NULRQ
  UNIT NETWORK RADIO SILENCE - NUNNRS
  UNIT FILTER - UNITFLTR

## Slide 4
References
APP 11 (D) 1
ADAPT 33
STANAG 5522
Notes: Your references are as follows:
APP 11 (D) 1
ADAPT 33
STANAG 5522
The main one for dissecting and extracting Link22 tactical data will be APP 11 (D) 1, MRN #N017, Version 5.2
This document will be supplied to you as we proceed through the various SETIDs used for creating and entering in the correct data in correct format: while also more important for this class, being able to break down these same SETID with ease.

## Slide 5
SETID Descriptors
Notes: Most of the SETID names for Link 22 start with an N (NILE Unit) for easy identifiers, though some SETIDs are generic to all segments such as “Heading”, and a small few are shared fields with Link 16 SETIDs which start with a J.
This is the list of the 8 Link 22 SETID Descriptors we will be covering for this lesson which focuses on extracting NILE Unit Specific Information from an OTL.
(Instructor to review name and Format Name Sets)
These IDSETs are either Mandatory (M), Conditional (C), or Operational )(O).
  If mandatory the IDSET must be included in the completed OTL.
  If conditional then this SETID is required due to a data variable entered in a mandatory SETID field.
  If Operationally Determined then SETID required for this Mission/Exercise

## Slide 6
HEADING
HEADING/LINK 22 SEGMENT
Notes: Indicates the start of the LINK 22 segment.
In the example you see the SETID as HEADING. With the M, which indicates that this is a mandatory field.
You have up to 61 alpha numerical characters to the Heading Information field. However in the OTL this will only be used with the Link 22 example given.
An example of this is the example on the slide. HEADING/LINK 22 SEGMENT

## Slide 7
PERIOD
Notes: Indicates a LINK 22 effective time period that is different from, but falls within, the overall OPTASK LINK effective time period.
In the example you see the SETID as PERIOD. With the M, which indicates that this is a mandatory field.
You have up to 14 alpha numerical characters for the Start of Period Information field. However this is the standard format of Day/Time Zulu/Month/Year.
You have up to 2 field: a 3 and a separate 14 alpha numerical characters for the End of Period Information field. The 3 character field is for examples on slide for UFN or NLT.
Many times with an OTL it is only valid for the duration of the exercise or operation. As opposed to a Standing OPTASK MSG for a Command that may say UFN.
PO1 Shawn Quigley is a Terminator, just ask him.

## Slide 8
GENTEXT
Notes: GENTEXT is for amplifying or additional information for operators vice machine/equipment.
In the example you see the SETID as GENTEXT. It is always an Operationally Determined
If you do use it, there are 2 mandatory fields: You have up to 61 alpha numerical characters for the Text Indicator Information field. This is the topic of the free text to follow.
You have unlimited alpha numerical characters for the Free Text content Information field. This is normal in plain English for format.
This is where data from an OPGEN/OPDIR or other tactical message can be inserted to assist with content or direction.
This where JICOs place supplement TDL info/data such as where they or a JICC is located, to listing contact info, to mission area or parameters critical to TDL portion.
Other options for use would be "MISSION AREA SUMMARY". "LATE NETWORK ENTRY INSTRUCTIONS". "LINK 22 NETWORK PROCEDURES". As suggested in APP 11(D) when compiling an OTL for Link 22, as scene in the bottom box.

## Slide 9
NUDATA
Notes: Provides information about the LINK 22 unit data. It is a mandatory SETID.
UNIT DESIGNATION: Your choices are one of the following:
  Ship: Enter "SHIP:" followed by the ship name, for example: "SHIP: HMCS WINNIPEG” or “USS NIMITZ“ in example.
  AC: Enter "AC:" followed by aircraft type or model, for example: "AC: CP140".
  Unit Designator: Enter "UNIT:" followed by the unit designator, for example: "UNIT:CADS NORTH BAY".
  Link Unit Line Number: Enter "LULN:" followed by the Link Unit Line Number, for example: "LULN:1234".
UNIT IDENTIFICATION CODE: Enter UIC:" followed by the unit identification code, for the unit, for example: "UIC:CANF1234". The units Country is used in 3 letter form. Followed by A for Army, F for Air Force, N for Naval, J for joint, b FOR Combined, I for Interservice, etc…
UNIT CALL SIGN: Enter "CS:" followed by the unit call sign, for example: "CS:EAGLE1“ or “CS:BISON338”
LINK UNIT ADDRESS: Enter the LINK 22 address of the LINK 22 unit, for example: "00776".
LINK TRACK NUMBER BLOCK: Enter the track number block assigned for LINK 22 use, for example: "AA200-BB776". “00200-00376”
RELAY SETTING: Enter the relay setting for the LINK 22 unit, for example: "1“ Automatic/ “2” Inhibited/ “3” Preferred - Amplification.
NETWORK STATUS: Enter the unit's initial transmission status in the LINK 22 super network, for example: "ACTIVE".
ROLE AUTOMATIC TAKEOVER FLAG: Enter whether the LINK 22 unit should takeover a SNMU or NMU role without operator intervention, for example: "DISABLED".
ROLE LOSS TIMEOUT: Enter the time in minutes necessary for the LINK 22 system to inform the operator that a specific role LINK 22 unit within the LINK 22 super network was lost, for example: "15".
LINK 22 FORWARDING TRACK NUMBER BLOCK ASSIGNMENT: Enter the LINK 22 forwarding track number block assigned, for example: "00777-01776".

## Slide 10
LINKDUTY
Notes: Provides the specific duties assigned to the unit for LINK 22 operations.
This SETID would be after each unit listed under SETID NUDATA.
Each Link duty is allocated a number, In this example duties are as listed:
  80-FORCE TRACK COORDINATOR AIR (FTC(A))
  830-IJMS Change Data Authority (ICDA)
  840-L22 SUPER NETWORK MANAGER (NSNMU)
  824-LINK 16 DATA FORWARDING UNIT LINK 11B (FJUB)
which We will cover on next slide for Link 22 only.

## Slide 11
LINK 22 Duties
Notes: These are the link duties for Link 22 only.

## Slide 12
NU LINK RECEPTION QUALITY- NULRQ
Notes: LINK 22 UNIT RECEPTION QUALITY : Provides information about the LINK 22 unit’s forced reception quality.
This is a Conditional SETID, (NULRQ) IS REQUIRED IF IDSET NUNNRS OCCURS, OTHERWISE IT IS PROHIBITED.
LINK 22 NETWORK IDENTIFIER: Enter the LINK 22 network identifier, for example: "2". which is a range [1 through 8].
SUPPORTING LINK 22 UNIT ADDRESS: Enter the assigned LINK 22 address of the unit designated as the supporting unit for a planned radio-silent unit, for example: "00775".
FORCED COMPLIMENTARY LINK RECEPTION QUALITY: Enter the forced complimentary link reception quality value for the unit designated as the supporting unit for a planned radio-silent unit, for example: "3".
  0 = None
  1 = Poor
  2 = Good
  3 = Excellent

## Slide 13
LINK 22 UNIT NETWORK RADIO SILENCE - NUNNRS
Notes: LINK 22 UNIT NETWORK RADIO SILENCE - Provides information about the LINK 22 unit’s network radio silence.
This is Operationally Determined, if used it must use SETID LINK 22 UNIT RECEPTION QUALITY
Enter the LINK 22 network identifier on which the unit should be radio silent, for example: "7". range 1 through 8.

## Slide 14
UNIT FILTERS
Notes: UNIT FILTERS DETAILS: Provides information about the LINK 22 unit’s data filter requirements.
This is Operationally Determined
FILTER IDENTIFIER NUMBER : Enter the transmit/forward filter number, for example: "A14". The Letter in this example “A” designates Link 11 Transmission Filter for something that was preset.
Currently there is no designation for Link 22 other then: “TRANSMIT FILTER FOR ALL LINKS IN A MULTI LINK INTERFACE” which is M.

## Slide 15
Confirmation Questions
Conduct 002.03.01 - Extract NILE Link 22 Unit Specific Information Mission Planning Sheet exercise utilizing the following resources:
    LO 002.03.01 lesson plan
    APP11 (D) OTL Break down.

## Slide 16
QUESTIONS?