## Slide 1
EO 003.02.01
Illustrate a Multi-Link Architecture based on an OTL

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
OVERVIEW
MTN/MTA
What is an IER
Illustrate the Architecture from the OTL
Link 11
Link 16
Link 22
Extended Interfaces
VMF
Notes: TP: The OTL is the message/machine readable document that explains the Multi-TDL Network / Multi-TDL Architecture for the operators. But Command isn't going to easily understand the plan just by reading this document unless they have lots of time and a lot of experience. The ICO or Planner will build a visual representation of the OTL to brief Command on the overall plan and how it meets the IERs by using the platform laydown, data exchange medium, link roles. Most people can understand the Multi-TDL plan when delivered in this format.

## Slide 4
Illustrate a Multi-Link Architecture based on an OTL
MTN
Satisfy IERs
Critical to the COP and various Recognized Pictures
MTA
Physical Configuration
Functional Organization
Operational Procedures
MTN and MTA, they are closely linked and in most cases considered synonymous
Notes: The MTN is designed to pass information and data automatically and rapidly between military platforms and systems within joint and coalition task groups. The purpose of the MTN is to satisfy Information Exchange Requirements and is critical to the Common Tactical Picture including the various Recognized Pictures.
The Multi-Tactical Data Link Architecture or MTA is the physical configuration, functional organization and operational procedures used in the MTN design.
When considering MTN and MTA, they are closely linked and in most cases considered synonymous

## Slide 5
Illustrate a Multi-Link Architecture based on an OTL
IER is
An IER answers:
Who
What
When
Where
Why
How
Sender Node | Receiver Node | Information | Medium | Message Format
12 er | CADS | Surveillance | JREAP C | J Series
12 er | CF188 | MM/WC, AC | Link 16 | J Series
HMCS Fredericton | MH148 Cyclone | ASW Information | Link 11 | M Series
“A statement of need to exchange info …..”
Notes: Definition of an IER: “a statement of need to exchange information between cooperating forces or HQs, specifically the information to be exchanged in a standardized manner, within the context of the mission, key tasks, required degree of interoperability and the parameters of CIS involved” - NATO, APP 15.
Formal identification of the ‘who, what, where, when and how’ of communicating information. A quick table like the example here can be easily used to verify the IERs. You will use this later in EO 003.02.03 to validate the path and flow of data.
An IER includes:
  Type of information (The “What”)
  Format of the information (The “What”)
  Security Classification/Designation (The “What”)
  The size of the files to be transferred (The “What”)
  Who requires the information (The “Who” and “Where”)
  How often the exchange takes place (The “When”)
  The medium used for the transfer (The “How”)
  The application(s) used to generate and/or read the information (The “How”)
Any other data needed to smooth the transfer of the information

## Slide 6: Link 11
NCS is in the middle
  Callsign/unit
  Define Link duty
  12 er
  NCS (S)
Notes: TP: Link 11 is depicted with the NCS unit in the center and the other players circling around it; this shows that if he drops out the connectors don't have any way to connected together without having someone assume the roll.
The Unit name and any defined duties are placed under the image or icon depicting that platform.
Activity: Using the OTL, draw out a simplified Link 11 Topology; be sure you indicate any special duties assigned.

## Slide 7
Illustrate a Multi-Link Architecture based on an OTL
Build the Link 11 Architecture based on your training OTL Link 11 Segment
Notes: Activity: Think, pair, share to compare architectures

## Slide 8: Link 16
Callsign/Unit
Define Link duty
CAJE0007A AKAT 1234 ZULU
CF188
IEJU
Notes: TP: Link 16 is commonly referred to as a Ring topology.
Label the link type: The name of the network, crypto, and time base is typically included in the center of the 'Link 16 ring'.
Similar to Link 11, special duties will be listed under each platform.
Lightning bolts are the common connectors used.
Activity: Using the OTL, draw out a simplified Link 16 Topology; be sure you indicate any special duties assigned.

## Slide 9
Illustrate a Multi-Link Architecture based on an OTL
Build the Link 16 Architecture based on your Training OTL Link 16 Segment
Notes: Activity: Think, pair, share to compare architectures

## Slide 10: Link 22
Callsign
Define Link duty
- NSNMU
- NSNMUSBY
NU 12
NU 25
PI
PI
NU 5
NU 12
NU 13
NU 10
NU 16
NN1-HF
NN3-HF
NU 15
Notes: TP: Link 22 is very similar to how Link 16 is depicted. Remember, a platform can be active in more than one Nile Network.
Similar to both Link 11 and 16, special duties will be listed under each platform.
Lightning bolts are the common connectors used.
Activity: Using the OTL, draw out a simplified Link 22 Topology; be sure you indicate any special duties assigned.

## Slide 11
Illustrate a Multi-Link Architecture based on an OTL
Build the Link 22 Architecture based on your Training OTL
Notes: Think, pair, share to compare architectures

## Slide 12: JREAP B/ Serial J
Label the link protocol
Baud
Phone number
Sync/ Async
Notes: TP: JREAP B is point-to-point, therefore it is depicted as a line with bi-directional arrows between the two connected participants. The name of the connection (ie: JREAP B), baud rate, phone number and whether the connection is Synchronous or Asynchronous is indicated under the connector.
Activity: Using the OTL, draw out a JREAP B Topology (if indicated)

## Slide 13: JREAP C
IP Address
Port #
IP Protocol
IP Address
Port #
IP Protocol
Label Network Enclave
Notes: TP: A single JREAP C is depicted as a line with bi-directional arrows between the two connected participants .
The name of the connection (ie: Label the enclave), IP address of the participant, Port # for that connection, protocol (TCP/IP or UDP) and whether the participant is Client or Server. (TCP Client, TCP Server, or UDP)
Activity: Using the OTL, draw out a JREAP C Topology based on those participants that connect to you (use the 'Student # - platform allocation from PO004).

## Slide 14
Illustrate a Multi-Link Architecture based on an OTL
Build the JREAP topology used in your OTL.
Notes: For JREAP C, each trainee has been assigned a specific platform that they will use for all exercises in PO004. They are to draw out those extended interfaces that connect to their platform. Some may have more than one.
Think, pair, share to compare architectures

## Slide 15: VMF
JTAC
TACP
TACP
Gateway
Bde HQ
DIV HQ
EPLRS
JTAC
DACAS
UHFLOS VMF
UHFSAT VMF
URN
IP Address

## Slide 16
Illustrate a Multi-Link Architecture based on an OTL
Build the VMF topology used in your OTL.
Notes: For JREAP C, each trainee has been assigned a specific platform that they will use for all exercises in PO004. They are to draw out those extended interfaces that connect to their platform. Some may have more than one.
Think, pair, share to compare architectures

## Slide 17
Illustrate a Multi-Link Architecture based on an OTL
Build the VMF topology used in your OTL.
Notes: For JREAP C, each trainee has been assigned a specific platform that they will use for all exercises in PO004. They are to draw out those extended interfaces that connect to their platform. Some may have more than one.
Think, pair, share to compare architectures

## Slide 18: Architecture
CF-188
IEJU
USFO0004B
8 ACCS
NTR
FJU
NATO E3
IEJU
FJUA
4 GS
IEJU
NN1-HF
TDL Enclave
CADS
12 ER
HMCS Halifax
NCS
HMCS Montreal
HMCS FREDERICTON
FNUJ
IEJU
CADS
TN 4551
Notes: TP: When you build the overall architecture into one picture you can show how the different forwarders are utilized to connect all platforms thereby meeting the IERs of the exercise. In this format, you can answer the 5 Ws / 1 H. None link assets need to be reported by units as tracks.

## Slide 19
Confirmation Questions
Build the entire Exercise Architecture from your training OTL.
Notes: TP: Remember all your forwarders to show how the various links are interconnected to build the MTN/MTA.
Think, pair, share to compare architectures

## Slide 20
QUESTIONS?