## Slide 1
EO 002.01
Extract Participating Unit Information

## Slide 2
This brief is
UNCLASSIFIED

## Slide 3
Overview
OPTASKLINK Message Text Formats
LINK 11 SEGMENT
LPUDATA Set
LKDUTY Set
INDIRUF Set
UNITFLTR Set

## Slide 4
OPTASKLINK Message
Text Formats
Message Text Formats (MTF) are a means of writing logical and unambiguous military orders
There are 2 different technical standards in use in the CAF Data Links:
  United States Message Text Format (USMTF)
  Allied Data Processing Publication number 3 (ADapt-3)
The OPTASKLINK in Canada is written to be compliant with ADapt-3 and is a subset of the NATO APP-11
APP-11 is the NATO catalog of all the military messages that are defined by NATO, for example:
  Air Tasking Orders (ATO)
  Operational Tasking Communications (OPTASKCOMS)
  Operational Tasking Common Operating Picture (OPTASKCOP)
Notes: This slide is a brief review of the OPTASKLINK message, and the different formats it's written in.
USMTF is not the same as APP-11, and an OTL written in USMTF may not have the same fields as one written in APP-11
The CAF has determined that APP-11 is the standard for handling OTLs

## Slide 5
LINK 11 SEGMENT
The LINK 11 SEGMENT in the OPTASKLINK defines Link 11 information
This includes all Link 11 parameters, including the Participating Unit addresses as well as track block allocations
A single unit can have up to 4 Sets defining it
In APP-11 the following Set IDs define a unit's parameters
Set ID | Set Format Name | Description
LPUDATA | Link 11 Participating Unit Data | Provides link PU data for Link 11
LKDUTY | Link 11 Duty | Provides the specific duties assigned to the unit for Link 11
INDIRIUF | Link 11 Indirect Interface Unit Filter | Identifies indirect Interface Units and their data forwarding filter
UNITFLTR | Link 11 Unit Filters | Assigns the unit-level active filter for Link 11
Notes: In USMTF, this segment is called LNKXI
In this segment, it determines how all of Link 11 is to operate.
For the purposes of this lesson, the focus is entirely on specific units, not global parameters like DLRP.

## Slide 6
LPUDATA Set
The LPUDATA segment defines a unit participating in Link 11
This segment defines exactly how a designated unit is to participate
  Defines Participating Unit Number
  Defines Track Block Allocation and Forwarding Track Block Allocation
LPUDATA/SHIP:NIMITZ/UIC:USAJ12345/CS:GANGBUSTER/PU:24 /BLOCK:0300-0500/RC/FBLOCK:3000-4567//
Notes: M = Mandatory field
O = Operational Determined field
The numbers in the field are the number of allowable characters. For example, the UNIT DESIGNATION field can have a maximum of 38 characters for units with very long names.

## Slide 7
LKDUTY Set
The LKDUTY Segment defines the duties that the given Link 11 unit are to perform
It includes a list of all duty codes the unit is to perform in Link 11
  For example : 84 for NCS
The duties are specific to Link 11. There are no other Link duty codes present.
LKDUTY/80/830/840/824//
Notes: Repeatable means that the duty code field may be repeated as many times as appropriate.

## Slide 8
INDIRUF Set
The INDIRUF Segment defines a unit's other Interface Units in use, as well as the data forwarding filters
This includes Link 11B (RU), Link 16 (JU), and Link 22 (NU)
INDIRIUF/B/RU:123/JU:71777/PU:76//
Notes: The term "indirect" here means that the unit is acting as a gateway. Direct means the C2 Host is directly on the RF interface, and indirect means that there is some kind of processing before that data is sent out.
If a unit was operating directly on two different interfaces, they would use the same JU/RU/PU, and this line would not be necessary.

## Slide 9
UNITFLTR Set
The UNITFLTR Segment defines filters that the unit has in place by the same filter codes as in the INDIRUF Segment
There can be more than one filter code in place
The filter codes are defined elsewhere in the OPTASKLINK, usually AMPN or GENTEXT
UNITFLTR/A14/A25//
Notes: The filters are designated with a letter (A,B,J, etc) and a number indicating an index.
These letters and numbers are defined elsewhere in the OTL. Filters are far too complicated to include in a Message Text Format elegantly, so this is the solution in mind. Many OTLs omit the filters settings in the OTL in favour of explaining filters through GENTEXT or separate messages or directives.

## Slide 10
Summary
OPTASKLINK Message Text Formats
LINK 11 SEGMENT
LPUDATA Set
LKDUTY Set
INDIRUF Set
UNITFLTR Set

## Slide 11
QUESTIONS?